## Slide 1
Chandra Bhat, C. Y. Tan and V. Grzelak
20190131
Booster DC studies: Adiabatic Beam Capture

## Slide 2: Adiabatic Beam Capture Studies prior to Aug 2018
Did capture studies with 8 GeV ramp after correcting RF phase on individual stations. Summary of that study was (Beams Doc 6613).
  Many PARAT curves were investigated.
  Bill’s non-adiabatic PARAT gave the best efficiency.
  Adiabatic PARAT gave smooth decrease in bunch length. But efficiency did not improve.
  All PARAT curves showed bunch splitting in the early part of the capture process.
   This was a great puzzle.
Possibly many of these issues can be resolved by measurements on a DC Ramp in the Booster!

## Slide 3: Planned Booster DC Study
First revisit the phases to individual RF stations. Next, conduct measurements in the DC mode (400 MeV)
  Compare RFSUM responses with NO beam for cases with
    Constant frequency, APG & a PARAT curves.
    Balance the amplitude for two RF system at a time.
    Measure RFSUM for
      A1+B1, A1+B2, A1+B3 …etc., and similarly
      A2+B1, A2+B1…etc.,
  Measurements on beam capture under similar conditions as above, but,
    Same number of A & B RF stations
    Tune the PARAT curve for best capture
Goal: Understand capture process.
Goal: Response of individual RF system pairs to same para-phase curve

## Slide 4: DC Measurements on two RF system at a time with NO Beam
Cavity 7(A) &
All “B” stations
18, 19 and 21 deviate significantly
Operational
PARAT
Va
Vb
Vc


Vc (Relative Units)
Master Station 7(A) and 8(B)

## Slide 5: DC Measurements on two RF system at a time with NO Beam (cont.)
Cavity 8(B) &
All “A” stations
Measured Vrf did not follow a simple relation
Vc=Va*(2*(1+cos(PARAT/PARATmax)))
Stations 18, 19, and 21 deviate noticeably.
Then data showed that implementing a calculated adiabatic PATAT curve in operation is not straight forward.
A PARAT curve developed for a combination of RF stations need not be ideal for some other combinations.
Vc (Relative Units)
Lesson Learnt: Global para-phase control and Vector balancing is not sufficient.
A new hardware is needed to control both locally & globally for adiabatic capture.

## Slide 6: Beam Capture in DC Ramp
20 rf stations:
  10 stations each for A & B.
Constant frequency curve
  frf =B:INJFRQ
Constant APG curve
Feedback turned off
  Disabled B:VAPLON & B:TFBON
Varied
  PARAT curves
  B:VXTPPP, B:PC1OFF B:CRVDLY, B:POTAIN, B:POTBIN.
Global balancer ON and OFF
3 Booster turn
Paraphase Curves used for 20181114 DC studies

## Slide 7: Comparison of Bunch Lengths for different PARAT

## Slide 8: Note: the neck makes a phase jump?
For whatever reason, the neck makes the beam take a phase jump.
Is this real? YES! See waterfall plot of injection.
The data without the PC1OFF correction to make it smooth sees this problem.
Phase jump
Vrf
WCM
Global balance OFF/ON

## Slide 9: What is going on during the Beam Capture?
Capture with Operational Paraphase Curve
Capture with Adiabatic Paraphase Curve
What was Expected?: In an ideal situation beam capture in DC mode the RF phase should not slip relative to bunch centroid.
Observations: We see two types of RF phase slip relative to the bunch centroid
fast and
slow
FB-20190123-4BT-1E12-E17-DC-20RFst-4
FB-20181114-DC-6
Vrf
Vrf
 How these are possible?
No “NECK”
Time(ns)
Time(ns)

## Slide 10: Possible Explanations
Va=Vb
VaVb; Vb/Va=0.90
If Va=Vb and |(start)| >90 deg then RF phase slips by 180 deg.
If VaVb |(start)|=90 deg then the RF phase slips slowly by 90 deg and occurs till the end of the capture.
If VaVb |(start)|>90 deg then both of these slips happens.
Flipping Phase
Slipping Phase
&
Plipping Phase
This undesirable feature has a consequence during early part of the beam capture

## Slide 11: ESME Simulations DC Beam Capture
Conclusions: For beam capture and acceleration without any losses one needs
  Balancing between vectors A and B better than 1% locally and globally.
  |(start)|90 deg.
Va/Vb=1
Va/Vb=0.96
Beam acceleration
Leaking beam particles
This result is good only for dE(Inj)~1.8 MeV

## Slide 12: 20 RF stations ON with global balancer ON (no neck)
Corroboration with BPM data.
The BPMs don’t seem to see this part of the phase slip. Not enough bunching?

## Slide 13: 20 RF stations ON with global balancer OFF (no neck)
Note no change in phase or energy (from turn by turn).
But see the ripples that are seen in TBT and the phase measurement!

## Slide 14: What Next?
DC studies in the Booster helped us to diagnose
  Possible symptom for beam losses in the first 4-5 ms of the beam cycle.
    Identifying and mitigating it is critical for the higher intensity operation of the Booster.
  Possible issues in emittance dilution in early part of the acceleration cycle.
We need to improve
  Balancer circuit for A and B cavities to control voltage and PARAT
    Globally &
    Locally
  Paraphase angle between Vectors A & B should be 180 deg, capable of controlling better than 1deg (which depends on dp/p of the incoming beam).

## Slide 15: Backup

## Slide 16: DC Measurements on pair of individual RF stations with NO Beam (cont.)