Guidelines for MI60 Extraction with Three Kickers

Dave Johnson

May 18, 2002

Assume all three kickers are downstream of Q602

Assume current instrumentation can be relocated

Assume downstream end of third kicker is ~7.5 meters downstream Q602

Vertical aperture of 3rd kicker must not be limiting aperture

Vertical design beta at QD location ~55 meters

Vertical ID of MI beam pipe ~ 1.88 “ (47.75 mm)

Vertical beta at downstream end 3rd kicker ~25 meters

Minimum vertical aperture of 3rd kicker beampipe

1.88” * sqrt (25/55)  =>  1.27”  (32 mm)

Vertical Acceptance of MI at 8 Gev:  Use +/-4to determine acceptance

47.75 mm / 8 =>   = 5.97 mm

Acceptance = 6(2 /  => 36.8 -mm-mr ~ 40 -mm-mr

If use +/2.45 =>  95 -mm-mr

Currently on stacking cycles   H   ~ 1.5* V   (V  ~ 15 -mm-mr)

Horizontal Acceptance limited by field free aperture in Lambertson.

W ~ MI beam pipe width/2 => 60 mm

Acceptance = 6(2 /  => 58 -mm-mr ~ 60 -mm-mr

Assume blow up beam emittance in each plane by factor  2 at 120 Gev, the emittance at 120 Gev to determine apertures should be

H  =>  120 -mm-mr

V  =>    60 -mm-mr

__________________________