Simulation of Main Injector 2.5 MHz Pbar Acceleration with Space Charge and Beam Loading Effects

Vincent Wu (MI Dept)

FNAL, Batavia, IL  60510

February 2003

(MI Note 295)

In Run II four pbar bunches from the Recycler will be accelerated in the Main Injector from 8 GeV to 150 GeV. At 150 GeV the pbar bunches will be injected into the  Tevatron for collider operation. Pbar transfer from Recycler to Main Injector is envisioned as 2.5 MHz bucket to bucket transfer. An acceleration scheme with a slow  ramp (2.5 MHz acceleration) followed by a fast ramp (53 MHz acceleration) was previously developed. (See references [1, 2, 3].) The simulations in this report follow a similar track as those of  [1, 2, 3] with the inclusions of space charge, beam loading and other miscellaneous effect. The simulations are performed using the ESME program [4]. The effects of beam loading compensations and a small 53 MHz voltage during the 2.5 MHz acceleration are studied in BD documents 849 and 910, respectively.

The initial beam and rf parameters in the following table are obtained from the Recycler Ring Technical Design Report.

- Total beam energy (GeV):  8.938

- Momentum compaction factor:  -0.008683

- Rf frequency (MHz):  2.5

- Rf voltage for 2.5 MHz rf system (kV):  2

- Invariant 95% longitudinal emittance (eVs):  1.5 / per bunch

- Number of particles per bunch:  6E10

The 2.5 MHz pbar acceleration scheme is first simulated without space charge and beam loading. The ramp and dp/dt are shown in figures 1-3.

Fig. 1  Momentum curve for the entire cycle.

Fig. 2   dP/dt curve for the 2.5 MHz acceleration (first 7.3 seconds of the ramp).

Fig. 3  dP/dt curve for the 53 MHz acceleration (last 2 seconds of the ramp).

The voltage and rf phase are shown in figures 4-7. The acceleration cycle begins with an adiabatic shrink of the bunch at 8 GeV for 0.5 second. During this period of time, the rf voltage increases from  2 kV to 50 kV adiabatically. After the bunch shrinkage, the beam is accelerated to 27 GeV using the 2.5 MHz rf system in about 6.6 seconds. The 2.5 MHz acceleration voltage is shown in Fig. 5. Because of the lack of phase focusing at transition, the rf voltage is lowered in the region of transition to reduce the energy spread. Simulation shows that this maneuver eases the problem of emittance dilution due to transition crossing. The emittance (rms) dilution for crossing transition is about 2 %.

Fig. 4  Voltage program for the entire cycle.

Fig. 5  The 2.5 MHz voltage program (first 7.3 seconds in figure 4). Transition occurs at about 4.7 second and at an energy of 20.49 GeV. The voltage at transition is 43 kV and the phase is 58 degree.  See Fig. 6 for the rf phase.

Fig. 6  Rf phase during the entire cycle.

Fig. 7  Change in rf frequency during the entire cycle. For the first 7.1 seconds, the base frequency (at the beginning of the cycle) is 2.5136 MHz. The maximum frequency change for the 2.5 MHz acceleration is about 13 kHz. This is within the 25 kHz frequency range (bandwidth) of the 2.5 MHz cavity. For the last 2 seconds, the base (starting) frequency is 53.046 MHz. The maximum frequency change during the 53 MHz acceleration is about 31 kHz. This is within the tuning range of the cavity which is 52.8 MHz to 53.1 MHz.

At the 27 GeV front porch, the voltage snaps to 4 kV and the bunch undergoes a quarter period of synchrotron rotation to stretch out. Then the voltage is raised to 60 kV for a fast rotation. At minimum bunch width, the bunch is captured by the 53 MHz bucket with about 0.7 MV. The first rotation takes about 115 ms and the second rotation takes about 46 ms. After the capture, the 53 MHz bunch is accelerated to 150 GeV. The entire acceleration cycle is about 9.2 second. Figure 8 shows some bunch samples during the cycle.

(a)                                                                 (b)

(c)                                                                (d)

(e)

Fig. 8  The left hand side vertical axis is energy in MeV and the right hand side vertical axis is rf voltage in kV. The horizontal axis is azimuthal angle around the machine in degree. (a) Initial beam at 8 GeV with 1.5 eVs emittance. (b) At 27 GeV front porch before rotation. (c) At the end of second rotation before 53 MHz capture. (d) 53 MHz acceleration. (e) Final beam at 150 GeV.

Plot (a) in Fig. 8 is the initial bunch at 8 GeV with an emittance (95%) of 1.3 eVs. The second (b) and third (c) pictures are before the second rotation and at the end of the second rotation, respectively. The fourth (d) picture is an accelerating 53 MHz bunch and the last (e) picture is at 150 GeV flattop with a final emittance (95%) of  about1.4 eVs. There is no particle loss during the cycle.

The antiproton bunch intensity is about a factor of 10 smaller than typical Main Injector operation. However, because of the unusually long (or slow) ramp, simulation with space charge is carried out to check emittance dilution. The effects of beam space charge and coupling impedance between the beam and the beam pipe are simulated with the following input parameters. (See reference 5 for the theoretical basis.)

- Assume circular beam pipe as a broadband resonator (Q=1) with 1.7 GHz cutoff frequency.

- Zll/n = 1.6 (MI longitudinal impedance per harmonic [6, 7]).

- Bunch intensity = 6E10.

- Initial 95% emittance 1.5 eVs.

Simulations are also carried out with Zll/n = 3.2, 4.8, 6.4, 8 and 24E10 (4 bunch intensity). The longitudinal emittance growth versus Zll/n is shown in the figure 9.

Fig. 9  Longitudinal emittance growth vs. Zll/n.

The space charge voltages are 20 V to 300 V for the 2.5 MHz acceleration and are 3 kV to 8 kV for the 53 MHz acceleration. Within a factor of three of Zll/n =1.6, there is no significant emittance growth. For the case of bunch intensity 24E10 and Zll/n =1.6, the emittance growth is less than 10% and particle loss is less than 1%.

For simulations with 2.5 MHz beam loading, four bunches and a single cavity are modeled in ESME. The quality factor and the shunt impedance of the 2.5 MHz cavity are112.5 and 45000 Ohm, respectively [10]. To simulate the total beam loading voltage of five cavities, the shunt impedance is increased by a factor of five.

Some examples of bunch motion are shown in figures 10-12.

(a)                                                               (b)

Fig. 10 (a) Initial distribution at 8 GeV. (b) Distribution at the end of the adiabatic bunch shrink (at 0.5 second of the cycle) at 8 GeV.

(a)                                                               (b)

Fig. 11 (a) First bunch at the beginning of the rotation at 27 GeV. (b) First bunch at the end of rotation.

(a)                                                                (b)

Fig. 12 (a) 53 MHz capture of the first bunch. (b) 53 MHz acceleration of the first bunch.

Figures 10-12 have shown that beam loading causes significant emittance dilution and phase shift to the bunch distribution. The peak beam loading voltage for the entire cycle as a function of time and an example of beam loading voltage as a function of azimuthal angle along the ring are shown in figure 13. The beam loading voltage at 8 GeV is about

(a)                                                                   (b)

Fig. 13 (a) Peak beam loading voltage vs cycle time. Ignore voltage after about 8 seconds at which 53 MHz acceleration takes over. (b) An example of the instantaneous beam loading voltage as a function of azimuthal angle around the ring.

900 V and the rf voltage is 2 kV. The phase shift to the rf is about 24 degrees. The peak beam loading voltage during acceleration is 2.1 kV and the rf is in the range of 43 to 60 kV. At 27 GeV the beam loading voltage is about 1.6 kV and the cavity voltage is 4 kV. The phase shift to the rf is 22 degrees. As one can see from figure 11 and 12, the off-centered bunch can’t be captured efficiently. Large emittance growth (over a factor of 2) and particle loss are observed. In conclusion, 2.5 MHz beam loading compensation is needed for the 2.5 MHz acceleration scheme.

The 53 MHz beam loading is simulated with one cavity and 4 bunches. A R/Q ratio of 104 is assumed for beam loading simulations. From 8 to 27 GeV (during 2.5 MHz acceleration), the shunt impedance and the quality factor used for the simulations are 260 k( and 2500.  From 27 to 150 GeV (during 53 MHz acceleration), the shunt impedance and the Q used for the simulations are 520 k( and 5000 [12].  To simulate 18 cavities, the shunt impedance is multiplied by a factor of 18. The initial emittance is 1.5 eVs and the bunch intensity is 6E10.

Figure 14 shows some phase space plots of bunch motion at various times of the cycle. According to the phase space plots, 53 MHz beam loading becomes important around transition crossing. In the region of transition crossing, the bunches resemble those of the 53 MHz bunches. The 53 MHz beam loading effect is most severe in this region. The bunches are greatly deformed after transition. Figure 15 shows an example of the instantaneous beam loading voltage around transition (1st plot) and the peak beam loading voltage during the cycle (2nd plot). Transition occurs around 4.7 second where the beam loading voltage peaks up (2nd plot). At transition the beam loading voltage is about 10 kV and the cavity voltage is about 56 kV. The peak beam loading voltage

Fig. 14  Starting from left to right and top to bottom, the first plot is the initial distribution, the second plot is the first bunch before transition, the third plot is the first bunch after transition, the fourth plot is the first bunch at the start of the 2nd rotation, the fifth plot is the first bunch at the end of the 2nd rotation, and the last plot is the 53 MHz capture.

Fig. 15  First plot shows the instantaneous beam loading voltage (keV) as a function of azimuthal angle around the machine and the second plot shows the peak beam loading voltage (MV) vs cycle time (second).

during 53 MHz acceleration is about 35 kV and the rf voltage is in the order of MV. The rf voltage is about two orders of magnitude larger than the beam loading voltage. Hence beam loading is not expected to be a problem during 53 MHz acceleration. The 53 MHz beam loading is a problem around transition and at 27 GeV where the cavity is at 4 kV. The overall emittance growth is over a factor of two and the particle loss is large. In conclusion, 53 MHz beam loading compensation is needed for 2.5 MHz acceleration.

Simulations with different initial emittance (other than 1.5 eVs) are carried out to determine the maximum acceptable injection emittance to Main Injector for acceleration. The studies are done without space charge and beam loading effects. For an initial emittance of 2 eVs, the emittance (95%) growth is 25% and no particles are lost. For an initial emittance of 2.5 eVs, the emittance growth is 13% and 0.6% of the beam is lost. For an initial emittance of 3.4  eVs, the emittance growth is 4% and 6% of the beam is lost. Note that the lower emittance growth for higher initial emittance is due to particle loss.

# Acknowledgments

I am thankful to Chandra Bhat and Jim MacLachlan for their guidance during this work. I have profited from many fruitful discussions with them. I am also thankful to Weiren Chou for Main Injector space charge issue and Brian Chase and Joe Dey for their helpful advices regarding cavity beam loading issue.

References

1.   Gerry Jackson, The Fermilab Recycler Ring Technical Design Report, November

1996.

2.   Chandra Bhat, Pbar Acceleration in the MI using 2.5 MHz rf System and rf

Specification, MI note 260, January 2000.

3.   J. A. MacLachlan, Antiproton Acceleration in the Main Injector with rf at Harmonic

Number h=28 or h=84, FERMILAB-TM-2177, June 2002.

4.   J. A. MacLachlan, User’s Guide to ESME 2002, November 2002.

5.   J. A. MacLachlan, Longitudinal Phase Space Tracking with Space Charge and

Wall Coupling Impedance, February 1987.

6.   M. A. Martens and K. Y. Ng, Impedance and Instability Threshold Estimates in the

Main Injector I.

7.   W. Chou, Intensity Limitations in Fermilab Main Injector, June 1997.

8.   S. Ohnuma, The Beam and the Bucket, January 1986.

9.   John Marriner, Main Injector Beam Loading in the 2.5 MHz System, March 2001.

10.   J. Dey and J. Steimel, Improving the Linearity of Ferrite Loaded Cavities using

Feedback.

11. Private communication with J. Dey.

12. J. Dey, J. Steimel and J. Reid, Narrowband Beam Loading Compensation in the

Fermilab Main Injector Accelerating Cavities, July 2001.