Status of Work on Helix up the Ramp

Y.Alexahin

The largest loss of pbars in the Tevatron now occurs in the end of the ramp (at energies > 500 GeV where the voltage on main separators, B11H & C17V, reaches its maximum) and the beginning of the squeeze.

Up the ramp the transition takes place from the new injection helix (introduced in May 2002) to the old one which uses only two separators (B11H & C17V) and provides too small separation at A0.

We use as a figure of merit the so-called “radial separation”

where

is the betatron part of the r.m.s. beam sizes

Radial separation at all 138 interaction points with squeeze step1 helix (injection cogging) at 980 GeV:

Beam-beam effects at flattop with the present and proposed helices

| helix | step | Smin | ¦((x¦max | ¦((y¦max | ¦R50¦max(1012 | ¦R07¦max(1013 |
| --- | --- | --- | --- | --- | --- | --- |
| present | EoR | 3.26 | .0066 | .0031 | 2.02 | 1.45 |
|  | BoS | 3.09 | .0078 | .0031 | 2.33 | 2.54 |
| new | EoR | 4.46 | .0033 | .0016 | 1.07 | 0.31 |
|  | BoS | 4.60 | .0045 | .0021 | 1.31 | 0.51 |

Table 1. Maximum beam-beam tuneshifts and resonance driving terms with the present and new helices. The cogging is different at the end of ramp (EoR) and the beginning of squeeze (BoS).

### The new helix promises significant reduction in the beam-beam effects

## Calculated helix up the ramp

Measured proton helix at flattop (red), blue – design.

## First results with the new helix (08/03/03)

Ramping 36x4 (08/05/03)

The reason of the quench was not understood. As a precaution the following steps will be taken:

1. Center the orbit where high losses were seen

2. Keep the old helix up to 400 GeV and only then make transition to the new helix

# Text boxes

proposed helix

present (2001) helix starting from B0 (reference emittance 15( mm mrad)

Minimun “radial” separation ((’s) vs. energy. Red – present helix, blue – new helix

Maximum vertical orbit [mm] vs. energy

# Maximum horizontal orbit [mm] vs. energy

Vertical orbit [mm] at VBPMs starting from VBPMB0D

Horizontal orbit [mm] at HBPMs starting from HBPMB0D

36 bunches on the proton helix

1 coalesced bunch on the pbar helix