Accelerator Clocks

Greg Vogel  x4949

Three types of clock systems around the accelerators

Tevatron Clock (TCLK)

Machine Data (MDAT)

Beam Sync Clocks (TVBS, APTVBS, MIBS & RRBS)

Info can be found on BD/Acc. Controls/Timing & Links Web Page

http://www-bd.fnal.gov/controls/hardware_vogel/index.html

Info can also be found in the Controls Rookie Book (BD/Operations)

TCLK - Tevatron Clock

- Main accelerator clock system on site

- Coordinates operations across the complex

- Clock events provide high level timing within and between machines

- 256 possible clock events ($00-$FF)

- 199 in use

http://www-bd.fnal.gov/controls/hardware_vogel/tclk.htm

- TLG is source of major beam related events

- Reflected Beam Sync events

- General timing events (0.2Hz, 1Hz, 15Hz, 720Hz)

- 1Hz is GPS sourced

- Originates in MAC Room

- TCLK is available in all Tevatron service buildings

- transmitted on fiber and copper

- A0=>C4; F4=>D0

- New installations should all be on the fiber system

- Events prioritized (lower priority event can be bumped)

TCLK - Signal Description

- 10 MHz serial link

- Modified Manchester Encoding

- 10 bit event (start bit =0, 8 bit data, parity)

- minimum of two 1's between each clock event

MDAT – Machine Data

- Provides for transmission of machine related data

- 31 defined frames

- Programmed magnet current, measured current

- Low Beta Sequence Number, Time of Day, etc.

- http://www-bd.fnal.gov/controls/hardware_vogel/mdat.htm

- 10 MHz serial link

- Modified Manchester Encoding

- 28 bit frame (start bits, 8 frame # bits, 16 data bits, parity, trailer)

- Set of frames repeat every 720 Hz

- 10uSec frame boundaries

Beam Sync Clocks

- TVBS

- Tevatron Proton Beam Sync Clock

- Tev proton rf/7

- Proton revolution marker ($AA)

- Available at all Tev Service buildings via fiber & copper

- fiber transmission also carries rf

- new installs on fiber system

- transmission around ring follows proton path

- starts at F0

- APTVBS

- Tevatron Antiproton Beam Sync Clock

- Tev pbar rf/7

- Pbar revolution marker ($AA)

- Available at all Tev Service buildings via fiber & copper

- fiber transmission also carries rf

- new installs on fiber system

- transmission around ring follows pbar path

- starts at F0

Available Decoding Hardware

CAMAC

TCLK – C377, C178

MDAT – C169

BS Clock – C279, C278, C479

VME

VUCD

VCDT

VRFT

IP-UCD

PMI-UCD