# Tevatron Beam Position Monitor Upgrade Specifications

## Beam Current Specifications

### Peak Current vs Bunch Intensity

### Spectral Component

## RF Hardware

### BPM Plates Specification

#### Physical Dimensions

#### Coupling Equations (Impedance)

##### Linear

##### Non-linear

#### Directivity

### Bandpass Filters

#### Bandwidth

#### Reflection Coefficients

#### Justification

##### Error on 1st turn orbits

##### Turn-by-turn measurements

### Cabling

#### RG-8 Specifications

#### Reflection Coefficients

##### Connectors

##### Filters

##### Digitizer input

## Digitizer

### Sampling Rate

### Input Range

### Number of Bits

### Non-linearity

#### Integral

#### Differential

#### Effective Number of Bits (ENOB)

### Justification

#### Dynamic Range

#### Resolution

#### Linearity

#### Gain Accuracy

## Digital Downconverter

### Sampling Rate

### Number of Input Bits

### NCO Frequency Granularity

### Justification

#### Compatibility with Digitizer

#### Changes in Center Frequency

## Digital Filters

### Clock Rate

#### Interpolation

#### Dissemination

### Bandwidth

#### Modes

##### Closed Orbit

##### Turn-by-Turn

##### First turn

#### Mode Switching

### Delay

#### Repeatability

#### Tracking with Mode Changes

### Justification

#### Operating Scenarios

#### Resolution

#### Compatibility with Digital Downconverter

#### Compatibility with Proton/Pbar Cross Correlation

## DSP

### Bit Width

### Calculations

#### Position & Amplitude

#### Calibration Corrections

### Memory

#### Depth

#### Organization

### Trigger Handling

### Internal Timing

### Local Control

### Backplane Communication

### Justification

#### Operating Scenarios

#### Compatibility with Digital Filters

#### Timing Requirements

#### Calibration Requirements

#### Compatibility with Local Bus

## Crate & Local Control

### Local Bus

### Processor

### BLM Control

### Cabling

### Mechanical Dimensions

### Power Requirements

## Timing & Synchronization

### Digitizer Clock Reference

### Time Stamp Synchronization

### TCLK

### BSYNC Clock

### State Transitions

## Calibration

### Attenuation Mismatch (A & B signals)

### Delay Mismatch (A & B signals)

### Delay Mismatch (protons & pbars)

### Directivity (protons & pbars)

### Linearity

### Amplitude Mismatch (different pickups)

### Delay Mismatch (different pickups)

## Diagnostics

### Hardware

### Beam-based

## Frontend

### Initialization of System

### Mode Control

### MOOC

### State Transitions

## Acnet Data Acquisition Routines

### Request Single Closed Orbit Measurement

### Request Profile of Single Closed Orbit Measurements

### Request Single Turn Measurement

### Request Multi-turn Measurement

### Request Turn-by-turn Measurement

## Acnet Control & Diagnostics Routines

### Perform Hardware Diagnostics Test

### Perform Beam Diagnostics Test

### Perform Calibration Measurement

## User Application Programs

### BPM/BLM Plots (T39)

### BLM Data and Control (T40)

### BLM Time Plot (T44)

### Tev Orbit Program (C50)

### BPM/BLM Test and Diagnostics

## Archive Routines

### CYBase

### Local Storage

### SDA

## Data Analysis Routines

### FFT Routines

### Lattice Parameter Calculations

### Cusp Finding