Requirements on new Tevatron equipment

V.Shiltsev 1

Beams-Doc-877, v.1 10/17/2003

This document contains current list of requirements for new equipment which is going to be installed in the Tevatron. The list is not a “law”: but if new equipment/apparatus fits the requirement  it will be definitely and promptly approved by the Tevatron Department Head,  if not – it can be approved after consultations/internal review.

- Aperture   	> 60 mm

- Vacuum   	< 2e-8 Torr*m (integrated load) 2

< 5e-8 Torr (local)

- Orbit distortion  <0.2 mm

- Tune and coupling change <0.0005   3

- Nonlinearities  <1 Tev dipole at 150 GeV or 4  5 Tm times:

(a,b)2 < 3e-4 	  @ R=1”

(a,b)4 < 1e-4

(a,b)6,8,10 < 10e-4

- Impedance  	Z/n < 0.05 Ohm

ZT < 0.1 Mohm/m 5

______________________________

1  with input from B.Hanna, J.Annala, V.Lebedev

2  equivalent RT N2, approx 1% of total Tevatron gas load, see beams-doc-240

3  including differential

4  see R.Hanft et al, IEEE Trans NS-30, No.4 (Aug 1983), p. 3381

5  approx 5% of total Tevatron broad-band impedance