Fermilab/AD/TEV

Beams-doc-1065-v2

Date 9 Mar 2004

Version 1.1

Tevatron BPM Consolidated Crate Specification

Bob Forster

# Introduction

The following is to be considered the minimum specification to be applied to each "BPM Project VME Crate". This is a controlled document.

# Features

The following is to be considered the minimum specification to be applied to each “BPM Project VME Crate” :

Each is a 19” rack mount VME64x powered enclosure with :

- 2" (+/-1") recessed 21-slot card cage (see 02 below),
6U by 160 mm front vertical orientation card cage with top and bottom front inject/eject extrusions.

12-Slot monolothic standard VME64x J1/J2 (no J0) backplane with

  - 5 row, 160 pin DIN connectors with  5 mm pin lengths with no rear P1
shrouds in all 12 J1 slots,

  - 5 row, 160 pin DIN connectors with 17 mm pin lengths with rear P2
shrouds in all 12 J2 slots,

  - On-Board Termination, automatic Bus Grant/IACK jumpering.

  - The backplane is mounted left-justified in the chassis when viewed from the front, so the open slots are towards the right of the chassis.

  - When viewed from the front, the leftmost non-backplane slot may be used for the installation of an air-flow control panel, if considered advantageous, leaving 8 useable non-backplane slots.  Other air-flow control panels should be installed as required or advantageous for user safety and/or air flow control.

  - Install top and bottom transition card guides mating with the rear of the
12 backplane slots.  A full chassis width card guide is acceptable if considered advantageous, for instance if an extruded transition card guide is used.

- 12-Slot backplane stiffener.  
A full 21-slot width backplane stiffener is acceptable if considered advantageous.

- 12-Slot +3.3V/+5V/Ground backplane power busbar set.

- Real-time monitoring and remote control (over ethernet) of system power, system cooling and automatic individual fan speed control in the event of a fan failure.  To control system power, the status monitor/control system must be independently powered.
Must have password protected user programming of default alarms and limits parameters through the ethernet port.

- A front panel chassis mounted alpha-numeric LED display must be provided as a local visual system status monitor interface.

Must use +12V DC fans with tachometer outputs, arranged to provide a bottom front input to top rear output air path as follows:

  - Solid bottom and top chassis panels allow placement of immediately
adjacent hardware without affecting airflow patterns.

  - Fan(s) suck ambient room air in thru a filter near the bottom of the front panel of the chassis.

  - Fan(s) push air up, bottom to top, across the inserted modules in a fairly laminar airflow pattern.

  - (Other) Fan(s) exhaust air from the top of the back panel of the chassis, achieving a push/pull effect, bottom/front to top/rear.

  - Each fan speed is monitored and controlled by a system status monitor (see 05 above).

- At least three Temperature Sensors.  Given the minimum set of three, they shall be placed as follows:

  - Two mounted in the frame above the card cage, and

  - One mounted in the exhaust air path,

all connected to, and report through the system status monitor (see 05 above).

- Autoranging Power Supply, providing at least 60A of +3.3V, 120A of +5V, 
10A of +12V, and 4A of -12V, powered by 110VAC.

- Front panel mounted Main Power and System Reset switches, with front panel main power ON indicator LED.

- Chassis mounted metal carrying handles.

- Fully assembled, wired, tested, with power cord and ready to use.

# Quantity

The total number of crates to ordered is 31.

# Delivery Schedule

# Acceptance Criteria

Delivered crates must meet manufacturer minimum specifications. Crates will be tested for  (what by whom … by PREP? )

# References

# Change Log

| Version | Issue Date | Concurrence | Description of Change |
| --- | --- | --- | --- |
| 1.0 |  | SW | Original |
| 1.1 |  | RGF | Fixed Outline. Shortened backplane to 12 slots in (2), (3) & (4). Added top & bottom transition card guides to (2.f). Propose incoming crates tested by PREP. |