Fermilab/BD/TEV

Beams-doc-xxx-v1

March xx, 2004

Tevatron Beam Position Monitor (BPM) Upgrade

Hardware Specifications for Data Acquisition

DRAFT DRAFT

Vince Pavlicek, Mark Bowden, Bill Haynes, Margaret Votava

Fermilab, Computing Division, CEPA

Bob Webber

Fermilab, Accelerator Division, Accelerator Controls Department

Abstract

This document contains the specification for the Beam Position Monitor/Beam Loss Monitor (BPM/BLM) upgrade data acquisition hardware.  Expected operating modes and interactions with the BPM/BLM software is described.  Analog signal processing, timing system and diagnostic circuits are specified in this document. Calibration and diagnostics procedures are described.

Overview	3

Requirements	4

Goals	4

Data Acquisition Operation	4

Functional Overview	4

Data Converter	5

Timing Module	5

Clock Signals	5

BPM Operations	5

BPM Measurement types	5

BPM Data Acquisition Modes	6

Normal operation	6

Injection	7

Turn by turn	8

Diagnostic Mode	8

Calibration Mode	8

BLM Operations	8

BPM/BLM Diagnostics	9

Self-Testing Procedures	9

Appendix	9

Schematics, Layouts, and drawings.	9

Crate Documentation	9

While this document is in draft form, Vince Pavlicek will be the editor.  If you have suggestions or changes, use a copy of the document, turn on change tracking, and send the document to Vince@fnal.gov.  He will integrate the changes into the database document.  Thanks.

# Overview

This note documents accumulated knowledge about the hardware needed for the data acquisition component of the Tevatron Beam Position Monitor (BPM) upgrade project.  The data acquisition hardware will digitize the analog position signal from the BPM sensors, digitally filter the signals and make them available to a VME front-end computer.  Figure 1 shows the functional block diagram and the different elements involved with the BPM upgrade project.

The Tevatron BPM sensors are two opposing stripline plates, approximately 20 cm long, oriented along the beam and each subtending approximately 110 degrees of arc around the beam.  The circular aperture of the pair is 6.6 cm.  There are connections at both ends of each plate, one connection emphasizing the proton direction of flight and the other the anti-proton direction.  The convention for the naming of the four signals from a BPM sensor are the A plate, proton and anti-proton end and the B plate, proton and anti-proton end.  Each of the BPM signals are treated identically in this Data Acquisition (DA) system except for a resistive attenuator which matches the signal amplitude to the AtoD converter input.  The signal amplitudes are proportional to the number of particles passing through the sensor.  In 2004 the amplitude of the proton signals is approximately 5 times as large as the anti-proton signal.  The sensors are on the end of quadrupole magnets in the beam tunnel and the BPM DA electronics modules are in service buildings around the ring.  200 to 300 meter long RG-8 cables bring the sensor signals to the DA system.  The signals go through the Diagnostic board first for level conditioning and bandpass filtering.  This module also has the capability to switch in a diagnostic signal and drive that signal out to the sensor.  By sequentially driving one output of a sensor and digitizing the other three sensor signals the condition of that sensor and cable plant can be determined.  Jumper cables move the signals from the Diagnostic module to the Analog to Digital converter board, an Echotek commercial digital signal receiver module.  The signals are converted from analog to digital, passed to a Digital Down Converter (DDC) for base banding and filtering and then placed in memory that is accessible through the VME backplane bus.  The VME crate controller is an MVME 2300 type processor that controls the data acquisition.  The software that resides on the front-end microprocessors, also referred to as the Data Acquisition (DA) software, is described in AD Document #860 Tevatron BPM Upgrade Software Specifications for Data Acquisition.  The system timing is controlled by the Timing module.  The timing is based on the Tevatron timing signals BSync and TClk.

Each front-end depicted in Figure 1 is a VME crate holding a series of BPM VME digitizing boards and BLM interface hardware.  One crate can also be referred as a house as there is one crate per service building. There are 24 service buildings or houses around the Tevatron ring, and each house has up to 6 BPM digitizing boards and 23 BLM digitizing boards in two BLM analog crates.  Figure 2 illustrates the organization of the cards in the BPMVME crate.

The BPM digitizing modules are Echotek module ECDR-GC814/8-xx, and each module digitizes data from 8 channels.  A given BPM sensor generates data on 4 channels – the A and B plates for the proton end of the sensor and the A and B plates for the antiproton end.  The digitized output that results from each channel may be either a calculated position or the raw data.  The details are in the Software Specifications document.  If it is the raw data, each channel is actually represented by two components: a real (Q) and imaginary (I) part.  The BLM analog circuitry and digitizers are in separate analog crates and the data is readout into the VME crate through a bus interface designed into the Timing Module or through a COTS digital I/O PMC board described below.

Figure 2 - Elements within a crate

The subrack controller board is responsible for establishing the communication link between user applications and the Echotek modules. All control and data transferred to/from the modules pass through the crate controller.

## Requirements

The requirements for this system are based on the system requirements documented in Tevatron BPM Upgrade Requirements Document (#554).

# Data Acquisition Operation

# Functional Overview

The communication between the front-end processor and the Echotek  modules happens through the VME backplane.  For the BLMs, data is exchanged through a digital I/O module on the timing board or as an I/O daughter board on the subrack processor.

Data coming from the BPM and BLM digitizers are stored into a set of buffers in the crate controller.  The depth and number of logical buffers that reside on the crate controller is defined in document #903.  At least some of the buffers, most notable the turn by turn data, is first stored in memory on the Echotek boards and then transferred to the crate controller on demand, as the processor/backplane does not have the bandwidth to acquire it in real time.  The actual physical implementation of the crate controller buffers will be described in the front-end software design document.

Data Converter

The Echotek module ECDR-GC814/8-xx is the baseline data converter.

[put data sheets for module and DDC in appendix]

Timing Module

[List Functional requirements]

[List I/O]

- Trigger possibilities: TCLK trigger

- TCLK + programmable delay

- TCLK + repeatable programmable delay

- BSYNCH trigger

- BSYNCH + programmable delay

- BSYNCH + repeatable programmable delay

- State device transition

- User request trigger – isn’t this the same of tclk + delay?

## Clock Signals

TCLK

BSYNCH

[What information they carry and how they are used here]

There are two TCLK decoders in a given house – one PCMUCD and one XXX. The ACNET/MOOC software infrastructure and applications are triggered by TCLK signals that are decoded by the PMUCD card. The other card will be discussed in subsequent sections. The crate controller can be programmed to read out BPM/BLM values based on a specific TCLK signal (e.g. TCLK $75). The crate controller does not receive BSYNCH events.

State device transition events are generated when a registered device changes its status, and a central service broadcasts the transition to predefined listeners. As an example of state device transition, the front-end can be waiting on the device V:CLDRST to switch to the “squeeze” state.

The preparation for read out is signaled by an arm event. An arm event may be originated by events generated by the above triggers. For example, a turn by turn measurement could be armed by TCLK.

## Data Acquisition Operations

## BPM Measurement types

In addition to the modes, there are two different types of measurements that can be made from the data in the digitizing cards. The data types are:

- Closed Orbit Measurements (aka Frame data). Frame data is an average of n measurements. The average is usually based on 8, 16, 32 or 64 single turn measurements, and is configurable. Frame data is the only data measurement made in normal operation mode. Note: the number used in the averages for normal operation mode is not necessarily the same number as in injection mode.

- Turn Data is the instantaneous single value (ie, not averaged over n readings) of the sensors once the trigger is received.

It is important to note that for turn measurements, all BPMs are triggered off the same bunch. However, for a closed orbit measurement, the specific bunches used in the averaging can be different across BPMs.

The data acquisition system must support systematic triggering of N events for both of these data types. For turn buffers, the arrays are of N consecutive measurements (ie, Turn by Turn). On the other hand, closed orbit buffers are built by a N triggers of a specific type.

The measurement types require different setups in the Echotek DDC modules, and, therefore have a time penalty associated with changing setup.  In general the data acquisition modes must switch to acquire a different type of measurement.

## BPM Data Acquisition Modes

There are different modes of BPM data acquisition. These modes are mutually exclusive due to the necessity to configure the filters and timing in the Echotek modules for a specific mode.  The modes are:

- Normal operation.

- Injection

- Turn by Turn

- Diagnostic

- Calibration

The modes are described in more detail in the following sections. The buffers are described in the Software specifications document.

### Normal operation

This is the default mode of the data acquisition system, and

Bandwidth and downconverter frequency are …

### Injection

Injection mode needs to be disabled and re-enabled on request because there are times when closed orbit data is preferred during proton injection.

### Turn by turn

Turn by turn mode is very similar to injection mode in that an 8K consecutive turns are taken when a turn by turn request is made.

The arming and triggering of the mode has not yet been specified.

### Diagnostic Mode

### Injection mode is disabled.

## Calibration Mode

## BLM Operations

The BLMs are simpler devices with relatively long time constants.  BLM values are read out periodically on triggers of the type described above.  There is no need for mode switching for BLMs, and there are no turn by turn requirements.  The BLM crate is read out through an External Device Bus (EDB).  The control, configuration and readout of the BLM devices is done through memory mapped registers within the EDB address space.

[Functional description]

[EDB description]

# Appendix

## Schematics, Layouts, and drawings.

## Crate Documentation

## Echotek DSPR Module

# Footnotes

The Tevatron Beam Position and Beam Loss Monitoring Systems (Beams-Doc-806)

# Text boxes

Front-end

card

User

Application

BPM/BLM

cards

- Data request

- Command

- Data request

- Command

- Position data

- Loss data

- Position data

- Loss data

ACNET

BPM

UTI

Sequencer

T pages

CLIB

VAX  (1)

ACNET

MOOC

DAQ Front-end Applications

Front-End (n)

Sun (DAQ engines) (n)

DAQ Jobs

Windows/Linux (n)

Java Application

Ethernet/RMI

java

BPM UTI

java

Ethernet

Front-end crate

FE Board

or

Crate Controller

Timing Module

BPM Cards

BLM Hardware (non VME)

Figure 1 Functional Block Diagram