# BPM Crate Prep

## Power-on Test of VME Crate

### Obtain IP address for crate diagnostics.

### Verify proper voltages of crate power supply without modules.

### Connect Ethernet line and test diagnostics.

## Slot-0 Processor Prep

### Pre-installation prep

#### Obtain IP address for card.

### Install PMC-UCD module.

### Install card in test-crate.

### Connect Ethernet line.

### Power-up processor in crate.

#### Verify communication with processor.

#### Verify proper software version is uploaded to processor.

### Verify timing

#### Confirm that processor is listening to TCLK.

#### Verify proper operation of program to different TCLK events.

## Timing Card Prep

### Install timing card in test-crate (with processor).

### Upload (install?) proper firmware to timing card.

### Connect TCLK and TVBS signals.

### Connect 53 MHz signal to PLL input and verify 74 MHz output clock.

### Set timing card into a diagnostics mode to verify continuous turn marker output.

### Set timing card into closed orbit mode to verify EchoTek closed orbit mode abort buffer triggers.

### Set timing card into turn-by-turn mode.

#### Verify reaction to BPM TBT TVBS event.

#### Verify proper number of turn marker triggers.

### Verify operation of diagnostic signal.

### Verify operation of BLM interface.

## Diagnostic Card Prep

### Install diagnostic card in test-crate.

### Connect diagnostic signal from timing card to diagnostic card.

### Connect test signal to BPM inputs.

## EchoTek Card Prep

### Install EchoTek card in test-crate.

### Connect digitizer clock and sample clock from timing module.

### Connect signal inputs from diagnostics card.

## Closed Orbit Mode Testing

### Connect signal generator to a set of diagnostics card BPM inputs (4 channels).

### Place trigger card into closed orbit mode.

### Place EchoTek card in raw signal mode to verify raw signals in EchoTek memory.

### Place EchoTek card in closed orbit mode.

### Program pattern of intensities from signal generators and verify proper position readings.

### Change signal pattern with signal generators and verify proper position readings.

## Calibration Routine Testing

### Place EchoTek in calibration mode.

### Program pattern of intensities from signal generators to verify proper calibration coefficient calculations.

## Turn-by-turn Mode Testing

### Place trigger card in diagnostic turn-by-turn mode.

### Place EchoTek card in TBT mode.

### Program patterns with signal generators and verify proper TBT data acquisition.

### Disconnect signal generators.

## Diagnostics Signal Testing

### Connect input of one diagnostic channel to RF splitter that drives the other three inputs.

### Place EchoTek card in raw signal mode and verify diagnostics signals.

### Disconnect splitters.

## BLM Communication

### Connect BLM communication line to test BLM system

### Verify robust communication with BLM test system.

# BPM Service Building Prep

## Connect Pbar Ends of BPMs in Tunnel.

## Cable Prep

### Dislodge pbar cables from Main Ring BPM racks.

### Pull pbar cables to new TeV BPM rack.

## Rack Prep (not F-houses)

### Remove cable TV.

### Remove TeV communication panel.

### Reconfigure safety system components (C-houses only).

### Prepare shelving for VME crate.

### Seat VME crate.

### Install cable organizer panels.

### Connect TCLK, TVBS, 53 MHz, and Ethernet to VME crate.

### Connect N-SMB cables to pbar cables and to diagnostic card inputs.

## On-line Configuration

### Activate Ethernet port connected to VME processor.

### Make changes to online configuration parameters to inform library functions and applications of addition in house.

## Power up Sequence

### Turn on crate

### Allow crate to boot, examine FP status LEDs

### Processor test and setup

#### Verify Ethernet communication with processor (ping?)

#### Download configuration parameters (done on boot?)

#### Verify TCLK connection to processor board

#### Place timing card in diagnostic mode and verify change.

#### Examine and verify EchoTek module memory and setup.

### Timing card tests

#### Verify proper PLL output frequency (80 MHz?)

#### Verify triggers (closed orbit & TBT)

#### Verify communication with BLM system

#### Set up diagnostic signal for power up tests

#### Verify diagnostic signal for power up tests

### EchoTek card tests

#### Drive beam signal inputs with signal generator.

##### Verify raw signal, bypass downconverter

##### Verify closed orbit bandwidth measurement

##### Verify 10 Hz closed orbit bandwidth measurement

##### Verify TBT bandwidth measurement

### Verify proper on-line communication and operation with diagnostics applications.

## Pbar Single Bunch Acquisition Timing

### Place timing card into single bunch acquisition mode.

### Place EchoTek cards into raw data mode.

### Examine EchoTek memory to verify that only beam from a single bunch is present.

# Single House Commissioning Plan

## Service Building Hardware Installation

### Cabling

#### Disconnect proton cables from NIM modules.

#### Connect N-SMB cables to proton cables.

#### Connect SMB cables to VME inputs.

#### Connect External Device Bus cable between BLM chassis and BLM interface on BPM system (if available).

#### Diagnostic signal calibration

##### Enable diagnostic outputs for channel 1 & 5 of each card.

##### Measure closed orbit bandwidth response of each signal path.

##### Archive the response measurements

##### Repeat the last three steps for channel pairs 2 & 6, 3 & 7, and 4 & 8.

## Beam First Turn Verification

### Scope verification

#### Compare timing of first turn trigger output from timing card with proton signal.

#### Verify that trigger is within 3 turns of proton injection.

#### Compare timing of sample trigger (AA marker) to proton signal.

#### Verify that trigger is within aperture delay of EchoTek sample.

### Trigger fine adjustment

#### Place EchoTek cards into raw data mode.

#### Trigger acquisition with first turn trigger.

#### Verify that first turn arrives at correct position in memory, fine tune trigger delay.

#### Place EchoTek cards into TBT mode and verify first turn goes to correct position in memory for all proton channels.

## Closed Orbit Verification

### Place EchoTek cards into closed orbit mode.

### Verify reasonable position and intensity values.

## On-line Configuration Parameters

### Make changes to online configuration parameters to activate upgrade.

### Verify proper on-line communication and operation with diagnostics applications.

# Miscellaneous Commissioning

## Turn-by-turn Verification

### Place EchoTek cards into TBT mode.

### Verify that beam signal occupies the proper location in memory, tune trigger delay.

## Proton Calibration

### Perform local bump around BPM and process a 7x7 grid of positions.

### Calculate corrections from I&Q data from each of the inputs for each of the positions.

### Save coefficients for corrections in memory for use in corrected position calculations.

## Proton Single Bunch Acquisition Timing

### Place timing card into single bunch acquisition mode.

### Place EchoTek cards into raw data mode.

### Examine EchoTek memory to verify that only beam from a single bunch is present.

## Service Building Decommissioning

### Remove old BPM modules and NIM crates

### Remove old BPM power supplies

### Remove TIM chassis

### Remove analog box

### Remove External Device Bus chassis