GMPS VXI CURRENT REGULATOR STATE DIAGRAM

State bits

| MSB 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | LSB 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| BDOTFLT | XDTRFLT | ACUP | ACFLG | SLWSTRT | BEGINSS | CNCTROK | GMPSON | RIRQOK | MCOOK | MCO |

MCO is set by program when MCO input interrupt is present.  Upon disappearance of MCO, the program zeroes voltage program output and then sits idle awaiting resumption of MCO interrupt signal.

MCOOK is set by program when it is determined that the MCO signal is sufficiently close in frequency to 15Hz.  In absence of MCOOK, program zeroes voltage program output and monitors MCO until it is again judged OK.

RIRQOK is set by program when an acceptable number of regular interrupts are received within MCO period.   In absence of RIRQOK, program zeroes voltage program output and monitors RIRQ until it is again judged OK.

GMPSON is set based upon external GMPS ON/OFF input signal. In absence of GMPSON, program zeroes voltage program output and monitors external GMPS ON/OFF signal until it again indicates ON.

CNCTROK is cleared by program when external CBC signal goes active (indicates any contactor being closed).  When CNCTROK is cleared, program begins delay during which time the voltage program output is zeroed.  When delay is completed, CNCTROK is reset and a new slow start is initiated as other conditions permit.

BEGINSS is set by program whenever conditions demand a new slow start of the voltage program output.  BEGINSS is reset when the requested slow start actually begins.

SLWSTRT is set during the time that the voltage program output slow start is actually in progress.

ACFLG is set by program based upon the external ACDC mode input signal.

ACUP is set by program based upon IMAX and IMIN transductor signals observed above acceptable threshold.

XDTRFLT is set by program when IMAX or IMIN transductor signals are determined to not be within an acceptable range.  XDTRFLT is cleared by initiation of new slow start or by dedicated reset control.

BDOTFLT is set???

ADJUSTABLE PARAMETERS (ALSO READABLE AND BACKED-UP IN BRAM)

AT LEAST FOR COMMISSIONING

Imin	Limits	min = 0	max = 200

Imax	Limits	min = 0	max = 1225 (10volts on ADC is 1250 with present transductor gain)

Bdotphaseset	Limits 	min = -8msec	max = +8msec

Acproportionalgain	Limits	min = 0	max = 100

Acintegralgain 	Limits	min = 0	max = 100

Dcproportionalgain 	Limits	min = 0	max = 100

Dcintegralgain 	Limits	min = 0	max = 100

Rdc     3.648  // dc resistance of magnet circuit 	Limits	min = 1	max = 10

Rac 3.84  // ac resistance of magnet circuit 	Limits	min = 1	max = 10

Bdotimindeltat -10000   // 12500 = 500usec 	Limits	min = -25000	max = 25000