Fermilab/BD/TEV

Beams-doc-1276

January 20, 2006

Version 06

Tevatron Beam Position Monitor Front End Software User’s Guide

DRAFT DRAFT DRAFT

Margaret Votava, Luciano Piccoli, Dehong Zhang, Kurt Biery

Fermilab, Computing Division, CEPA

Abstract

This document is geared to help past developers remember what they did, future developers to know how to build and distribute the software, commissioners to understand how to configure a system, and maintainers to help diagnose software problems. Contact tev-bpm-daqsw@fnal.gov for comments/updates.

1	Overview	4

2	Commissioning	4

2.1	Crate Controller Configuration	4

2.1.1	Registration	4

2.1.2	Boot Parameters	4

2.1.3	Startup Script	5

2.1.4	Changing the vxWorks startup script for all houses	7

2.1.5	Changing the vxWorks startup script for a particular house	7

2.2	Echotek Board Configuration	8

2.3	Timing Module Configuration	8

3	Developing	8

3.1	Build Environment	9

3.2	Build Instructions	9

3.3	Unit Tests	9

3.3.1	GBPM Unit Tests	9

3.3.2	TBPM Unit Tests	11

3.3.3	Echotek Driver Unit Test	11

4	Diagnostics	12

4.1	Software Statistics	12

4.1.1	bpmAlarm	13

4.1.2	bpmChangeBool	13

4.1.3	bpmChangeChannel	13

4.1.4	bpmChangeConfig	14

4.1.5	bpmChangeFloat	14

4.1.6	bpmClearAlarm	14

4.1.7	bpmClearBuffers	15

4.1.8	bpmDumpAll	15

4.1.9	bpmDumpBuffer	16

4.1.10	bpmMode	16

4.1.11	bpmPeek	17

4.1.12	bpmPeekPos	18

4.1.13	bpmStart	18

4.1.14	bpmStartTest	19

4.1.15	bpmShow	19

4.1.16	bpmShowAlarms	21

4.1.17	bpmShowBuffers	21

4.1.18	bpmShowChannels	22

4.1.19	bpmShowConfig	23

4.1.20	bpmShowGenerators	26

4.1.21	bpmShowModes	27

4.1.22	bpmShowQueues	28

4.1.23	bpmShowStates	28

4.1.24	bpmShowTasks	29

4.1.25	bpmShowTCLK	29

4.1.26	bpmPeekDiag	30

4.1.27	bpmTBTEvent	30

4.1.28	bpmTCLK	31

4.2	Trace Diagnostics	31

4.2.1	Trace Levels	32

4.3	VME Backplane Diagnostics	33

4.4	Looking at ACNET variables	39

5	Appendix: Node name/ACNET addresses	40

6	Appendix: Full VME trace	41

# Overview

This document is intended to be a guide for the front end users of the Tevatron BPM system. It is meant to help

- developers build system and verify the builds

- commissioners now how install and commission boards and crates

- maintainers diagnose problems

# Commissioning

## Crate Controller Configuration

The crate controller in a TBPM house is a Motorola 2400 running vxWorks. Node names are selected with the convention of tbpm<id> where <id> is a two character identifier of location in the ring, e.g., tbpma3.

### Registration

General instructions can be found at:

http://www-bd.fnal.gov/controls/micro_p/rom_install.html.

IP addresses must be obtained through the Acceleration Division networking group. Before requesting an IP address, you must know the Fermilab ID and Ethernet MAC address of the board. Once that has been identified, register the board at:

http://www-bdnew.fnal.gov/Netwebrequests/net-connection.asp

Once the IP address is obtained, each host will also need an ACNET address, which consists of the above node name plus an assigned trunk and node id. Contact Brian Hendricks to procure a trunk and node id.

### Boot Parameters

Boards are currently running VxWorks v5.5. Each crate controller should have the following boot parameters:

boot device          : dc0

processor number     : 0

host name            : fecode-bd

file name            : vxworks_boot/kernel/mv2400-512MB/vxWorks-a32-512

inet on ethernet (e) : 131.225.<xxx>.<yyy>:ffffff00

inet on backplane (b):

host inet (h)        : 131.225.121.145

gateway inet (g)     : 131.225.<xxx>.200

user (u)             : vxworks_boot

ftp password (pw) (blank = use rsh):

flags (f)            : 0x0

target name (tn)     : <nodename>_0x<trunkid><nodeid>

startup script (s)   : vxworks_boot/fe/tpm/tpmstartup

other (o)            :

Where <xxx>, <yyy>, <trunkid>, and <nodeid> are obtained in the registration step above.

Note that this is a custom kernel – it specifically adds the gateway node to the route table with the following command:

routeAdd "0.0.0.0", "131.225.<xxx>.200"

This is done so that all houses can use the same startup script.

### Startup Script

The Tevatron BPM software is designed to detect EchoTek board addresses at run time, so all BPMs can share the same startup script. The startup script pointed to in the boot parameters currently contains:

#------------------------------------------------------------------------

#--- General initialization

#------------------------------------------------------------------------

shellPromptSet( "Booting incomplete->" )

taskPrioritySet( taskIdFigure( "tExcTask" ), 1 )

taskPrioritySet( taskIdFigure( "tLogTask" ), 250 )

# get target name in 6 characters

targetName=malloc(20)

gethostname(targetName,20)

targetName[6]=0

#routeAdd ("239.128.1.1","131.225.126.200")

#------------------------------------------------------------------------

# mount NFS file systems - 1217, 5143 is user vxworks_boot group bdmicrop

#------------------------------------------------------------------------

topLevel="vxworks_write/fe/tbpm"

outputDir=malloc (strlen(topLevel) + strlen(targetName))

strcpy(outputDir,topLevel)

strcat(outputDir,targetName)

nfsMount( "fecode-bd", "vxworks_boot/module/PPC604", "/controls"  )

nfsMount( "fecode-bd", "vxworks_boot/fe", "/fe"  )

nfsMount( "fecode-bd", outputDir, "/write" )

nfsAuthUnixSet( "fecode-bd", 1217, 5143, 0, 0 )

# TEMPORARY

nfsMount( "fecode-bd", "vxworks_write/fe/fccts1", "/write1")

#------------------------------------------------------------------------

#--- Load MOOC and ACNET services

# THESE LOCATIONS NEEED TO CHANGE!!!!!

#-----------------------------------------------------------------------

# class library to initialize the techno box

ld (1, 1, "vxworks_boot/fe/rbpm/controls/pmcclassLib_mv2400-lastest.o");

# mooc

# 5.4 libraries

#ld < /controls/libpmctrig-latest.o

#ld < /controls/libssm-2.3.o

#ld < /controls/acnet-1.021.o

#ld < /controls/libmooc-3.6.o

# 5.5 libraries

ld < /controls/libpmctrig-2.13.o

ld < /controls/libssm-2.4.o

ld < /controls/acnet-1.026.o

ld < /controls/libmooc-3.7.o

#ld < /controls/libmooc-3.6.o

#ld < /controls/libmooc-latest.o

ACNET_SSM_avail=0

# what is this?

ld < /fe/rfiinst/devlib/VW_54/MVME2434/libmiscutil.out

# bpm stuff

ld < /fe/echotek_tbpm/libechotek_tbpm.out

# Warren's ECSG-1R3ADC-PMC I/O drivers

ld < /fe/rfiinst/lib/VW_54/MVME2434/libecsg1r3adcfermi.out

ld < /fe/tbpm/libculite.out

ld < /fe/gbpm/libgbpm.out

ld < /fe/tbpm/libtbpm.out

#------------------------------------------------------------------------

#--- Start things

# THESE LOCATIONS NEEED TO CHANGE!!!!!

#------------------------------------------------------------------------

# set the downloadable file

set_rbf_file ("vxworks_boot/fe/rbpm/controls/pmcucd.rbf");

# download the techno box; 0 is the instance or slot

pmcucd_start(0)

# set the addresses for ucd

pmcucd_set_adr (get_alteramem(0))

pmcucd_set_madr (get_alteramem(0)+0x1000)

initssc (0,calloc(0x10000,1))

MoocNew()

# void ecsg( int fref, int n, int p, int r, int b, int a, int c, int d );

# request 73.5 MHz and get 73.444444 MHz

#ecsg( 53104696, 504, 8, 40, 63, 0, 3, 3)

cd( "/fe/tbpm/ini" )

ecdr814gcReadSetup("53MHzNarrowBand.ini",    0);

ecdr814gcReadSetup("53MHzEnsemble.ini",      1);

ecdr814gcReadSetup("53MHzEnsemble-debug.ini",2);

#ecdr814gcReadSetup("rawDmaD64.ini",          3);

#ecdr814gcReadSetup("rawDmaD64.ini",          4);

#ecdr814gcReadSetup("rawDmaD64.ini",          5);

#ecdr814gcReadSetup("rawDmaD64.ini",          6);

ecdr814gcReadSetup("rawDmaD64.ini",          7);

ecdr814gcReadSetup("rawDmaD64Long.ini",      8);

ecdr814gcReadSetup("count.ini",             19);

ecdr814gcShowSetupAll();

# FilterSetIndex( 0, 23 )

# FilterSetIndex( 2, 23 )

#$$$MoocAlarmScan( 1 )

MoocDeviceDownLoad( 0 )

#------------------------------------------------------------------------

#--- Start trace buffer

#------------------------------------------------------------------------

# Clock prescale value

*0xfef80020=0x63ce0001

traceInit 100000,10,0xfef80100

traceMode 1

traceGlobalOn 0,25,0

traceOff 1,0,31,0

#traceMode 2

#traceGlobalOn 0,31,2

#traceOff 1,0,31,2

traceGlobalOff 17,17,0

traceGlobalOff 19,19,0

traceGlobalOff 20,20,0

#------------------------------------------------------------------------

#--- Finish up

#------------------------------------------------------------------------

prompt = malloc(30)

strcpy (prompt,targetName)

strcat (prompt,":tbpm> ")

shellPromptSet ( prompt )

free(prompt)

free(targetName)

free(outputDir)

traceOthersOff

#ecdr814gcInstall("ECDR-GC814-FV2",0x9000,0x19000000,0,"/config/rcvr_stratix_dual_14b.rbf",4)

#ecdr814gcDemo_count( "/write/Count_Test_0x9000", 1, 0, 0, 0, 100 )

TBPMSetPriority ("ucd60hz", 40);

TBPMSetPriority ("tExcTask", 40);

TBPMSetPriority ("tWdbTask", 40);

# Change the priority of the tShell task

TBPMChangeShellPriority (50);

#traceGlobalOff 12,12,0

#traceGlobalOff 16,16,0

traceGlobalOff 15,16,0

bpmStart 500

a_alarms_enable ()

a_reload_data ()

### Changing the vxWorks startup script for all houses

The Tevatron BPM houses share a common startup script that resides in nova.fnal.gov:/fecodde-bd/vxworks_boot/fe/tbpm; however, it is maintained in the tbpm CVS module. If the startup scripts for all houses need to change, please follow the build instructions in subsequent section.

Note that we are loading fixed versions of the ACNET/MOOC libraries. These versions need to match the versions of ACNET/MOOC header files that are compiled into both gbpm and tbpm. When reloading a different version of mooc, you will also need to edit the _acnetheaders.h file in both packages and recompile (see build instructions below).

### Changing the vxWorks startup script for a particular house

While debugging problems at a specific house, there will sometimes be a need to have a startup script that is specific to that particular house. Since this is only a temporary state, there is no need to track the changes. Simply:

nova> cd /fecode-bd/vxworks_boot/fe/tbpm

nova> cp tbpmstartup temp_startup

Edit the temp_startup script as necessary, being sure to change the vxworks boot parameters to use this script. Please remember to reset the boot parameters to use the canonical script when done.

## Echotek Board Configuration

The current Echotek driver supports up to 20 different setup files that are specified in the startup script.  Different configurations are used based on the mode of operation of the software. See document #860 for a description of the operational modes. In a particular mode, all Echotek modules in a house will use the same setup file, i.e. there is no provision for allowing the boards to be configured differently. By convention, these setup files have an extension of .ini.

Additionally, each board setup file contains another pointer to a file that contains information regarding a channel setup. Unless you really know what you’re doing, all channels should be configured with the same file. By convention, the channel setup files have an extension of .ch. By convention, the <abc>.ini file will read in a channel file named <abc>.ch.

The driver reads the associated files from the current working directory, so it’s important to cd to this directory in the VxWorks startup script.

| Operational Mode | Setup file index |
| --- | --- |
| Closed orbit | 0 |
| Turn X Turn | 1 |
| First injection | 1 |
| Raw ADC | 7 |
| Closed orbit debug | 2 |

Table 1 – Echotek configuration files used for the different modes of operation

## Timing Module Configuration

The timing board is described in detail in the document #1065. The base address defined for the timing board is 0x2000. If the board is set to any other address the software will not be able to contact it.

# Developing

There are 3 packages that constitute the Tevatron BPM software, they are:

- gbpm – generic bpm classes

- tbpm – bpm implementation specific to the tevatron

- echotek_tbpm – underlying echotek driver

## Build Environment

The Tevatron BPM software uses the RFI build methodology. Please refer to Beams Document #1271 for a description of the tools and, for first time users, how to configure your account on nova.fnal.gov. Following these instructions please set your work group to rfiinst.  All code is compiled on nova.fnal.gov.

## Build Instructions

All packages are built in a similar fashion

nova-> cd ~/esd/src		# only do once; create if needed

nova-> cvs checkout gbpm	# only do this once

nova-> setup gbpm

nova-> cvs update –d 		# cvs checkout gbpm if first time

nova-> make clean

nova-> make

nova-> make development		# put in development location

nova-> make test			# put in test location

nova-> make production		# put in production location (will

# be installed at next reboot)

Library locations are:

nova.fnal.gov:/fecode-bd/vxworks_boot/fe/gpm/devgpm.out  # development

nova.fnal.gov:/fecode-bd/vxworks_boot/fe/gpm/testgpm.out # test

nova.fnal.gov:/fecode-bd/vxworks_boot/fe/gpm/libgpm.out  # production

There is a similar set of commands to build tbpm and echotek_tbpm.

The Targets

## Unit Tests

The three tbpm packages have unit or module tests associated with them. The unit tests are designed to verify the core functionality of the packages. The tests should be used only when adding new functionality to the software in order to check whether new code has affected existing functions. The gbpm and tbpm packages use an underlying software package called culite.

The culite product is based on CppUnitLite, developed by Michael Feathers (http://c2.com/cgi/wiki?CppUnitLite). The source code is available from the Computing Division repository: cvsuser@cdcvs.fnal.gov:/cvs/cd. Version v1_0 is installed on nova on /fecode-bd/vxworks_boot/fe/culite.

### GBPM Unit Tests

The GBPM unit tests can be executed by running the command GBPMUnitTest, which should generate the following output:

fccts0:tbpm-dev> GBPMUnitTest

traceLevel array at 0x1da1ba50, traceTid array at 0x1da1bcd8

sizeof(ENTRY_T)=32

callocing 32000 bytes

traceCircQueBegin=0x1d2561f0, traceCircQueEnd=0x1d25deef (last byte of

allocation)

cfreeing

*** Starting Unit Tests ***

1) DataEntry

There were no test failures

2) TestDataEntry

There were no test failures

3) Packer

There were no test failures

4) TestPacker

There were no test failures

5) Event

There were no test failures

6) EventListener

There were no test failures

7) EventGenerator

There were no test failures

8) InterruptEventGenerator

There were no test failures

9) HardwareInterruptEventGenerator

There were no test failures

10) TimeEventGenerator

There were no test failures

11) AuxTimeEventGenerator

There were no test failures

12) TCLKEventGenerator

There were no test failures

13) AlarmGenerator

There were no test failures

14) DataAcquisitionTask

There were no test failures

15) DataBuffer

There were no test failures

16) CircularDataBuffer

There were no test failures

17) TestControl

There were no test failures

18) TestControlTask

There were no test failures

19) AlarmTask

There were no test failures

20) StateChangeEventGenerator

Please set V:PING to 5 or 10

Failure: "Listener didn't receive ping event in time" line 77 in

StateChangeEventGeneratorUnitTest.cpp

Failure: "For succeeding in this unit test you must set V:PING to 5 or

10" line 78 in StateChangeEventGeneratorUnitTest.cpp

Failure: "Listener didn't receive ping event in time" line 82 in

StateChangeEventGeneratorUnitTest.cpp

Failure: "For succeeding in this unit test you must set V:PING to 5 or

10" line 83 in StateChangeEventGeneratorUnitTest.cpp

There were 4 failures

21) ConfigStateChangeListener

There were no test failures

22) ConfigStateChangeTask

There were no test failures

23) FTPClass

There were no test failures

*** Unit Tests End ***

value = 2543116 = 0x26ce0c = cout

Each test (from 1 to 23) can be executed individually. The entry point is the name of the test followed by UnitTest (e.g. AlarmTaskUnitTest).

The StateChangeEventGenerator unit test expects the state device V:PING to be changed to 10 after the test is started. It waits for 5 seconds. If the state device does not change within this period the test fails. In order to change the value of V:PING one should use the ACL script window available through the ACNET pages. The command ‘set V:PING=10’ should be issued.

### TBPM Unit Tests

fccts0:tbpm-dev> TBPMUnitTest

traceLevel array at 0x1da1ba50, traceTid array at 0x1da1bcd8

sizeof(ENTRY_T)=32

traceCircQueBegin=0x1d254420, traceCircQueEnd=0x1d25c11f (last byte of

allocation)

*** Starting TBPMUnit Tests ***

1) TBPMClosedOrbitPacker

There were no test failures

2) TBPMTurnByTurnPacker

There were no test failures

3) TBPMDiagnosticSystem

There were no test failures

4) EchoTekPool

*** TBPMUnit Tests End ***

value = 2543116 = 0x26ce0c = cout

### Echotek Driver Unit Test

The Echotek driver uses a different testing structure. The command ecdr814gcUnitTest can be used to test the driver. The command has two arguments. The first is the address of the Echotek card to be tested, followed by the setup file index.

The addresses used for the Tevatron BPM project always start at 0x8000, increasing by 0x1000. The Echotek board closer to the processor board always has the lowest address. Neighbor boards to the right have higher base addresses.

The setup file index available can be showed by using the command ecdr814gcShowSetupAll:

fccts0:tbpm-dev> ecdr814gcShowSetupAll

0: 53MHzNarrowBand.ini

1: 53MHzEnsemble.ini

2: 53MHzEnsemble-debug.ini

3: 53MHzEnsembleSafe.ini

7: rawDmaD64.ini

8: rawDmaD64Long.ini

18: diagnostic_test.ini

19: count.inivalue = 0 = 0x0

The setup index 19 contains the most basic setup for testing an Echotek board. It sets the board to a simple counting mode and the unit test checks if the data generated is correct. The following is a sample output from the unit test:

fccts0:tbpm-dev> ecdr814gcUnitTest 0x8000,19

0x1da441e0 (tShell): Test board(s)  at:  0x8000 (0 means all), using

setup #19 ( count.ini )

0x1da441e0 (tShell): Candiate board at:  0x8000,  local address:  0xfbff8000

0x1da441e0 (tShell): Program the gray chips ...

0x1da441e0 (tShell): Set up the daq conditions

0x1da441e0 (tShell): Reset the board(s)

0x1da441e0 (tShell): Do a software trigger

0x1da441e0 (tShell): Read out the board(s) ...

value = 32 = 0x20 = ' '

fccts0:tbpm-dev> 0x1da441e0 (tShell): Check the counting sequences ...

0x1da441e0 (tShell): Done with the checking

# Diagnostics

Once the system is up and running, how do you start analyzing problems? There are many diagnostic tools available. Choosing the right one to most expediently analyze the problem is a combination of experience and instinct. The following sections describe various diagnostic information that are available in the tbpm software.

## Software Statistics

The bpm software internally keeps structures that one can peek at through the vxworks shell. The bpmHelp command will list the most current set of commands that are available:

tbpma0:tbpm> bpmHelp

BPMHelp> help

list - display list of available BPM commands.

help - print this help.

quit - exit BPM help.

BPMHelp> list

Commands available:

bpmAlarm                bpmChangeBool

bpmChangeChannel        bpmChangeConfig

bpmChangeFloat          bpmClearAlarm

bpmClearBuffers         bpmDumpAll

bpmDumpBuffer           bpmMode

bpmPeek                 bpmPeekPos

bpmStart                bpmStartTest

bpmShow                 bpmShowAlarms

bpmShowBuffers          bpmShowChannels

bpmShowConfig           bpmShowGenerators

bpmShowModes            bpmShowQueues

bpmShowStates           bpmShowTasks

bpmShowTCLK             bpmPeekDiag

bpmTBTEvent             bpmTCLK

BPMHelp> quit

value = 0 = 0x0

tbpma0:tbpm>

The following are the description for each of the commands available through the bpmHelp command and a sample output where applicable.

### bpmAlarm

BPMHelp> bpmAlarm

----------------------------------------------------

bpmAlarm (alarmNumber, alarmMessage)

Description:

Generate an alarm that is processed by the system

Parameters:

alarmNumber: integer number for alarm

alarmMessage: character string with message

----------------------------------------------------

The bpmAlarm command should be used for development only.

### bpmChangeBool

BPMHelp> bpmChangeBool

----------------------------------------------------

bpmChangeBool (index, value)

Description:

Assign a new value to the boolean variable at the given index

Parameters:

index: entry number in the config manager to be changed

value: boolean value to be assigned (0 or 1)

----------------------------------------------------

This command can be used to change any booleans shown by the bpmShowConfig command. There are only a few boolean variables defined in the system, all of them used for development and debugging purposes.

+-------- Booleans -----------------------------------+

| 20    - USE_TEST_SOURCE               false

| 21    - DIAGNOSTIC_MODE               false

| 22    - CHECK_PHASE                   false

| 23    - USE_CALIBRATION               false

+-------------   End of configuration   -------------+

### bpmChangeChannel

BPMHelp> bpmChangeChannel

----------------------------------------------------

bpmChangeChannel (bpm, type, on/off)

Description:

Enable or disable the readout of a particular proton or pbar channel

Parameters:

bpm: bpm index (0 - 11), -1 to change all bpms

type: 0 for proton, 1 for pbar and -1 for both

on/off: 0 to turn channel off, 1 to turn it on

----------------------------------------------------

For more information check the bpmShowChannel command section.

Be careful when using this command. You may disable a bpm channel by mistake.

### bpmChangeConfig

BPMHelp> bpmChangeConfig

----------------------------------------------------

bpmChangeConfig (index, value)

Description:

Assign a new value to the integer variable at the given index

Parameters:

index: entry number in the config manager to be changed

value: integer value to be assigned

----------------------------------------------------

This command can be used to change any integers shown by the bpmShowConfig command.

Be careful when using this command. You may change by mistake important system parameters.

### bpmChangeFloat

BPMHelp> bpmChangeFloat

----------------------------------------------------

bpmChangeFloat (index, value)

Description:

Assign a new value to the float variable at the given index

Parameters:

index: entry number in the config manager to be changed

value: float value to be assigned

----------------------------------------------------

This command can be used to change any floats shown by the bpmShowConfig command. There are only a few float variables defined in the system. They are used for defining thresholds, default values and parameters.

+--------  Floats -------------------------------------+

| 20    - PROTON_INTENSITY_THRESHOLD    10

| 21    - PBAR_INTENSITY_THRESHOLD      20

| 22    - LOW_INTENSITY_POSITION        999

| 23    - BPM_SCALE_FACTOR              26

| 24    - SAFE_MODE_VARIATION           0.1

### bpmClearAlarm

BPMHelp> bpmClearAlarm

----------------------------------------------------

bpmClearAlarm (alarmNumber)

Description:

Clear the specified alarm

Parameters:

alarmNumber: alarm to be cleared

----------------------------------------------------

### bpmClearBuffers

BPMHelp> bpmClearBuffers

----------------------------------------------------

bpmClearBuffers ()

Description:

Clear all buffers in the system

----------------------------------------------------

All buffers in the system are cleared with this command. Pointers are reset and data is zeroed.

### bpmDumpAll

BPMHelp> bpmDumpAll

----------------------------------------------------

bpmDumpAll (buffer)

Description:

Display all contents of the buffer for all bpms. The position/intensities and I/Q pairs are shown

Parameters:

buffer:

fast abort (11)

slow abort (12)

profile (13)

display (14)

user TCLK (15)

turn-by-turn (16)

injection (17)

injection closed orbit (18)

diagnostic (19)

closed orbit (20)

safe injection (21)

----------------------------------------------------

The buffer index starts at 11 instead of 0. Lower buffer indexes are reserved for internal use and tests.

Data from all BPMs for the specified buffer is written to the standard output. The output can be redirected to a file. This command is an alternative for ACNET when reading data from the front-ends. The following example shows how to read all fast abort data for all front-end BPMs:

tbpma0:tbpm> bpmDumpAll 11 > /write1/fastAbort-A0.data

value = 0 = 0x0

tbpma0:tbpm>

The output generated has the following pattern:

### BPM 0

1010>[-0.845604, 115.784][-9.48365, 58.5636] - [-57,-18] [-56,1] [-34,-21] [-15,-11]

1011>[-0.864243, 115.444][-9.58456, 59.1785] - [-49,34] [-33,45] [-38,14] [-18,5]

1012>[-0.744931, 114.862][-9.68906, 59.8979] - [-3,59] [14,54] [-13,39] [-8,17]

1013>[-0.883092, 116.123][-10.0692, 58.1158] - [30,-52] [11,-55] [29,-28] [14,-11]

1014>[-0.803378, 116.031][-9.91739, 58.1995] - [-21,-56] [-35,-44] [-4,-40] [0,-18]

…

### BPM 3

778>[7.72163, 172.731][9.01028, 34.9162] - [-17,71] [-27,96] [7,-12] [1,-21]

779>[7.70948, 174.039][9.41197, 34.8618] - [44,59] [58,82] [-4,-13] [-16,-14]

780>[7.7781, 173.306][9.35311, 33.2237] - [73,3] [100,7] [-12,-5] [-20,3]

781>[7.82088, 173.499][10.0281, 33.1212] - [48,-55] [68,-74] [-11,6] [-10,18]

782>[7.67408, 174.288][9.73124, 34.7426] - [-67,31] [-93,38] [13,-3] [17,-13]

The first number (e.g. 1011>) can be ignored. It is the entry number within the buffer. The following numbers are the [proton position, proton intensity][anti-proton position, anti-proton intensity]. The raw I and Q values are printed after the dash. The first two [I,Q] pairs are from the proton channels and the last two are from the anti-proton channels.

Even though the front-end may have only a few BPMs (e.g. A0 has 4), the system allocates buffers for the maximum of 12 BPMs. Values for the non-existing BPMs are still printed out with the bpmDumpAll command, they will be all zeros.

Please check section 4.1.17 for potential problems regarding this command.

### bpmDumpBuffer

BPMHelp> bpmDumpBuffer

----------------------------------------------------

bpmDumpBuffer (bpm, buffer)

Description:

Display all contents of the buffer for a given bpm. The position/intensities and I/Q pairs are shown

Parameters:

bpm: 0 through 11

buffer:

fast abort (11)

slow abort (12)

profile (13)

display (14)

user TCLK (15)

turn-by-turn (16)

injection (17)

injection closed orbit (18)

diagnostic (19)

closed orbit (20)

safe injection (21)

----------------------------------------------------

This command alows the user to dump the contents of a given buffer for a given BPM. The BPM index always starts at 0.

Please check section 4.1.17 for potential problems regarding this command.

### bpmMode

BPMHelp> bpmMode

----------------------------------------------------

bpmMode (mode, turns)

Description:

Change system the mode of operation

Parameters:

mode: 0 for displaying list of modes

turns: number of turns if in turn-by-turn mode

----------------------------------------------------

The bpmMode command can be used to force the system to enter a specific mode of operation. The system changes mode automatically according to TCLKs received.

If the system is not in the expected mode of operation, e.g. in turn-by-turn or abort mode when it should be in the closed orbit mode, one can use the command 'bpmMode 10' to force the front-end to get back to the closed orbit mode.

### bpmPeek

BPMHelp> bpmPeek

----------------------------------------------------

bpmPeek (bpm, buffer)

Description:

Show the latest entry for a selected buffer

Parameters:

bpm: 0 through 11

buffer:

fast abort (11)

slow abort (12)

profile (13)

display (14)

user TCLK (15)

turn-by-turn (16)

injection (17)

injection closed orbit (18)

diagnostic (19)

closed orbit (20)

safe injection (21)

The bpmPeek command can be used to check the most recent data from any of the system buffers. If no parameters are passed to the command, the most recent value from the first bpm on the closed orbit buffer (index 20) is displayed. The following is an example of a bpmPeek  command.

tbpma0:tbpm> bpmPeek

========= BPM 0 [1023] ====

Status: 0x0

Proton position=5.164508 intensity=3918.397461

Pbar position=3.024627 intensity=2622.326904

I/Q Pairs: [-1362 781] [-1557 1758] [310 807] [299 505]

Turn Timestamp: MON SEP 19 11:20:54 2005

BPM Timestamp: 0x0000 0x0499 0x7ab9 0x0f8f

=========================

The status shows the intensity for the BPM is above the predefined threshold. The first bit represents the status of the proton channels and the second bit is the status of the anti-proton channels. The intensity threshold defined for protons and anti-protons are available through the bpmShowConfig command.

The next two lines show the calculated positions and intensities for proton and anti-proton channels, followed by the raw I and Q values for the two proton channels and the two anti-proton channels.

There are two timestamps displayed. The first (Turn Timestamp) is a course time of the day timestamp. The BPM Timestamp is a counter from the timing board, which is reset on every injection (BSYNC event 0x7C) and incremented at 106 MHz.

Please check section 4.1.17 for potential problems regarding this command.

### bpmPeekPos

BPMHelp> bpmPeekPos

----------------------------------------------------

bpmPeekPos (bpm, buffer, position, format)

Description:

Show element at specified location

Parameters:

bpm: 0 through 11

buffer:

fast abort (11)

slow abort (12)

profile (13)

display (14)

user TCLK (15)

turn-by-turn (16)

injection (17)

injection closed orbit (18)

diagnostic (19)

closed orbit (20)

safe injection (21)

position: element index in buffer (starting at 0)

format: 0 (proton/pbar) - 1 (proton) - 2 (pbar)

----------------------------------------------------

The bpmPeekPos command is very similar to bpmPeek. However it allows the user to specify a position within the buffer. The first position is always zero and the last one is the buffer size minus one. The following example shows the entry number 500 of the fast abort buffer. An explanation of each field displayed is available in the previous command description.

tbpma0:tbpm> bpmPeekPos 0,11,500

========= BPM 0 [500] ====

Status: 0x0

Proton position=4.962633 intensity=3758.565430

Pbar position=3.048932 intensity=2361.975586

I/Q Pairs: [-237 1502] [377 2206] [717 299] [497 115]

Turn Timestamp: MON SEP 19 14:12:14 2005

BPM Timestamp: 0x0000 0x0597 0xaf92 0x2e0f

=========================

### bpmStart

BPMHelp> bpmStart

----------------------------------------------------

bpmStart (rate, source, useTCLK, bsyncBase)

Description:

Start up the TBPM system

Parameters:

rate: closed orbit rate (in Hz)

source: 0 (EchoTek) - 1 (TestEchoTek)

useTCLK: 0 (enable) - 1 (disable)

bsyncBase: BSYNC decoder base address

----------------------------------------------------

The bpmStart command is invoked by the production startup script. When using the development startup script the user should use this command to start the system. Usually the ACNET/MOOC processes are already started by the script.

If no parameters are specified to the command the system is started with the closed orbit rate set to 50 Hz. For starting it at 500 Hz the first parameter should be specified. The next three parameters should be used for development and debugging only. Source defines whether the Echotek boards are used or data are generated by software (TestEchoTek); useTCLK enables or disables the decoding of TCLK signals; and bsyncBase defines the base address of the timing board.

### bpmStartTest

BPMHelp> bpmStartTest

----------------------------------------------------

bpmStartTest (rate)

Description:

Start the TBPM system using no hardware

Parameters:

rate: closed orbit rate (in Hz)

----------------------------------------------------

This command used for development and debugging only. It is used instead of the regular bpmStart command. The system is started up without configuring the Echotek boards and the timing hardware.

### bpmShow

BPMHelp> bpmShow

----------------------------------------------------

bpmShow ()

Description:

Display general system information

----------------------------------------------------

The bpmShow command displays general information about the system. A typical output of this command consists of three parts. The first shows the current mode of operation (for all available modes use the command bpmMode without arguments), the state (usually the same as the mode), the closed orbit frequency, status of the diagnostics (on or off) and the versions of the GBPM and TBPM libraries.

If the mode of operation shown by bpmShow is not in the expected mode of operation, e.g. in turn-by-turn or abort mode when it should be in the closed orbit mode, one can use the command 'bpmMode 10' to force the front-end to get back to the closed orbit mode.

The second part of the report contains information regarding the Echotek boards and their configuration. The number of boards is shows, followed by the current burst count (1 for closed orbit mode and 8192 for turn-by-turn mode), number of triggers, samples to be skipped and channel pair delays. The versions of the driver as well as the FPGA code are displayed. The following fields show information about calibration. Currently the upper portion (Survey offsets used (house)) is being used, but the system is expected to start using the data shown on the “Calibration Data” section. That calibration data is read from a database and pushed down to the front-ends.

The last part contains information about the timing system (please refer to document 1065 for more details about the timing system).

If the system is not taking data, e.g. the values on Fast Time Plots are stuck on the same value, please use the bpmShow command and check if the mode of operation is correct of if there is some missing signal reported by the timing system report, e.g. 53MHz: not present.

tbpma0:tbpm> bpmShow

TBPM system started on THU SEP 08 10:37:14 2005

Mode:   10 (CLOSED ORBIT)

State:  10

Freq:   500 Hz

Diag:   off

GBPM version: v1_37

TBPM version: v1_61

# Hit enter to continue or 'q'>

EchoTekPool information:

Boards: 2

Burst:  1

Trig:   1

Skip:   0

Delays: 4 4 4 4

6 6 6 6

Driver version: v1_6

FPGA version:   2000007

Survey offsets used (a0):

0, -0.4, 0.8, 3.7

Calibration Data:

BPM     Scale   Surv.   Fud(p)  Fud(a)  T(p)    T(a)    K(p)    K(a)

0       26      0       0       0       0.89060 1.00046 0       0

1       26      -0.4    0       0       1.02001 0.95634 0       0

2       26      0.8     0       0       1.03338 0.94923 0       0

3       26      3.7     0       0       1.01676 0.95797 0       0

# Hit enter to continue or 'q'>

Timing Signal Generator information:

Acquisition enabled

BSYNC: enabled  TCLK: enabled   53MHz: present

Turn event:   0xaa      present

Start event:  0x10      NOT PRESENT

Trig. delay:  6

Global delay: 0

House delay:  2140

Board delays: 0 2 0 0 0 0

Turns counter: -132142356

Missing turn: 66542

FPGA version: 2.1.1

BSYNC received: 0x7c 0xaa 0xda

TCLK received: 0x0 0x2 0x5 0x7 0x8 0x9 0xa 0xb 0xc 0xd

0xe 0xf 0x10 0x11 0x12 0x13 0x14 0x15 0x16 0x17

0x18 0x19 0x1a 0x1b 0x1c 0x1d 0x1e 0x1f 0x21 0x22

0x23 0x24 0x25 0x26 0x27 0x28 0x29 0x2a 0x2b 0x2c

0x2d 0x2e 0x2f 0x30 0x31 0x34 0x35 0x36 0x38 0x39

0x3a 0x3b 0x3c 0x3d 0x40 0x41 0x42 0x43 0x44 0x45

0x46 0x47 0x48 0x4a 0x4b 0x4c 0x4d 0x4e 0x4f 0x50

0x51 0x52 0x53 0x55 0x5b 0x5c 0x5d 0x5e 0x60 0x61

0x62 0x63 0x64 0x65 0x68 0x69 0x6c 0x6d 0x6f 0x71

0x72 0x73 0x74 0x75 0x76 0x77 0x78 0x79 0x7a 0x7b

0x7c 0x7d 0x7e 0x80 0x81 0x82 0x83 0x84 0x87 0x88

0x8c 0x8d 0x8e 0x8f 0x90 0x91 0x92 0x93 0x94 0x95

0x99 0x9a 0x9c 0xa4 0xa5 0xa6 0xa8 0xa9 0xb8 0xc0

0xc1 0xc3 0xc4 0xc5 0xc6 0xc7 0xc9 0xcb 0xce 0xcf

0xd4 0xdb 0xdd 0xe0 0xe2 0xe3 0xe4 0xe7 0xe8 0xeb

0xec 0xed 0xee 0xef 0xf0 0xf2 0xf3 0xf5 0xf7 0xfa

### bpmShowAlarms

BPMHelp> bpmShowAlarms

----------------------------------------------------

bpmShowAlarms (enabled)

Description:

Show current alarms in the system

Parameters:

enabled: 0 (only enabled alarms) - 1 (all alarms)

----------------------------------------------------

This command displays a summary of the alarms detected by the front-end system. The current version (GBPM v1_37 and TBPM v1_61) defines the following alarms:

0 – Missing TCLK signal

1 – Missing BSYNC signal

2 – Missing 53 MHz signal

3 – Failure to start timing board

4 – Failure to start EchoTek boards

5 – Low proton intensity detected on closed orbit

6 – Low pbar intensity detected on closed orbit

7 – Safe injection mode is enabled

The following is the output of the bpmShowAlarms command:

tbpma0:tbpm> bpmShowAlarms

Alarm   Counter Low     High    Clear   Disp    Enable  Msg

0       0       -       -       0       0       1

1       0       -       -       0       0       1

2       0       -       -       0       0       1

3       0       -       -       0       0       1

4       0       -       -       0       0       1

5       10	 -       -       0       0       1 Low proton intensity on closed orbit.

6       147     -       -       0       0       1 Low pbar intensity on closed orbit.

7       0       -       -       0       0       1

These alarms should be mapped to ACNET alarms. The current implementation does not generate ACNET alarms. Alarms 5 and 6, for low signal intensity, should be disregarded. Many of those alarms, possibly all of them, are being mistakenly generated. The software does not check if the machine has protons or anti-protons circulating and assumes that the low intensity is an error instead of the simple lack of particles in the machine.

### bpmShowBuffers

BPMHelp> bpmShowBuffers

----------------------------------------------------

bpmShowBuffers ()

Description:

Display current status/info of system buffers

----------------------------------------------------

The bpmShowBuffers command can be used to monitor the current number of elements in all the buffers available in the system. An example of output is shown below. For each buffer the current number of elements and the maximum number of elements is shown. The output also informs if there are any blocked tasks trying to access the buffer. Buffers are shared resources between the system tasks and can be accessed only after the task has acquired a lock associated with the buffer. If the task is waiting for the buffer lock then its name will be printed out as a blocked task.

tbpma0:tbpm> bpmShowBuffers

System Buffers:

Elemts  Size    Blocked Tasks

ClosedOrbit:    1024    1024    None

FastAbort:      1024    1024    None

SlowAbort:      1024    1024    None

Profile:        36      128     None

Display:        0       1       None

TurnByTurn:     8192    8192    None

I.TurnByTurn:   8192    8192    None

SafeInjection:  0       8192    None

I.ClosedOrbit:  1       1       None

User TCLK:      0       128     None

The bpmPeek and bpmDump commands all need to access to get the buffer lock before accessing the data. If those commands are killed in the middle of the processing (after acquiring the lock) then the buffer will not be accessible by other tasks. For example, if there was a bpmPeek command invoked to check the latest closed orbit value and the user killed it using ^C before it finished, then the system will not be able to add new values to the buffer and bpmShowBuffer will show that the ClosedOrbit task is blocked.

### bpmShowChannels

BPMHelp> bpmShowChannels

----------------------------------------------------

bpmShowChannels ()

Description:

Display EchoTek channel mask

----------------------------------------------------

The front-end creates buffers for the maximum amount of BPMs for a house, which is 12. However not all houses have 12 BPMs installed. In fact only 1 of the 27 houses around the ring has the 12 BPMs. In order to avoid processing unnecessary data, the front-end system defines a channel mask for every house. The values are hardcoded, but the configuration of what channel is on or off can be controlled by the bpmChangeChannel command. The front-end knows which house it is running based on the hostname. Next is an example of the command output.

tbpma0:tbpm> bpmShowChannels

BPM 0: proton [enabled] pbar [enabled]

BPM 1: proton [enabled] pbar [enabled]

BPM 2: proton [enabled] pbar [enabled]

BPM 3: proton [enabled] pbar [enabled]

BPM 4: proton [disabled] pbar [disabled]

BPM 5: proton [disabled] pbar [disabled]

BPM 6: proton [disabled] pbar [disabled]

BPM 7: proton [disabled] pbar [disabled]

BPM 8: proton [disabled] pbar [disabled]

BPM 9: proton [disabled] pbar [disabled]

BPM 10: proton [disabled] pbar [disabled]

BPM 11: proton [disabled] pbar [disabled]

### bpmShowConfig

BPMHelp> bpmShowConfig

----------------------------------------------------

bpmShowConfig ()

Description:

Display detailed system configuration

----------------------------------------------------

The front-end software has several configuration parameters that can be changed by the user while the system is running (bpmChangeConfig, bpmChangeFloat, bpmChangeBool). Some of those parameters are used at initialization time and event if the user changes them later the system will not be affected by its change. For example the CLOSED_ORBIT_RATE (index 21) value is used only when the system is started.

The command shows all variables defined in the system at once. One can always redirect the command output to a file if it is not possible to see all values. The following is a sample output:

tbpma0:tbpm> bpmShowConfig

+--------------- BPM Configuration      ---------------+

| Index Variable                        Value

+----------------------------------------------------+

|         Integers

| 0     - DEFAULT_EVENT_QUEUE_SIZE      100

| 1     - TCLK_REG_BASE                 0x6000

| 2     - TCKL_MEM_BASE                 0x8000000

| 3     - BSYNC_REG_BASE                0x2000

| 4     - CONTROL_TASK_PRIORITY         15

| 5     - ALARM_TASK_PRIORITY           42

| 5     - ALARM_TASK_PRIORITY           42

| 7     - BSYNC_START_EVENT             0x10

| 8     - BSYNC_TURN_EVENT              0xaa

| 9     - CONTROL_TASK                  0x1da35110

| 10    - MODE                          10

| 11    - MODE_CHANGE_TIME              1127943228

| 12    - START_TIME                    1126175834

|        Booleans

| 0     - DEFAULT_READOUT               false

| 1     - USE_TEST_TCLK                 false

| 2     - USE_TEST_TIMING               false

+-------------   End of configuration   -------------+

+-------------   TeV BPM Configuration  -------------+

| Index Variable                        Value

+----------------------------------------------------+

+-------- Integers ----------------------------------+

| 20    - SAMPLES                       64

| 21    - CLOSED_ORBIT_RATE             500

| 22    - DATA_SOURCE                   0

| 23    - TRIGGER_TYPE                  0

| 24    - TRIGGER_VALUE                 500

| 25    - BUNCH_TYPE_PROTON             2

| 26    - BUNCH_TYPE_PBAR               2

| 27    - MACHINE_STATE                 14

| 28    - HELIX_STATE                   2

| 29    - PROTON_BUNCHES                0

| 30    - PBAR_BUNCHES                  0

| 31    - ECHOTEK_CONFIG                0

| 32    - ECHOTEK_READ_TIMEOUT          10

| 33    - DIAG_CHANNELA                 0

| 34    - DIAG_CHANNELB                 1

| 35    - DIAG_TRIGGER_TYPE             0

| 36    - DIAG_TRIGGER_VALUE            500

| 37    - DIAG_DATA_MODE                0

| 38    - DIAG_RAW_DATA_TYPE            2

| 39    - DATA_MODE                     0

| 40    - CLOSED_ORBIT_PRIORITY         19

| 41    - FAST_ABORT_PRIORITY           25

| 42    - SLOW_ABORT_PRIORITY           35

| 43    - PROFILE_PRIORITY              35

| 44    - DISPLAY_PRIORITY              35

| 45    - TBT_PRIORITY                  18

| 46    - TBT_PRIORITY_LOW              27

| 47    - INJEC_TBT_PRIORITY            18

| 48    - INJ_TBT_PRIORITY_LOW          27

| 49    - INJEC_CO_PRIORITY             30

| 50    - USER_TCLK_PRIORITY            35

| 51    - TBT_START_EVENT               0xda

| 52    - ECHOTEK_TRIGGER_COUNT         8192

| 53    - ECHOTEK_BURST_COUNT           32

| 54    - DEFAULT_USER_TCLK             0xff

| 55    - PROFILE_CLEAR_TCLK            0xc2

| 56    - DISPLAY_CLEAR_TCLK            0xc1

| 57    - SLOW_ABORT_SAMPLES            100

| 58    - ACQSPEC_ARM_EVENT             0xda

| 59    - ACQSPEC_TRIGGER_EVENT         0xaa

| 60    - ACQSPEC_MODE                  0

| 61    - INJ_TBT_START_EVENT           0x7c

| 62    - INJ_TBT_TRIGGER_COUNT         8192

| 63    - TBT_ARM_EVENT                 0x4c

| 64    - TEVBPM_STATE                  2

| 65    - INJ_CO_SKIP                   0

| 66    - INJ_CO_TURNS                  8192

| 67    - CHECK_STATUS_TIME             3

| 68    - FLASH_FRAME_INDEX             9

| 69    - CLOSED_ORBIT_CONFIG           0

| 70    - TURN_BY_TURN_CONFIG           1

| 71    - SAFE_MODE_CONFIG              3

| 72    - COUNT_CONFIG                  19

| 73    - DEBUG_CO_CONFIG               2

| 74    - RAW_CO_CONFIG                 7

| 75    - ZERO_FIFO                     0

| 76    - SAFE_MODE_STATE               1

| 77    - SAFE_MODE_START_EVENT         0x7c

| 78    - SAFE_MODE_WINDOW              10

| 79    - TBPMSF_STATE                  1

+--------  Floats -------------------------------------+

| 20    - PROTON_INTENSITY_THRESHOLD    10

| 21    - PBAR_INTENSITY_THRESHOLD      20

| 22    - LOW_INTENSITY_POSITION        999

| 23    - BPM_SCALE_FACTOR              26

| 24    - SAFE_MODE_VARIATION           0.1

+-------- Booleans -----------------------------------+

| 20    - USE_TEST_SOURCE               false

| 21    - DIAGNOSTIC_MODE               false

| 22    - CHECK_PHASE                   false

| 23    - USE_CALIBRATION               false

+-------------   End of configuration   -------------+

The following tables contain the meaning of all variables. The names shown by bpmShowConfig command are used internally with prefixes such as CFG_INT, CFG_BOOL, TBPM_CFG_INT, TBPM_CFG_BOOL.

| Variable | Meaning |
| --- | --- |
| CFG_INT_TCLK_REG_BASE | VME base address for TCLK registers |
| CFG_INT_TCLK_MEM_BASE | VME base address for TCLK memory |
| CFG_INT_BSYNC_REG_BASE | VME base address for BSYNC decoder register |
| CFG_INT_CONTROL_TASK_PRIORITY | Priority for the control task |
| CFG_INT_ALARM_TASK_PRIORITY | Priority for the alarm task |
| CFG_INT_STATE_CHANGE_TASK_PRIORITY | Priority for state change task |
| CFG_INT_BSYNC_START_EVENT | BSYNC start event |
| CFG_INT_BSYNC_TURN_EVENT | BSYNC turn event |
| CFG_INT_CONTROL_TASK | ptr to the control task (used for sending evts) |
| CFG_INT_MODE | system mode of operation |
| CFG_INT_MODE_CHANGE_TIME | time of the last mode change |
| CFG_INT_START_TIME | system startup time |

Table 2 – Integer configuration variables defined for GBPM

| Variable | true | false |
| --- | --- | --- |
| TBPM_CFG_BOOL_USE_TEST_TCLK | don't use TCLK board | use TCLK board |
| TBPM_CFG_BOOL_USE_TEST_TIMING | use 2ms timer | use Timing board |

Table 3 – Boolean configuration variables defined for GBPM

| Variable | Meaning |
| --- | --- |
| TBPM_CFG_INT_SAMPLES | number of samples taken after the turn marker |
| TBPM_CFG_INT_CLOSED_ORBIT_RATE | rate (in Hz) for closed orbit sampling |
| TBPM_CFG_INT_DATA_SOURCE | source of the data (see TBPMDefs.hpp for values) |
| TBPM_CFG_INT_TRIGGER_TYPE | type of the trigger in use (idem) |
| TBPM_CFG_INT_TRIGGER_VALUE | value for the trigger in use. The meaning of this field depends on the value of the trigger type. |
| TBPM_CFG_INT_BUNCH_TYPE_PROTON | proton bunch type (V:COALAP) |
| TBPM_CFG_INT_BUNCH_TYPE_PBAR | pbar bunch type (V:COALA) |
| TBPM_CFG_INT_MACHINE_STATE | current tevatron state (V:CLDRST) |
| TBPM_CFG_INT_HELIX_STATE | current helix state (V:HELIX) |
| TBPM_CFG_INT_PROTON_BUNCHES | proton bunches (V:PBKTC) |
| TBPM_CFG_INT_PBAR_BUNCHES | pbar bunches (V:ABKTC) |
| TBPM_CFG_INT_ECHOTEK_CONFIG | current echotek configuration |
| TBPM_CFG_INT_ECHOTEK_READ_TIMEOUT | timeout for an echotek read |
| TBPM_CFG_INT_DIAG_CHANNELA | diagnostic channel number A |
| TBPM_CFG_INT_DIAG_CHANNELB | diagnostic channel number B |
| TBPM_CFG_INT_DIAG_TRIGGER_TYPE | type of the trigger in use (idem) |
| TBPM_CFG_INT_DIAG_TRIGGER_VALUE | value for the trigger in use |
| TBPM_CFG_INT_DIAG_DATA_MODE | current operating mode (diagnostics) |
| TBPM_CFG_INT_DIAG_RAW_DATA_TYPE | type of data being generated |
| TBPM_CFG_INT_DATA_MODE | current operating mode |
| TBPM_CFG_INT_FAST_ABORT_PRIORITY | fast abort task priority |
| TBPM_CFG_INT_SLOW_ABORT_PRIORITY | slow abort task priority |
| TBPM_CFG_INT_PROFILE_PRIORITY | profile task priority |
| TBPM_CFG_INT_DISPLAY_PRIORITY | display task priority |
| TBPM_CFG_INT_TBT_PRIORITY | turn-by-turn task priority |
| TBPM_CFG_INT_TBT_PRIORITY_LOW | Low priority for turn-by-turn task, used when system is not in turn-by-turn mode |
| TBPM_CFG_INT_INJEC_TBT_PRIORITY | injection turn-by-turn task priority |
| TBPM_CFG_INT_INJ_TBT_PRIORITY_LOW | Low priority for injection turn-by-turn task. Used when system is not in injection mode |
| TBPM_CFG_INT_INJEC_CO_PRIORITY | injection closed orbit task priority |
| TBPM_CFG_INT_USER_TCLK_PRIORITY | user TCLK task priority |
| TBPM_CFG_INT_TBT_START_EVENT | turn-by-turn BSYNC start event |
| TBPM_CFG_INT_ECHOTEK_TRIGGER_COUNT | number of triggers for the echoteks |
| TBPM_CFG_INT_ECHOTEK_BURST_COUNT | number of points taken on each turn |
| TBPM_CFG_INT_DEFAULT_USER_TCLK | TCLK used to trigger the user buffer |
| TBPM_CFG_INT_PROFILE_CLEAR_TCLK | TCLK used to clear the profile buffer |
| TBPM_CFG_INT_DISPLAY_CLEAR_TCLK | TCLK used to clear the display buffer |
| TBPM_CFG_INT_SLOW_ABORT_SAMPLES | number of elements in the slow abort avrg |
| TBPM_CFG_INT_ACQSPEC_ARM_EVENT | acquisition specification arm event |
| TBPM_CFG_INT_ACQSPEC_TRIGGER_EVENT | acquisition specification trig. event |
| TBPM_CFG_INT_ACQSPEC_MODE | acquisition spec. mode (define time delays) |
| TBPM_CFG_INT_INJ_TBT_START_EVENT | BSYNC start event for the injection mode |
| TBPM_CFG_INT_INJ_TBT_TRIGGER_COUNT | number of events to be taken in inj.mod |
| TBPM_CFG_INT_TBT_ARM_EVENT | TCLK event used to arm a turn-by-turn |
| TBPM_CFG_INT_TEVBPM_STATE | Allow injection turn-by-turn (V:TEVBPM) |
| TBPM_CFG_INT_INJ_CO_SKIP | Number of injection tbt to be skip'd |
| TBPM_CFG_INT_INJ_CO_TURNS | Number of turns to average |
| TBPM_CFG_INT_CHECK_STATUS_TIME | Time int. to check BSYNC and TCLK signals |
| TBPM_CFG_INT_FLASH_FRAME_INDEX | Flash index in the injection tbt buffer |
| TBPM_CFG_INT_CLOSED_ORBIT_CONFIG | EchoTek setup file index for close orbit |
| TBPM_CFG_INT_TURN_BY_TURN_CONFIG | EchoTek setup file index for TBT |
| TBPM_CFG_INT_SAFE_MODE_CONFIG | EchoTek setup file index for SAFE mode |
| TBPM_CFG_INT_COUNT_CONFIG | EchoTek setup file index for couting test |
| TBPM_CFG_INT_DEBUG_CO_CONFIG | EchoTek setup file index for debug C.O. |
| TBPM_CFG_INT_RAW_CO_CONFIG | EchoTek setup file index for the raw mode |
| TBPM_CFG_INT_ZERO_FIFO | if 1 then zeros EchoTek FIFOs before TBT, if 0 then don't zero the FIFOs |
| TBPM_CFG_INT_SAFE_MODE_START_EVENT | safe mode BSYNC start event |
| TBPM_CFG_INT_SAFE_MODE_WINDOW | safe mode average window size |
| TBPM_CFG_INT_TBPMSF_STATE | Defines if system is in safe or regular inj. |
| TBPM_CFG_INT_POS_BCAST1 | 1st. BPM index whose position will be broadcast |
| TBPM_CFG_INT_POS_BCAST2 | 2nd. BPM index whose position will be broadcast |
| TBPM_CFG_INT_BCAST_RATE | Frequency for the position broadcast |

Table 4 – Integer configuration variables defined for TBPM

| Variable | Meaning |
| --- | --- |
| TBPM_CFG_FLT_PROTON_INTENSITY_THRESHOLD | Min acceptable p intensity |
| TBPM_CFG_FLT_PBAR_INTENSITY_THRESHOLD | Min acceptable pbar intensity |
| TBPM_CFG_FLT_LOW_INTENSITY_POSITION | Position to be reported if |
| Intensity is bellow min threshold |  |
| TBPM_CFG_FLT_BPM_SCALE_FACTOR | BPM scale factor (26mm or 72.6mm on F0) |
| TBPM_CFG_FLT_BPM_SAFE_MODE_VARIATION | variation on the averages |

Table 5 – Floating point configuration variables defined for TBPM

| Variable | true | false |
| --- | --- | --- |
| TBPM_CFG_BOOL_USE_TEST_SOURCE | use TestEchoTekPoo | use EchoTekPool |
| TBPM_CFG_BOOL_DIAGNOSTIC_MODE | In diagnostic mode | not in diag mode |
| TBPM_CFG_BOOL_CHECK_PHASE | check BPM0 phases | don't check phase |
| TBPM_CFG_BOOL_USE_CALIBRATION | use calib. from DB | no calib from DB |
| TBPM_CFG_BOOL_POS_BROADCAST | broadcasts BPM pos | no broadcast using UDP |

Table 2 – Boolean configuration variables defined for TBPM

### bpmShowGenerators

BPMHelp> bpmShowGenerators

----------------------------------------------------

bpmShowGenerators ()

Description:

Display status of the event generators

----------------------------------------------------

The front-end system has several of the so-called event generators. They are software components that generate events, where an event can be a TCLK received, a BSYNC received or a timing event. These events are broadcast to a certain number of listener tasks, triggering some specific computation.

The bpmShowGenerators displays the total number of events generated, which is a sum of the number of events broadcast when the generator was enabled, number of times events failed to be the broadcast and the number of events not broadcast because the generator was disabled.

The output below shows the status of the generators. The print out also shows whether the generator is enabled or not at that time.

tbpma0:tbpm> bpmShowGenerators

Generator       Enabled         Fail            Disabled        Total

C. Orbit  (Off) 901820524       0               8               901820532

FastAbort (On)  796688863       0               105131604       901820467

SlowAbort (On)  1593377         0               0               1593377

TurnXTurn (Off) 621             0               0               621

Inj. C.O. (On)  451             0               0               451

TCLK 0x47 (On)  24              0               0               24

TCLK 0x4B (On)  949             0               0               949

TCLK 0x4D (On)  1698            0               0               1698

TCLK 0x71 (On)  1425            0               0               1425

TCLK 0x75 (On)  2507            0               0               2507

TCLK 0x78 (On)  1242            0               611             1853

Arm TxT   (On)  170             0               0               170

User TCLK (On)  0               0               0               0

Check     (On)  607242          0               0               607242

### bpmShowModes

BPMHelp> bpmShowModes

----------------------------------------------------

bpmShowModes ()

Description:

Show the last N modes of operation of the system

----------------------------------------------------

This command shows the last 500 modes of operation of the system. Whenever the system enters a new mode of operation (e.g. when a turn-by-turn is requested) a new entry is added. Each entry contains shows the operating mode and the time when the mode switch completed.

tbpma0:tbpm> bpmShowModes

Mode History (elements = 500)

0) Mode CLOSED ORBIT - FRI JUL 01 08:49:49 2005

1) Mode ABORT - FRI JUL 01 08:50:08 2005

2) Mode INJECTION - FRI JUL 01 08:50:46 2005

3) Mode CLOSED ORBIT - FRI JUL 01 08:50:49 2005

4) Mode ABORT - FRI JUL 01 08:51:08 2005

5) Mode INJECTION - FRI JUL 01 08:51:46 2005

6) Mode CLOSED ORBIT - FRI JUL 01 08:51:49 2005

7) Mode ABORT - FRI JUL 01 08:52:08 2005

8) Mode INJECTION - FRI JUL 01 08:52:46 2005

9) Mode CLOSED ORBIT - FRI JUL 01 08:52:49 2005

10) Mode ABORT - FRI JUL 01 08:53:08 2005

…

491) Mode INJECTION - TUE JUL 05 04:29:59 2005

492) Mode CLOSED ORBIT - TUE JUL 05 04:30:02 2005

493) Mode ABORT - TUE JUL 05 04:30:45 2005

494) Mode INJECTION - TUE JUL 05 04:31:13 2005

495) Mode CLOSED ORBIT - TUE JUL 05 04:31:16 2005

496) Mode ABORT - TUE JUL 05 04:39:49 2005

497) Mode INJECTION - TUE JUL 05 04:40:28 2005

498) Mode CLOSED ORBIT - TUE JUL 05 04:40:31 2005

499) Mode ABORT - TUE JUL 05 04:56:54 2005

The output of the commands bpmShowModes, bpmShowStates, bpmShowTCLK and bpmShowConfig can be used to generate valuable information when the system is not responding correctly (e.g. a system is stuck in injection mode). The output of those commands should be saved for further analysis. The command output can be saved to a file by redirecting the output to a file, e.g. “bpmShowMode > /write1/A0_MODES”.

### bpmShowQueues

BPMHelp> bpmShowQueues

----------------------------------------------------

bpmShowQueues ()

Description:

Display status of event queues

----------------------------------------------------

All events generated in the system are sent to event queues. The bpmShowQueues allows the user to check if there is some event queue with pending events. Every line shows the queue name, the current number of messages followed by some VxWorks queue properties. The last column shows the tasks that are currently waiting for events to appear in the queue. The number of messages in the queue should be at most 1. A greater number indicates problem. The number of tasks blocked should also be 1 or 0 (as in the case of the ClosedOrbit queue below).

tbpma0:tbpm> bpmShowQueues

System Queues:

Msgs   T.Wait  S.Tout  R.Tout  Opts    MaxLen  MaxTask Blocked Tasks

ClosedOrbit    0      0       0       0       0       100     256     None

FastAbort      0      1       0       0       0       100     256     FastAbort

SlowAbort      0      1       0       0       0       100     256     SlowAbort

Profile        0      1       0       0       0       100     256     Profile

Display        0      1       0       0       0       100     256     Display

TurnByTurn     0      1       0       0       0       100     256     TurnByTurn

I.TurnByTurn   0      1       0       0       0       100     256     InjectionTurnByTurn

User TCLK      0      1       0       0       0       100     256     TBPMUserTCLK

Control        0      1       0       0       0       100     256     ControlTask

### bpmShowStates

BPMHelp> bpmShowStates

----------------------------------------------------

bpmShowStates ()

Description:

Display the state device change history

----------------------------------------------------

The bpmShowStates displays a history of the state changes recorded by the front-end. The number of state change history is set to 1000. Every line shows the device identifier and the new state value along with the time stamp when the change was received. The state id can be translated to a device name using the application page D80.

tbpma0:tbpm> bpmShowStates

State History (elements = 1000)

Last state change received on MON AUG 22 06:14:00 2005

0) Device: 146764 State: 1 - SUN AUG 14 08:18:30 2005

1) Device: 171151 State: 2 - SUN AUG 14 08:18:33 2005

2) Device: 146764 State: 8 - SUN AUG 14 12:09:21 2005

3) Device: 146764 State: 9 - SUN AUG 14 12:10:48 2005

4) Device: 146764 State: 10 - SUN AUG 14 12:12:23 2005

5) Device: 146764 State: 11 - SUN AUG 14 12:12:59 2005

6) Device: 171151 State: 4 - SUN AUG 14 12:13:25 2005

7) Device: 171151 State: 2 - SUN AUG 14 12:13:29 2005

8) Device: 171151 State: 4 - SUN AUG 14 12:14:18 2005

9) Device: 171151 State: 2 - SUN AUG 14 12:14:18 2005

10) Device: 146764 State: 17 - SUN AUG 14 12:35:19 2005

…

991) Device: 146764 State: 10 - MON AUG 22 05:57:30 2005

992) Device: 146764 State: 11 - MON AUG 22 05:58:09 2005

993) Device: 171151 State: 4 - MON AUG 22 05:58:48 2005

994) Device: 171151 State: 2 - MON AUG 22 05:58:51 2005

995) Device: 171151 State: 4 - MON AUG 22 05:59:40 2005

996) Device: 171151 State: 2 - MON AUG 22 05:59:41 2005

997) Device: 146764 State: 12 - MON AUG 22 06:00:51 2005

998) Device: 146764 State: 13 - MON AUG 22 06:01:34 2005

999) Device: 146764 State: 14 - MON AUG 22 06:14:05 2005

### bpmShowTasks

BPMHelp> bpmShowTasks

----------------------------------------------------

bpmShowTasks ()

Description:

Display status of the data acquisition tasks

----------------------------------------------------

Command used to get current readout information from the data acquisition tasks. For every task there is information regarding the number of events read out, number of failed read out events and number of times the read out was disabled.

tbpma0:tbpm> bpmShowTasks

Readout

Task                    Counter Failed  Disabled

ClosedOrbit             116062  0       0

FastAbort               98766   0       0

SlowAbort               0       0       0

Profile                 2726    1225    0

Display                 1636    0       0

TurnByTurn              0       0       0

InjectionTurnByTurn     0       0       0

TBPMUserTCLK            0       0       0

A failed read out event can result from a destination buffer being full or the source buffer had no data available. It is also possible to have failed read out events in case the system is not in the correct mode of operation, for example if a profile frame is requested while the system is in turn-by-turn or abort mode.

### bpmShowTCLK

BPMHelp> bpmShowTCLK

----------------------------------------------------

bpmShowTCLK ()

Description:

Display the TCLK history

----------------------------------------------------

The bpmShowTCLK command shows a history of the last 500 TCLKs received by the front-end. Along with the TCLK received there are three timestamps. The first one, preceded by (T) is the timing board TCLK timestamp, which records the timestamp at the last TCLK 0x4B. The second timestamp (B) is also from the timing boards, however it is the timestamp of the last BYNC 0x7C (last injection). Finally a time of the day timestamp at the time the TCLK was received is displayed.

tbpma0:tbpm> bpmShowTCLK

TCLK History (elements = 500)

Last TCLK received on TUE JUL 05 05:53:21 2005

0) TCLK 0x75 - (T) 0xa967c48c553 - (B) 0xaf6197f7 - SUN JUL 03 23:51:21 2005

1) TCLK 0x75 - (T) 0xa967c48c553 - (B) 0xaf6197f7 - SUN JUL 03 23:51:27 2005

2) TCLK 0x75 - (T) 0xa967c48c553 - (B) 0xaf6197f7 - SUN JUL 03 23:51:33 2005

3) TCLK 0x75 - (T) 0xa967c48c553 - (B) 0xaf6197f7 - SUN JUL 03 23:51:41 2005

4) TCLK 0x4b - (T) 0xa9becbfed61 - (B) 0xaf6197f7 - SUN JUL 03 23:53:15 2005

5) TCLK 0xc1 - (T) 0xa9becbfed61 - (B) 0xaf6197f7 - SUN JUL 03 23:53:45 2005

6) TCLK 0x75 - (T) 0xa9becbfed61 - (B) 0xaf6197f7 - SUN JUL 03 23:53:56 2005

7) TCLK 0x75 - (T) 0xa9becbfed61 - (B) 0xaf6197f7 - SUN JUL 03 23:54:18 2005

8) TCLK 0x75 - (T) 0xa9becbfed61 - (B) 0xaf6197f7 - SUN JUL 03 23:54:32 2005

9) TCLK 0x75 - (T) 0xa9becbfed61 - (B) 0xaf6197f7 - SUN JUL 03 23:54:41 2005

10) TCLK 0x75 - (T) 0xa9becbfed61 - (B) 0xaf6197f7 - SUN JUL 03 23:54:48 2005

…

491) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:51:52 2005

492) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:51:57 2005

493) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:52:02 2005

494) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:52:07 2005

495) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:52:12 2005

496) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:52:17 2005

497) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:52:22 2005

498) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:52:27 2005

499) TCLK 0x75 - (T) 0x29a10d691c - (B) 0x75d0f0e7 - TUE JUL 05 05:53:21 2005

### bpmPeekDiag

BPMHelp> bpmPeekDiag

----------------------------------------------------

bpmPeekDiag ()

Description:

Display current contents of the diagnostic buffer

----------------------------------------------------

The command bpmPeekDiag displays the first elements of the diagnostics buffer. That buffer is used only when the front-end is in diagnostics mode (using the bpmMode 30 command or using the page W25).

### bpmTBTEvent

BPMHelp> bpmTBTEvent

----------------------------------------------------

bpmTBTEvent (tclk)

Description:

Change the TCLK event that arms a turn-by-turn measurement

Parameters:

tclk: TCLK that will arm the turn-by-turn

----------------------------------------------------

This command is for development and debugging only. It changes the TCLK that arms turn-by-turn measurements.

There is an equivalent ACNET variable for changing the TCLK event, the device is T:xxTTEV, where xx is the house name (e.g. A0).

The current TCLK for arming turn-by-turn can be viewed with the bpmShowConfig command. The configuration variable is called TBT_ARM_EVENT and has index 63.

### bpmTCLK

BPMHelp> bpmTCLK

----------------------------------------------------

bpmTCLK (tclk)

Description:

Generate a TCLK event that is processed by the system

Parameters:

tclk:

0x47: ABORT

0x4D: Tevatron reset - proton injection

0x71: Prepare for beam

0x75: BPM profile

0x77: Arm turn-by-turn measurement

0x78: BPM display

0x100: User TCLK generation

----------------------------------------------------

This is a development and debugging command. Should not be using during normal operations. This command creates a fake TCLK. For example, the command bpmTCLK 0x47 will make the system enter the ABORT mode.

## Trace Diagnostics

The Tevatron BPM software packages are using a trace facility to monitor software behavior. This document is not meant to be a tutorial for that facility - Refer to the output of the traceHelp command (sample below) for an overview of the trace commands that are available.

fccts1:tbpm-dev> traceHelp

Trace Facility Help

traceMode(mode)          Sets the target(s) of the trace messages.

'mode' can be:

0 = tracing is disabled

1 = trace into circular buffer

2 = trace to VxWorks log facility

3 = trace to both

traceModeGet()           Returns the current trace mode.

traceInfo()              Shows information associated with the

trace facility. Each trace source is

also shown along with its level mask.

traceShow(opts, lines, skip, fd)

Dumps the contents of the trace buffer.

The arguments have the following effects:

'opts' is a bit mask:

bits 0,1:

0 = Relative timestamps are shown

1 = Absolute, but zeroed, timestamps

2 = Absolute timestamps

bit 2:

0 = do not show trace level

1 = show trace level

'lines' can be:

0 = Display all entries (default)

Otherwise only display the first

'lines' entries

'skip' can be:

0 = Don't skip entries

Otherwise display every 'skip'

entry

'fd' can be an open file descriptor. If

it is zero, then standard output is used.

traceReset()             Clears the circular trace buffer.

traceOn(id, lo, hi, f)      Turns on the specified levels of trace

source 'id'. This value can be found

using traceInfo(). 'lo' and 'hi' define

the range of levels to enable (0 - 31).

f is the "function" (currently -

0=circular, 1=logMsg.

traceOff(id, lo, hi, f)     Turns off the specified levels of trace

source 'id'. 'lo' and 'hi' define

the range of levels to disable (0 - 31).

f is same as above.

traceGlobalOn(lo, hi, f)    Like traceOn(), but it affects every

trace source.

f is same as above.

traceGlobalOff(lo, hi, f)   Like traceOff(), but it affects every

trace source.

f is same as above.

traceFreezeOn(lo, hi)    Enables a range of "freeze" levels. If

your code calls traceFreeze(lvl) and the

lvl'th freeze bit was set, the circular

trace queue is frozen (similar to calling

traceMode(0).) traceInfo() shows the

current freeze mask.

traceFreezeOff(lo, hi)   Disables a range of "freeze" levels.

As a quick overview, we typically use the tracing facility in a circular buffer mode where all traced processes write into that buffer. The software is exploiting many levels of trace that can be turned on/off to fine tune which information is stored in the buffer.

As an example, the following use of the traceShow command would display (on standard output) the most recent 100 entries in the trace buffer without skipping any entries, and each entry would be shown with an absolute timestamp and its trace level.

traceShow 6, 100, 0, 0

### Trace Levels

The GBPM library defines in the file Defs.h the trace levels used for the different parts of the system. The following table defines the levels used throughout the code.

| Level | Start | End |
| --- | --- | --- |
| ERROR_LEVEL | 0 | 0 |
| DRIVER_LEVEL | 1 | 8 |
| EVENT_LEVEL | 9 | 11 |
| READOUT_LEVEL | 12 | 15 |
| BUFFER_LEVEL | 16 | 17 |
| CONTROL_LEVEL | 18 | 18 |
| ACNET_LEVEL | 19 | 20 |
| ALARM_LEVEL | 21 | 21 |
| TIMING_LEVEL | 22 | 23 |

## VME Backplane Diagnostics

Bus analyzers are a powerful tool in understanding what is actually happening on the backplane. Using a Vanguard VME bus analyzer and the companion Bus Analyzer software version 4 the following traces where obtained to show VME timing of typical transfers:

| AbsTime | Transfer | AM/XAM | Address | Data | Size | Cycle | Status | Iack | IRQ[7:1]* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Timing board interrupt (500 Hz rate) |
| 0.0ns | Single | A16nD | IACK=6 | ......A0 | LBYTE | Rd | Data | IACK6 | 1011111 |
| Echotek interrupt – First channel of first board is done |
| 1.358ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |
| Interrupt handler checks the status of all channels |
| 1.362ms | Single | A16nD | 8314 | FF000000 | D32 | Rd | Data | ----- | 111111 |
| 1.363ms | Single | A16nD | 8314 | 1000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.367ms | Single | A16nD | 8314 | FE000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.368ms | Single | A16nD | 8314 | FE000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.369ms | Single | A16nD | 9314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.370ms | Single | A16nD | 9314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.370ms | Single | A16nD | A314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.371ms | Single | A16nD | A314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.372ms | Single | A16nD | B314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.373ms | Single | A16nD | B314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.373ms | Single | A16nD | C314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.374ms | Single | A16nD | C314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.375ms | Single | A16nD | D314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.376ms | Single | A16nD | D314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.377ms | Single | A32nD | 18000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.378ms | Single | A32nD | 18000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.379ms | Single | A32nD | 19000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.380ms | Single | A32nD | 19000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.381ms | Single | A32nD | 1A000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.382ms | Single | A32nD | 1A000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.383ms | Single | A32nD | 1B000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.384ms | Single | A32nD | 1B000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.385ms | Single | A32nD | 1C000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.386ms | Single | A32nD | 1C000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.387ms | Single | A32nD | 1D000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.388ms | Single | A32nD | 1D000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| Board 0 – data read out (8 single transfers) |
| 1.389ms | Single | A32nD | 18100000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.391ms | Single | A32nD | 18180000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.392ms | Single | A32nD | 18200000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.394ms | Single | A32nD | 18280000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.396ms | Single | A32nD | 18300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.397ms | Single | A32nD | 18380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.399ms | Single | A32nD | 18400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.400ms | Single | A32nD | 18480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| Board 1 – data read out (8 single transfers) |
| 1.402ms | Single | A32nD | 19100000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.404ms | Single | A32nD | 19180000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.406ms | Single | A32nD | 19200000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.407ms | Single | A32nD | 19280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.409ms | Single | A32nD | 19300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.410ms | Single | A32nD | 19380000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.412ms | Single | A32nD | 19400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.414ms | Single | A32nD | 19480000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| Board 2 – data read out (8 single transfers) |
| 1.415ms | Single | A32nD | 1A100000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.417ms | Single | A32nD | 1A180000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.419ms | Single | A32nD | 1A200000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.420ms | Single | A32nD | 1A280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.422ms | Single | A32nD | 1A300000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.423ms | Single | A32nD | 1A380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.425ms | Single | A32nD | 1A400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.426ms | Single | A32nD | 1A480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| Board 3 – data read out (8 single transfers) |
| 1.428ms | Single | A32nD | 1B100000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.430ms | Single | A32nD | 1B180000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.432ms | Single | A32nD | 1B200000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.433ms | Single | A32nD | 1B280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.435ms | Single | A32nD | 1B300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.436ms | Single | A32nD | 1B380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.438ms | Single | A32nD | 1B400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.440ms | Single | A32nD | 1B480000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| Board 4 – data read out (8 single transfers) |
| 1.441ms | Single | A32nD | 1C100000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.443ms | Single | A32nD | 1C180000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.445ms | Single | A32nD | 1C200000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.446ms | Single | A32nD | 1C280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.448ms | Single | A32nD | 1C300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.449ms | Single | A32nD | 1C380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.451ms | Single | A32nD | 1C400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.452ms | Single | A32nD | 1C480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| Board 5 – data read out (8 single transfers) |
| 1.454ms | Single | A32nD | 1D100000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.456ms | Single | A32nD | 1D180000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.458ms | Single | A32nD | 1D200000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.459ms | Single | A32nD | 1D280000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.461ms | Single | A32nD | 1D300000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.462ms | Single | A32nD | 1D380000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.464ms | Single | A32nD | 1D400000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.466ms | Single | A32nD | 1D480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| Reading timing boad registers (timestamp and turns count) |
| 1.469ms | Single | A16nD | 203A | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.471ms | Single | A16nD | 203C | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.472ms | Single | A16nD | 203E | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.473ms | Single | A16nD | 2040 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.475ms | Single | A16nD | 2054 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.476ms | Single | A16nD | 2052 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| Board 0 arming (38 ms – Total of 35 VME read and write operations, first and last shown only) |
| 1.525ms | Single | A32nD | 18010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.563ms | Single | A32nD | 18000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| Board 1 arming (38 us) |
| 1.564ms | Single | A32nD | 19010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.602ms | Single | A32nD | 19000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| Board 2 arming (37 us) |
| 1.603ms | Single | A32nD | 1A010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.640ms | Single | A32nD | 1A000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| Board 3 arming (38 us) |
| 1.641ms | Single | A32nD | 1B010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.679ms | Single | A32nD | 1B000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| Board 4 arming (37 us) |
| 1.680ms | Single | A32nD | 1C010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.717ms | Single | A32nD | 1C000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| Board 5 arming (38 us) |
| 1.718ms | Single | A32nD | 1D010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.756ms | Single | A32nD | 1D000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| Waiting for next timing board interrupt… |
| 2.012ms | Single | A16nD | IACK=6 | ......A0 | LBYTE | Rd | Data | IACK6 | 1011111 |
| 3.370ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |

| AbsTime | Transfer | AM/XAM | Address | Data | Size | Cycle | Status | Iack | IRQ[7:1]* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Timing board interrupt – BSYNC 0x7C or 0xDA received |
| 0.0ns | Single | A16nD | IACK=6 | ......A1 | LBYTE | Rd | Data | IACK6 | 1111111 |
| Echotek interrupt – First channel of first board is done. 8192 turns sampled |
| 171.817ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |
| Interrupt handler checks the status of all channels |
| 171.822ms | Single | A16nD | 8314 | FF000000 | D32 | Rd | Data | ----- | 111111 |
| 171.824ms | Single | A16nD | 8314 | 1000000 | D32 | Wr | Data | ----- | 1111111 |
| 171.833ms | Single | A16nD | 8314 | FE000000 | D32 | Rd | Data | ----- | 1111111 |
| 171.834ms | Single | A16nD | 8314 | FE000000 | D32 | Wr | Data | ----- | 1111111 |
| 171.835ms | Single | A16nD | 9314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 171.835ms | Single | A16nD | 9314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 171.836ms | Single | A16nD | A314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 171.837ms | Single | A16nD | A314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 171.838ms | Single | A16nD | B314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 171.838ms | Single | A16nD | B314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 171.839ms | Single | A16nD | C314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 171.840ms | Single | A16nD | C314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 171.841ms | Single | A16nD | D314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 171.842ms | Single | A16nD | D314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 171.844ms | Single | A32nD | 18000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 171.845ms | Single | A32nD | 18000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 171.846ms | Single | A32nD | 19000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 171.847ms | Single | A32nD | 19000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 171.848ms | Single | A32nD | 1A000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 171.850ms | Single | A32nD | 1A000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 171.851ms | Single | A32nD | 1B000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 171.852ms | Single | A32nD | 1B000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 171.853ms | Single | A32nD | 1C000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 171.854ms | Single | A32nD | 1C000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 171.856ms | Single | A32nD | 1D000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 171.857ms | Single | A32nD | 1D000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 171.859ms | Single | A32nD | 18000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 171.859ms | Single | A32nD | 18000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 171.860ms | Single | A16nD | 8220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 171.860ms | Single | A16nD | 8218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 171.861ms | Single | A16nD | 8204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 171.861ms | Single | A16nD | 8220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 171.864ms | Start | A32sMBLT | 25079800 FFF | E000100000001 | D64 | Wr | Data | ----- | 1111111 |
| 32702 VME operations omitted |
| 176.859ms | Start | A32sMBLT | 24980800 FFF | F0001FFFD0005 | D64 | Wr | Data | ----- | 1111111 |
| DMA ready interrupt for board 0 |
| 176.870ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |
| 176.874ms | Single | A16nD | 8314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 176.875ms | Single | A16nD | 8314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 176.970ms | Single | A32nD | 19000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 176.971ms | Single | A32nD | 19000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 176.971ms | Single | A16nD | 9220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 176.972ms | Single | A16nD | 9218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 176.972ms | Single | A16nD | 9204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 176.972ms | Single | A16nD | 9220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 176.976ms | Start | A32sMBLT | 24878800 000 | 0FFFF00010000 | D64 | Wr | Data | ----- | 1111111 |
| 181.963ms | Start | A32sMBLT | 2417F800 FFF | F000000010002 | D64 | Wr | Data | ----- | 1111111 |
| DMA ready interrupt for board 1 |
| 181.974ms | Single | A16nD | IACK=7 | ......E3 | LBYTE | Rd | Data | IACK7 | 111111 |
| 181.978ms | Single | A16nD | 9314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 181.979ms | Single | A16nD | 9314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 182.068ms | Single | A32nD | 1A000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 182.069ms | Single | A32nD | 1A000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 182.069ms | Single | A16nD | A220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 182.069ms | Single | A16nD | A218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 182.070ms | Single | A16nD | A204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 182.070ms | Single | A16nD | A220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 182.074ms | Start | A32sMBLT | 24077800 FFF | F000100000004 | D64 | Wr | Data | ----- | 1111111 |
| 32704 VME operations omitted |
| 187.064ms | Start | A32sMBLT | 2397E800 FFF | E0003FFFF0003 | D64 | Wr | Data | ----- | 1111111 |
| DMA ready interrupt for board 2 |
| 187.075ms | Single | A16nD | IACK=7 | ......E5 | LBYTE | Rd | Data | IACK7 | 111111 |
| 187.079ms | Single | A16nD | A314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 187.080ms | Single | A16nD | A314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 187.168ms | Single | A32nD | 1B000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 187.169ms | Single | A32nD | 1B000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 187.169ms | Single | A16nD | B220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 187.170ms | Single | A16nD | B218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 187.170ms | Single | A16nD | B204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 187.171ms | Single | A16nD | B220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 187.174ms | Start | A32sMBLT | 23876800 000 | 10001 | D64 | Wr | Data | ----- | 1111111 |
| 32704 VME operations omitted |
| 192.162ms | Start | A32sMBLT | 2317D800 000 | 00001FFFF0001 | D64 | Wr | Data | ----- | 1111111 |
| DMA ready interrupt for board 3 |
| 192.173ms | Single | A16nD | IACK=7 | ......E7 | LBYTE | Rd | Data | IACK7 | 111111 |
| 192.177ms | Single | A16nD | B314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 192.178ms | Single | A16nD | B314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 192.267ms | Single | A32nD | 1C000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 192.268ms | Single | A32nD | 1C000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 192.268ms | Single | A16nD | C220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 192.269ms | Single | A16nD | C218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 192.269ms | Single | A16nD | C204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 192.270ms | Single | A16nD | C220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 192.273ms | Start | A32sMBLT | 23075800 000 | 1FFFFFFFE0001 | D64 | Wr | Data | ----- | 1111111 |
| 32704 VME operations omitted |
| 197.349ms | Start | A32sMBLT | 2297C800 FFF | D0002FFFF0003 | D64 | Wr | Data | ----- | 1111111 |
| DMA ready interrupt for board 4 |
| 197.362ms | Single | A16nD | IACK=7 | ......E9 | LBYTE | Rd | Data | IACK7 | 111111 |
| 197.365ms | Single | A16nD | C314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 197.366ms | Single | A16nD | C314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 197.470ms | Single | A32nD | 1D000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 197.470ms | Single | A32nD | 1D000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 197.471ms | Single | A16nD | D220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 197.471ms | Single | A16nD | D218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 197.472ms | Single | A16nD | D204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 197.472ms | Single | A16nD | D220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 197.476ms | Start | A32sMBLT | 22874800 000 | 0FFFD00000000 | D64 | Wr | Data | ----- | 1111111 |
| 32704 VME operations omitted |
| 202.650ms | Start | A32sMBLT | 2217B800 000 | 0FFFE0002FFFE | D64 | Wr | Data | ----- | 1111111 |
| DMA ready interrupt for board 5 |
| 202.663ms | Single | A16nD | IACK=7 | ......EB | LBYTE | Rd | Data | IACK7 | 111111 |
| 202.667ms | Single | A16nD | D314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 202.668ms | Single | A16nD | D314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| Timing information from timing board |
| 202.762ms | Single | A16nD | 203A | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.763ms | Single | A16nD | 203C | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.765ms | Single | A16nD | 203E | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.766ms | Single | A16nD | 2040 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.769ms | Single | A16nD | 2044 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.771ms | Single | A16nD | 2042 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.773ms | Single | A16nD | 2048 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.774ms | Single | A16nD | 2046 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| Configure timing board to start taking closed orbits |
| 202.818ms | Single | A16nD | 2030 | ....1603 | WORD | Rd | Data | ----- | 1111111 |
| 202.819ms | Single | A16nD | 2030 | ....1000 | WORD | Wr | Data | ----- | 1111111 |
| 202.820ms | Single | A16nD | 2030 | ....1000 | WORD | Rd | Data | ----- | 1111111 |
| 202.821ms | Single | A16nD | 2030 | ....1040 | WORD | Wr | Data | ----- | 1111111 |
| 202.822ms | Single | A16nD | 2060 | ....09A1 | WORD | Rd | Data | ----- | 1111111 |
| 202.823ms | Single | A16nD | 2060 | ....09A1 | WORD | Wr | Data | ----- | 1111111 |
| 202.826ms | Single | A16nD | 2066 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 202.829ms | Single | A16nD | 2034 | ....00AA | WORD | Wr | Data | ----- | 1111111 |
| 202.830ms | Single | A16nD | 2036 | ....0010 | WORD | Wr | Data | ----- | 1111111 |
| 202.830ms | Single | A16nD | 2010 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.831ms | Single | A16nD | 2012 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.832ms | Single | A16nD | 2014 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.833ms | Single | A16nD | 2016 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.834ms | Single | A16nD | 2018 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.835ms | Single | A16nD | 201A | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.835ms | Single | A16nD | 201C | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.836ms | Single | A16nD | 201E | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 202.837ms | Single | A16nD | 2030 | ....0040 | WORD | Wr | Data | ----- | 1111111 |
| 202.838ms | Single | A16nD | 2026 | ....005F | WORD | Wr | Data | ----- | 1111111 |
| 202.839ms | Single | A16nD | 2030 | ....0040 | WORD | Rd | Data | ----- | 1111111 |
| 202.840ms | Single | A16nD | 2030 | ....00C0 | WORD | Wr | Data | ----- | 1111111 |
| 202.843ms | Single | A16nD | 2060 | ....01A0 | WORD | Wr | Data | ----- | 1111111 |
| 202.844ms | Single | A16nD | 2070 | ....0009 | WORD | Wr | Data | ----- | 1111111 |
| Load closed orbit configuration – board 0 (7216 VME transfers – 10 ms) |
| 205.776ms | Single | A32nD | 18000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| Load closed orbit configuration – board 1 (7216 VME transfers – 10 ms) |
| 215.294ms | Single | A32nD | 19000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| Load closed orbit configuration – board 2 (7216 VME transfers – 10 ms) |
| 224.810ms | Single | A32nD | 1A000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| Load closed orbit configuration – board 3 (7216 VME transfers – 10 ms) |
| 234.311ms | Single | A32nD | 1B000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| Load closed orbit configuration – board 4 (7216 VME transfers – 10 ms) |
| 243.808ms | Single | A32nD | 1C000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| Load closed orbit configuration – board 5 (7216 VME transfers – 10 ms) |
| 253.653ms | Single | A32nD | 1D000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| Board 0 arming (36 us) |
| 263.317ms | Single | A16nD | 8310 | 1010000 | D32 | Rd | Data | ----- | 1111111 |
| Board 1 arming (29 us) |
| 263.353ms | Single | A16nD | 9310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| Board 2 arming (28 us) |
| 263.382ms | Single | A16nD | A310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| Board 3 arming (29 us) |
| 263.410ms | Single | A16nD | B310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| Board 4 arming (28 us) |
| 263.439ms | Single | A16nD | C310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| Board 5 arming (30 us) |
| 263.467ms | Single | A16nD | D310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 263.497ms | Single | A32nD | 18000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 263.497ms | Single | A32nD | 19000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 263.498ms | Single | A32nD | 1A000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 263.499ms | Single | A32nD | 1B000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 263.499ms | Single | A32nD | 1C000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 263.500ms | Single | A32nD | 1D000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 263.501ms | Single | A32nD | 18000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 263.528ms | Single | A32nD | 19000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 263.553ms | Single | A32nD | 1A000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 263.577ms | Single | A32nD | 1B000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 263.601ms | Single | A32nD | 1C000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 263.626ms | Single | A32nD | 1D000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 263.658ms | Single | A32nD | 18010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 263.699ms | Single | A32nD | 19010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 263.737ms | Single | A32nD | 1A010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 263.776ms | Single | A32nD | 1B010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 263.814ms | Single | A32nD | 1C010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 263.853ms | Single | A32nD | 1D010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 263.905ms | Single | A16nD | 2060 | ....01A0 | WORD | Rd | Data | ----- | 1111111 |
| 263.906ms | Single | A16nD | 2060 | ....11A0 | WORD | Wr | Data | ----- | 1111111 |
| 263.916ms | Single | A16nD | 2030 | ....00C0 | WORD | Rd | Data | ----- | 1111111 |
| 263.917ms | Single | A16nD | 2030 | ....02C0 | WORD | Wr | Data | ----- | 1111111 |
| 263.918ms | Single | A16nD | 2062 | ....10C6 | WORD | Rd | Data | ----- | 1111111 |
| 263.919ms | Single | A16nD | 2062 | ....10C6 | WORD | Wr | Data | ----- | 1111111 |
| 263.921ms | Single | A16nD | 2030 | ....02C0 | WORD | Rd | Data | ----- | 1111111 |
| 263.922ms | Single | A16nD | 2030 | ....02C0 | WORD | Wr | Data | ----- | 1111111 |
| 263.923ms | Single | A16nD | 2062 | ....10C6 | WORD | Rd | Data | ----- | 1111111 |
| 263.924ms | Single | A16nD | 2062 | ....10C6 | WORD | Wr | Data | ----- | 1111111 |
| 263.926ms | Single | A16nD | 2030 | ....02C0 | WORD | Rd | Data | ----- | 1111111 |
| 263.928ms | Single | A16nD | 2030 | ....02C0 | WORD | Wr | Data | ----- | 1111111 |
| 263.929ms | Single | A16nD | 2062 | ....10C6 | WORD | Rd | Data | ----- | 1111111 |
| 263.930ms | Single | A16nD | 2062 | ....10C6 | WORD | Wr | Data | ----- | 1111111 |
| 263.931ms | Single | A16nD | 2030 | ....02C0 | WORD | Rd | Data | ----- | 1111111 |
| 263.932ms | Single | A16nD | 2030 | ....0280 | WORD | Wr | Data | ----- | 1111111 |
| 263.933ms | Single | A16nD | 2030 | ....0280 | WORD | Rd | Data | ----- | 1111111 |
| 263.934ms | Single | A16nD | 2030 | ....0683 | WORD | Wr | Data | ----- | 1111111 |
| Waiting for next closed orbit trigger |
| 265.294ms | Single | A16nD | IACK=6 | ......A0 | LBYTE | Rd | Data | IACK6 | 1011111 |
| 266.653ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |

## Looking at ACNET variables

From an ACNET console page, select the “ACL Edit/Run” option from the Pgm_Tools menu which is located near the top right corner of the page. In the Action section of the ACL Edit Window, type ‘read <variableName>’ and type <ctrl>-r to run the command. When the command is run, the ACNET window will split into two parts, the command source (which you typed) and the output. As an example, ‘read V:PING’ followed by <ctrl-r> should return a result like “V:PING =  5    ping” in the output pane.

Setting ACNET variables uses the same ACL Edit/Run application, but first you need to configure your ACNET console to allow variables to be set.  This is done from the Utilities window. Click on the Setting option in the Utilities window and set the value to one hour. Back on the ACL Edit/Run page, you can now set variable values using commands of the form ‘set <variableName>=<value>’.  For example, to set the value of V:PING, you could use a command like ‘set V:PING=5’ (followed by <ctrl>-r).

# Appendix: Node name/ACNET addresses

| node name | ip address | ACNET address | Location |
| --- | --- | --- | --- |
| FCCTS0 | 131.225.126.243 | 0x0BD3 | FCC3 |
| TBPMA0 | 131.225.127.116 | 0x0C28 | A0 |
| TBPMA1 | 131.225.127.117 | 0x0C29 | A1 |
| TBPMA2 | 131.225.127.118 | 0x0C2A | A2 |
| TBPMA3 | 131.225.127.233 | 0x0C2B | A3 |
| TBPMA4 | 131.225.127.119 | 0x0C2C | A4 |
| TBPMB0 | 131.225.127.115 | 0x0C2D | B0 |
| TBPMB1 | 131.225.127.120 | 0x0C2E | B1 |
| TBPMB2 | 131.225.127.121 | 0x0C2F | B2 |
| TBPMB3 | 131.225.127.128 | 0x0C30 | B3 |
| TBPMB4 | 131.225.127.122 | 0x0C31 | B4 |
| TBPMC1 | 131.225.127.123 | 0x0C32 | C1 |
| TBPMC2 | 131.225.127.124 | 0x0C33 | C2 |
| TBPMC3 | 131.225.127.130 | 0x0C34 | C3 |
| TBPMC4 | 131.225.127.131 | 0x0C35 | C4 |
| TBPMD0 | 131.225.128.207 | 0x0C36 | D0 |
| TBPMD1 | 131.225.128.172 | 0x0C37 | D1 |
| TBPMD2 | 131.225.128.173 | 0x0C38 | D2 |
| TBPMD3 | 131.225.128.174 | 0x0C39 | D3 |
| TBPMD4 | 131.225.128.176 | 0x0C3A | D4 |
| TBPME1 | 131.225.128.193 | 0x0C3B | E1 |
| TBPME2 | 131.225.128.194 | 0x0C3C | E2 |
| TBPME3 | 131.225.128.195 | 0x0C3D | E3 |
| TBPME4 | 131.225.128.196 | 0x0C3E | E4 |
| TBPMF1 | 131.225.128.197 | 0x0C3F | F1 |
| TBPMF2 | 131.225.128.198 | 0x0C40 | F2 |
| TBPMF3 | 131.225.128.199 | 0x0C41 | F3 |
| TBPMF4 | 131.225.128.205 | 0x0C42 | F4 |

# Appendix: Full VME trace

| AbsTime | Transfer | AM/XAM | Address | Data | Size | Cycle | Status | Iack | IRQ[7:1]* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.0ns | Single | A16nD | IACK=6 | ......A0 | LBYTE | Rd | Data | IACK6 | 1011111 |
| 1.358ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |
| 1.362ms | Single | A16nD | 8314 | FF000000 | D32 | Rd | Data | ----- | 111111 |
| 1.363ms | Single | A16nD | 8314 | 1000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.367ms | Single | A16nD | 8314 | FE000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.368ms | Single | A16nD | 8314 | FE000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.369ms | Single | A16nD | 9314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.370ms | Single | A16nD | 9314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.370ms | Single | A16nD | A314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.371ms | Single | A16nD | A314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.372ms | Single | A16nD | B314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.373ms | Single | A16nD | B314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.373ms | Single | A16nD | C314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.374ms | Single | A16nD | C314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.375ms | Single | A16nD | D314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 1.376ms | Single | A16nD | D314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 1.377ms | Single | A32nD | 18000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.378ms | Single | A32nD | 18000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.379ms | Single | A32nD | 19000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.380ms | Single | A32nD | 19000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.381ms | Single | A32nD | 1A000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.382ms | Single | A32nD | 1A000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.383ms | Single | A32nD | 1B000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.384ms | Single | A32nD | 1B000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.385ms | Single | A32nD | 1C000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.386ms | Single | A32nD | 1C000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.387ms | Single | A32nD | 1D000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 1.388ms | Single | A32nD | 1D000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 1.389ms | Single | A32nD | 18100000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.391ms | Single | A32nD | 18180000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.392ms | Single | A32nD | 18200000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.394ms | Single | A32nD | 18280000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.396ms | Single | A32nD | 18300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.397ms | Single | A32nD | 18380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.399ms | Single | A32nD | 18400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.400ms | Single | A32nD | 18480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.402ms | Single | A32nD | 19100000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.404ms | Single | A32nD | 19180000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.406ms | Single | A32nD | 19200000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.407ms | Single | A32nD | 19280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.409ms | Single | A32nD | 19300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.410ms | Single | A32nD | 19380000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.412ms | Single | A32nD | 19400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.414ms | Single | A32nD | 19480000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.415ms | Single | A32nD | 1A100000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.417ms | Single | A32nD | 1A180000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.419ms | Single | A32nD | 1A200000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.420ms | Single | A32nD | 1A280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.422ms | Single | A32nD | 1A300000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.423ms | Single | A32nD | 1A380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.425ms | Single | A32nD | 1A400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.426ms | Single | A32nD | 1A480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.428ms | Single | A32nD | 1B100000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.430ms | Single | A32nD | 1B180000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.432ms | Single | A32nD | 1B200000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.433ms | Single | A32nD | 1B280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.435ms | Single | A32nD | 1B300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.436ms | Single | A32nD | 1B380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.438ms | Single | A32nD | 1B400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.440ms | Single | A32nD | 1B480000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.441ms | Single | A32nD | 1C100000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.443ms | Single | A32nD | 1C180000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.445ms | Single | A32nD | 1C200000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.446ms | Single | A32nD | 1C280000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.448ms | Single | A32nD | 1C300000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.449ms | Single | A32nD | 1C380000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.451ms | Single | A32nD | 1C400000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.452ms | Single | A32nD | 1C480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.454ms | Single | A32nD | 1D100000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.456ms | Single | A32nD | 1D180000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.458ms | Single | A32nD | 1D200000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.459ms | Single | A32nD | 1D280000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.461ms | Single | A32nD | 1D300000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.462ms | Single | A32nD | 1D380000 | 1 | D32 | Rd | Data | ----- | 1111111 |
| 1.464ms | Single | A32nD | 1D400000 | 0000FFFF | D32 | Rd | Data | ----- | 1111111 |
| 1.466ms | Single | A32nD | 1D480000 | 0 | D32 | Rd | Data | ----- | 1111111 |
| 1.469ms | Single | A16nD | 203A | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.471ms | Single | A16nD | 203C | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.472ms | Single | A16nD | 203E | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.473ms | Single | A16nD | 2040 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.475ms | Single | A16nD | 2054 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.476ms | Single | A16nD | 2052 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 1.525ms | Single | A32nD | 18010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.526ms | Single | A32nD | 18010010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.528ms | Single | A32nD | 18011440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.529ms | Single | A32nD | 18011440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.530ms | Single | A32nD | 18011C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.532ms | Single | A32nD | 18011C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.533ms | Single | A32nD | 18010000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.534ms | Single | A32nD | 18010010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.534ms | Single | A32nD | 18020000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.535ms | Single | A32nD | 18020010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.536ms | Single | A32nD | 18021440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.538ms | Single | A32nD | 18021440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.539ms | Single | A32nD | 18021C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.541ms | Single | A32nD | 18021C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.542ms | Single | A32nD | 18020000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.542ms | Single | A32nD | 18020010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.543ms | Single | A32nD | 18030000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.544ms | Single | A32nD | 18030010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.545ms | Single | A32nD | 18031440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.547ms | Single | A32nD | 18031440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.548ms | Single | A32nD | 18031C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.550ms | Single | A32nD | 18031C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.550ms | Single | A32nD | 18030000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.551ms | Single | A32nD | 18030010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.552ms | Single | A32nD | 18040000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.553ms | Single | A32nD | 18040010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.554ms | Single | A32nD | 18041440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.556ms | Single | A32nD | 18041440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.557ms | Single | A32nD | 18041C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.559ms | Single | A32nD | 18041C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.559ms | Single | A32nD | 18040000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.560ms | Single | A32nD | 18040010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.561ms | Single | A32nD | 18000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.562ms | Single | A32nD | 18000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.563ms | Single | A32nD | 18000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| 1.564ms | Single | A32nD | 19010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.565ms | Single | A32nD | 19010010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.566ms | Single | A32nD | 19011440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.568ms | Single | A32nD | 19011440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.569ms | Single | A32nD | 19011C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.571ms | Single | A32nD | 19011C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.571ms | Single | A32nD | 19010000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.572ms | Single | A32nD | 19010010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.573ms | Single | A32nD | 19020000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.574ms | Single | A32nD | 19020010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.575ms | Single | A32nD | 19021440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.577ms | Single | A32nD | 19021440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.578ms | Single | A32nD | 19021C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.579ms | Single | A32nD | 19021C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.580ms | Single | A32nD | 19020000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.581ms | Single | A32nD | 19020010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.582ms | Single | A32nD | 19030000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.583ms | Single | A32nD | 19030010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.584ms | Single | A32nD | 19031440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.585ms | Single | A32nD | 19031440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.587ms | Single | A32nD | 19031C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.588ms | Single | A32nD | 19031C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.589ms | Single | A32nD | 19030000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.590ms | Single | A32nD | 19030010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.591ms | Single | A32nD | 19040000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.591ms | Single | A32nD | 19040010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.593ms | Single | A32nD | 19041440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.594ms | Single | A32nD | 19041440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.596ms | Single | A32nD | 19041C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.597ms | Single | A32nD | 19041C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.598ms | Single | A32nD | 19040000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.599ms | Single | A32nD | 19040010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.600ms | Single | A32nD | 19000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.601ms | Single | A32nD | 19000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.602ms | Single | A32nD | 19000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| 1.603ms | Single | A32nD | 1A010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.603ms | Single | A32nD | 1A010010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.605ms | Single | A32nD | 1A011440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.606ms | Single | A32nD | 1A011440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.607ms | Single | A32nD | 1A011C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.609ms | Single | A32nD | 1A011C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.610ms | Single | A32nD | 1A010000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.611ms | Single | A32nD | 1A010010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.611ms | Single | A32nD | 1A020000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.612ms | Single | A32nD | 1A020010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.614ms | Single | A32nD | 1A021440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.615ms | Single | A32nD | 1A021440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.616ms | Single | A32nD | 1A021C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.618ms | Single | A32nD | 1A021C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.619ms | Single | A32nD | 1A020000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.620ms | Single | A32nD | 1A020010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.620ms | Single | A32nD | 1A030000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.621ms | Single | A32nD | 1A030010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.622ms | Single | A32nD | 1A031440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.624ms | Single | A32nD | 1A031440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.625ms | Single | A32nD | 1A031C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.627ms | Single | A32nD | 1A031C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.628ms | Single | A32nD | 1A030000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.628ms | Single | A32nD | 1A030010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.629ms | Single | A32nD | 1A040000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.630ms | Single | A32nD | 1A040010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.631ms | Single | A32nD | 1A041440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.633ms | Single | A32nD | 1A041440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.634ms | Single | A32nD | 1A041C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.636ms | Single | A32nD | 1A041C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.636ms | Single | A32nD | 1A040000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.637ms | Single | A32nD | 1A040010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.638ms | Single | A32nD | 1A000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.639ms | Single | A32nD | 1A000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.640ms | Single | A32nD | 1A000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| 1.641ms | Single | A32nD | 1B010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.642ms | Single | A32nD | 1B010010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.643ms | Single | A32nD | 1B011440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.645ms | Single | A32nD | 1B011440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.646ms | Single | A32nD | 1B011C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.648ms | Single | A32nD | 1B011C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.648ms | Single | A32nD | 1B010000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.649ms | Single | A32nD | 1B010010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.650ms | Single | A32nD | 1B020000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.651ms | Single | A32nD | 1B020010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.652ms | Single | A32nD | 1B021440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.654ms | Single | A32nD | 1B021440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.655ms | Single | A32nD | 1B021C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.656ms | Single | A32nD | 1B021C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.657ms | Single | A32nD | 1B020000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.658ms | Single | A32nD | 1B020010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.659ms | Single | A32nD | 1B030000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.660ms | Single | A32nD | 1B030010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.661ms | Single | A32nD | 1B031440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.662ms | Single | A32nD | 1B031440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.664ms | Single | A32nD | 1B031C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.665ms | Single | A32nD | 1B031C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.666ms | Single | A32nD | 1B030000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.667ms | Single | A32nD | 1B030010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.668ms | Single | A32nD | 1B040000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.668ms | Single | A32nD | 1B040010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.670ms | Single | A32nD | 1B041440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.671ms | Single | A32nD | 1B041440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.672ms | Single | A32nD | 1B041C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.674ms | Single | A32nD | 1B041C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.675ms | Single | A32nD | 1B040000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.676ms | Single | A32nD | 1B040010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.676ms | Single | A32nD | 1B000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.678ms | Single | A32nD | 1B000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.679ms | Single | A32nD | 1B000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| 1.680ms | Single | A32nD | 1C010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.680ms | Single | A32nD | 1C010010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.682ms | Single | A32nD | 1C011440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.683ms | Single | A32nD | 1C011440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.684ms | Single | A32nD | 1C011C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.686ms | Single | A32nD | 1C011C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.687ms | Single | A32nD | 1C010000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.688ms | Single | A32nD | 1C010010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.688ms | Single | A32nD | 1C020000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.689ms | Single | A32nD | 1C020010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.690ms | Single | A32nD | 1C021440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.692ms | Single | A32nD | 1C021440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.693ms | Single | A32nD | 1C021C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.695ms | Single | A32nD | 1C021C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.696ms | Single | A32nD | 1C020000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.696ms | Single | A32nD | 1C020010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.697ms | Single | A32nD | 1C030000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.698ms | Single | A32nD | 1C030010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.699ms | Single | A32nD | 1C031440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.701ms | Single | A32nD | 1C031440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.702ms | Single | A32nD | 1C031C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.704ms | Single | A32nD | 1C031C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.704ms | Single | A32nD | 1C030000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.705ms | Single | A32nD | 1C030010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.706ms | Single | A32nD | 1C040000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.707ms | Single | A32nD | 1C040010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.708ms | Single | A32nD | 1C041440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.710ms | Single | A32nD | 1C041440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.711ms | Single | A32nD | 1C041C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.712ms | Single | A32nD | 1C041C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.713ms | Single | A32nD | 1C040000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.714ms | Single | A32nD | 1C040010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.715ms | Single | A32nD | 1C000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.716ms | Single | A32nD | 1C000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.717ms | Single | A32nD | 1C000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |
| 1.718ms | Single | A32nD | 1D010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.719ms | Single | A32nD | 1D010010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.720ms | Single | A32nD | 1D011440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.722ms | Single | A32nD | 1D011440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.723ms | Single | A32nD | 1D011C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.725ms | Single | A32nD | 1D011C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.725ms | Single | A32nD | 1D010000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.726ms | Single | A32nD | 1D010010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.727ms | Single | A32nD | 1D020000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.728ms | Single | A32nD | 1D020010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.729ms | Single | A32nD | 1D021440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.731ms | Single | A32nD | 1D021440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.732ms | Single | A32nD | 1D021C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.733ms | Single | A32nD | 1D021C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.734ms | Single | A32nD | 1D020000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.735ms | Single | A32nD | 1D020010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.736ms | Single | A32nD | 1D030000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.737ms | Single | A32nD | 1D030010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.738ms | Single | A32nD | 1D031440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.739ms | Single | A32nD | 1D031440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.741ms | Single | A32nD | 1D031C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.742ms | Single | A32nD | 1D031C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.743ms | Single | A32nD | 1D030000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.744ms | Single | A32nD | 1D030010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.745ms | Single | A32nD | 1D040000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.745ms | Single | A32nD | 1D040010 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 1.747ms | Single | A32nD | 1D041440 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.748ms | Single | A32nD | 1D041440 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.749ms | Single | A32nD | 1D041C40 | FF001E08 | D32 | Rd | Data | ----- | 1111111 |
| 1.751ms | Single | A32nD | 1D041C40 | FF001E08 | D32 | Wr | Data | ----- | 1111111 |
| 1.752ms | Single | A32nD | 1D040000 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.753ms | Single | A32nD | 1D040010 | 0E738F06 | D32 | Wr | Data | ----- | 1111111 |
| 1.753ms | Single | A32nD | 1D000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.755ms | Single | A32nD | 1D000000 | 010FF000 | D32 | Rd | Data | ----- | 1111111 |
| 1.756ms | Single | A32nD | 1D000000 | 010FF001 | D32 | Wr | Data | ----- | 1111111 |

| TRIG: | ---- | 0.0ns | Single | A16nD | IACK=6 | ......A1 | LBYTE | Rd | Data | IACK6 | 1111111 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | ---- | 171.817ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |
| 2 | ---- | 171.822ms | Single | A16nD | 8314 | FF000000 | D32 | Rd | Data | ----- | 111111 |
| 3 | ---- | 171.824ms | Single | A16nD | 8314 | 1000000 | D32 | Wr | Data | ----- | 1111111 |
| 4 | ---- | 171.833ms | Single | A16nD | 8314 | FE000000 | D32 | Rd | Data | ----- | 1111111 |
| 5 | ---- | 171.834ms | Single | A16nD | 8314 | FE000000 | D32 | Wr | Data | ----- | 1111111 |
| 6 | ---- | 171.835ms | Single | A16nD | 9314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 7 | ---- | 171.835ms | Single | A16nD | 9314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 8 | ---- | 171.836ms | Single | A16nD | A314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 9 | ---- | 171.837ms | Single | A16nD | A314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 10 | ---- | 171.838ms | Single | A16nD | B314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 11 | ---- | 171.838ms | Single | A16nD | B314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 12 | ---- | 171.839ms | Single | A16nD | C314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 13 | ---- | 171.840ms | Single | A16nD | C314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 14 | ---- | 171.841ms | Single | A16nD | D314 | FF000000 | D32 | Rd | Data | ----- | 1111111 |
| 15 | ---- | 171.842ms | Single | A16nD | D314 | FF000000 | D32 | Wr | Data | ----- | 1111111 |
| 16 | ---- | 171.844ms | Single | A32nD | 18000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 17 | ---- | 171.845ms | Single | A32nD | 18000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 18 | ---- | 171.846ms | Single | A32nD | 19000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 19 | ---- | 171.847ms | Single | A32nD | 19000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 20 | ---- | 171.848ms | Single | A32nD | 1A000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 21 | ---- | 171.850ms | Single | A32nD | 1A000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 22 | ---- | 171.851ms | Single | A32nD | 1B000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 23 | ---- | 171.852ms | Single | A32nD | 1B000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 24 | ---- | 171.853ms | Single | A32nD | 1C000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 25 | ---- | 171.854ms | Single | A32nD | 1C000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 26 | ---- | 171.856ms | Single | A32nD | 1D000000 | 010FF001 | D32 | Rd | Data | ----- | 1111111 |
| 27 | ---- | 171.857ms | Single | A32nD | 1D000000 | 010FF000 | D32 | Wr | Data | ----- | 1111111 |
| 28 | ---- | 171.859ms | Single | A32nD | 18000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 29 | ---- | 171.859ms | Single | A32nD | 18000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 30 | ---- | 171.860ms | Single | A16nD | 8220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 31 | ---- | 171.860ms | Single | A16nD | 8218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 32 | ---- | 171.861ms | Single | A16nD | 8204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 33 | ---- | 171.861ms | Single | A16nD | 8220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 34 | 3--- | 171.864ms | Start | A32sMBLT | 25079800 FFF | E000100000001 | D64 | Wr | Data | ----- | 1111111 |
| 290 | 3--- | 171.903ms | Start | A32sMBLT | 2507A000 FFF | F00010000FFFF | D64 | Wr | Data | ----- | 1111111 |
| 32738 | 3--- | 176.859ms | Start | A32sMBLT | 24980800 FFF | F0001FFFD0005 | D64 | Wr | Data | ----- | 1111111 |
| 32802 | ---- | 176.870ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |
| 32803 | ---- | 176.874ms | Single | A16nD | 8314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 32804 | ---- | 176.875ms | Single | A16nD | 8314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 32805 | ---- | 176.970ms | Single | A32nD | 19000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 32806 | ---- | 176.971ms | Single | A32nD | 19000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 32807 | ---- | 176.971ms | Single | A16nD | 9220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 32808 | ---- | 176.972ms | Single | A16nD | 9218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 32809 | ---- | 176.972ms | Single | A16nD | 9204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 32810 | ---- | 176.972ms | Single | A16nD | 9220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 32811 | 3--- | 176.976ms | Start | A32sMBLT | 24878800 000 | 0FFFF00010000 | D64 | Wr | Data | ----- | 1111111 |
| 65515 | 3--- | 181.963ms | Start | A32sMBLT | 2417F800 FFF | F000000010002 | D64 | Wr | Data | ----- | 1111111 |
| 65579 | ---- | 181.974ms | Single | A16nD | IACK=7 | ......E3 | LBYTE | Rd | Data | IACK7 | 111111 |
| 65580 | ---- | 181.978ms | Single | A16nD | 9314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 65581 | ---- | 181.979ms | Single | A16nD | 9314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 65582 | ---- | 182.068ms | Single | A32nD | 1A000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 65583 | ---- | 182.069ms | Single | A32nD | 1A000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 65584 | ---- | 182.069ms | Single | A16nD | A220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 65585 | ---- | 182.069ms | Single | A16nD | A218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 65586 | ---- | 182.070ms | Single | A16nD | A204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 65587 | ---- | 182.070ms | Single | A16nD | A220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 65588 | 3--- | 182.074ms | Start | A32sMBLT | 24077800 FFF | F000100000004 | D64 | Wr | Data | ----- | 1111111 |
| 98292 | 3--- | 187.064ms | Start | A32sMBLT | 2397E800 FFF | E0003FFFF0003 | D64 | Wr | Data | ----- | 1111111 |
| 98356 | ---- | 187.075ms | Single | A16nD | IACK=7 | ......E5 | LBYTE | Rd | Data | IACK7 | 111111 |
| 98357 | ---- | 187.079ms | Single | A16nD | A314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 98358 | ---- | 187.080ms | Single | A16nD | A314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 98359 | ---- | 187.168ms | Single | A32nD | 1B000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 98360 | ---- | 187.169ms | Single | A32nD | 1B000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 98361 | ---- | 187.169ms | Single | A16nD | B220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 98362 | ---- | 187.170ms | Single | A16nD | B218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 98363 | ---- | 187.170ms | Single | A16nD | B204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 98364 | ---- | 187.171ms | Single | A16nD | B220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 98365 | 3--- | 187.174ms | Start | A32sMBLT | 23876800 000 | 10001 | D64 | Wr | Data | ----- | 1111111 |
| 131069 | 3--- | 192.162ms | Start | A32sMBLT | 2317D800 000 | 00001FFFF0001 | D64 | Wr | Data | ----- | 1111111 |
| 131133 | ---- | 192.173ms | Single | A16nD | IACK=7 | ......E7 | LBYTE | Rd | Data | IACK7 | 111111 |
| 131134 | ---- | 192.177ms | Single | A16nD | B314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 131135 | ---- | 192.178ms | Single | A16nD | B314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 131136 | ---- | 192.267ms | Single | A32nD | 1C000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 131137 | ---- | 192.268ms | Single | A32nD | 1C000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 131138 | ---- | 192.268ms | Single | A16nD | C220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 131139 | ---- | 192.269ms | Single | A16nD | C218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 131140 | ---- | 192.269ms | Single | A16nD | C204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 131141 | ---- | 192.270ms | Single | A16nD | C220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 131142 | 3--- | 192.273ms | Start | A32sMBLT | 23075800 000 | 1FFFFFFFE0001 | D64 | Wr | Data | ----- | 1111111 |
| 163846 | 3--- | 197.349ms | Start | A32sMBLT | 2297C800 FFF | D0002FFFF0003 | D64 | Wr | Data | ----- | 1111111 |
| 163910 | ---- | 197.362ms | Single | A16nD | IACK=7 | ......E9 | LBYTE | Rd | Data | IACK7 | 111111 |
| 163911 | ---- | 197.365ms | Single | A16nD | C314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 163912 | ---- | 197.366ms | Single | A16nD | C314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 163913 | ---- | 197.470ms | Single | A32nD | 1D000020 | 400 | D32 | Wr | Data | ----- | 1111111 |
| 163914 | ---- | 197.470ms | Single | A32nD | 1D000024 | 8800000C | D32 | Wr | Data | ----- | 1111111 |
| 163915 | ---- | 197.471ms | Single | A16nD | D220 | 007F0000 | D32 | Wr | Data | ----- | 1111111 |
| 163916 | ---- | 197.471ms | Single | A16nD | D218 | 40000 | D32 | Wr | Data | ----- | 1111111 |
| 163917 | ---- | 197.472ms | Single | A16nD | D204 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 163918 | ---- | 197.472ms | Single | A16nD | D220 | 0C000088 | D32 | Wr | Data | ----- | 1111111 |
| 163919 | 3--- | 197.476ms | Start | A32sMBLT | 22874800 000 | 0FFFD00000000 | D64 | Wr | Data | ----- | 1111111 |
| 196623 | 3--- | 202.650ms | Start | A32sMBLT | 2217B800 000 | 0FFFE0002FFFE | D64 | Wr | Data | ----- | 1111111 |
| 196687 | ---- | 202.663ms | Single | A16nD | IACK=7 | ......EB | LBYTE | Rd | Data | IACK7 | 111111 |
| 196688 | ---- | 202.667ms | Single | A16nD | D314 | 10000 | D32 | Rd | Data | ----- | 111111 |
| 196689 | ---- | 202.668ms | Single | A16nD | D314 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 196690 | ---- | 202.762ms | Single | A16nD | 203A | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196691 | ---- | 202.763ms | Single | A16nD | 203C | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196692 | ---- | 202.765ms | Single | A16nD | 203E | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196693 | ---- | 202.766ms | Single | A16nD | 2040 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196694 | ---- | 202.769ms | Single | A16nD | 2044 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196695 | ---- | 202.771ms | Single | A16nD | 2042 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196696 | ---- | 202.773ms | Single | A16nD | 2048 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196697 | ---- | 202.774ms | Single | A16nD | 2046 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196698 | ---- | 202.818ms | Single | A16nD | 2030 | ....1603 | WORD | Rd | Data | ----- | 1111111 |
| 196699 | ---- | 202.819ms | Single | A16nD | 2030 | ....1000 | WORD | Wr | Data | ----- | 1111111 |
| 196700 | ---- | 202.820ms | Single | A16nD | 2030 | ....1000 | WORD | Rd | Data | ----- | 1111111 |
| 196701 | ---- | 202.821ms | Single | A16nD | 2030 | ....1040 | WORD | Wr | Data | ----- | 1111111 |
| 196702 | ---- | 202.822ms | Single | A16nD | 2060 | ....09A1 | WORD | Rd | Data | ----- | 1111111 |
| 196703 | ---- | 202.823ms | Single | A16nD | 2060 | ....09A1 | WORD | Wr | Data | ----- | 1111111 |
| 196704 | ---- | 202.826ms | Single | A16nD | 2066 | ....0000 | WORD | Rd | Data | ----- | 1111111 |
| 196705 | ---- | 202.829ms | Single | A16nD | 2034 | ....00AA | WORD | Wr | Data | ----- | 1111111 |
| 196706 | ---- | 202.830ms | Single | A16nD | 2036 | ....0010 | WORD | Wr | Data | ----- | 1111111 |
| 196707 | ---- | 202.830ms | Single | A16nD | 2010 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196708 | ---- | 202.831ms | Single | A16nD | 2012 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196709 | ---- | 202.832ms | Single | A16nD | 2014 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196710 | ---- | 202.833ms | Single | A16nD | 2016 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196711 | ---- | 202.834ms | Single | A16nD | 2018 | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196712 | ---- | 202.835ms | Single | A16nD | 201A | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196713 | ---- | 202.835ms | Single | A16nD | 201C | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196714 | ---- | 202.836ms | Single | A16nD | 201E | ....0001 | WORD | Wr | Data | ----- | 1111111 |
| 196715 | ---- | 202.837ms | Single | A16nD | 2030 | ....0040 | WORD | Wr | Data | ----- | 1111111 |
| 196716 | ---- | 202.838ms | Single | A16nD | 2026 | ....005F | WORD | Wr | Data | ----- | 1111111 |
| 196717 | ---- | 202.839ms | Single | A16nD | 2030 | ....0040 | WORD | Rd | Data | ----- | 1111111 |
| 196718 | ---- | 202.840ms | Single | A16nD | 2030 | ....00C0 | WORD | Wr | Data | ----- | 1111111 |
| 196719 | ---- | 202.843ms | Single | A16nD | 2060 | ....01A0 | WORD | Wr | Data | ----- | 1111111 |
| 196720 | ---- | 202.844ms | Single | A16nD | 2070 | ....0009 | WORD | Wr | Data | ----- | 1111111 |
| 196721 | ---- | 205.776ms | Single | A32nD | 18000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 203937 | ---- | 215.294ms | Single | A32nD | 19000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 211153 | ---- | 224.810ms | Single | A32nD | 1A000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 218369 | ---- | 234.311ms | Single | A32nD | 1B000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 225585 | ---- | 243.808ms | Single | A32nD | 1C000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 232801 | ---- | 253.653ms | Single | A32nD | 1D000000 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 240017 | ---- | 263.317ms | Single | A16nD | 8310 | 1010000 | D32 | Rd | Data | ----- | 1111111 |
| 240018 | ---- | 263.318ms | Single | A16nD | 8310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240019 | ---- | 263.319ms | Single | A16nD | 8314 | FFFFFFFF | D32 | Wr | Data | ----- | 1111111 |
| 240020 | ---- | 263.319ms | Single | A16nD | 8310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240021 | ---- | 263.320ms | Single | A16nD | 8310 | 1010000 | D32 | Wr | Data | ----- | 1111111 |
| 240022 | ---- | 263.321ms | Single | A32nD | 18000008 | 000000FF | D32 | Wr | Data | ----- | 1111111 |
| 240064 | ---- | 263.353ms | Single | A16nD | 9310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240065 | ---- | 263.354ms | Single | A16nD | 9310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240066 | ---- | 263.354ms | Single | A16nD | 9314 | FFFFFFFF | D32 | Wr | Data | ----- | 1111111 |
| 240067 | ---- | 263.355ms | Single | A16nD | 9310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240068 | ---- | 263.356ms | Single | A16nD | 9310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240069 | ---- | 263.356ms | Single | A32nD | 19000008 | 000000FF | D32 | Wr | Data | ----- | 1111111 |
| 240111 | ---- | 263.382ms | Single | A16nD | A310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240112 | ---- | 263.383ms | Single | A16nD | A310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240113 | ---- | 263.383ms | Single | A16nD | A314 | FFFFFFFF | D32 | Wr | Data | ----- | 1111111 |
| 240114 | ---- | 263.384ms | Single | A16nD | A310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240115 | ---- | 263.385ms | Single | A16nD | A310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240116 | ---- | 263.385ms | Single | A32nD | 1A000008 | 000000FF | D32 | Wr | Data | ----- | 1111111 |
| 240158 | ---- | 263.410ms | Single | A16nD | B310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240159 | ---- | 263.411ms | Single | A16nD | B310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240160 | ---- | 263.412ms | Single | A16nD | B314 | FFFFFFFF | D32 | Wr | Data | ----- | 1111111 |
| 240161 | ---- | 263.412ms | Single | A16nD | B310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240162 | ---- | 263.413ms | Single | A16nD | B310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240163 | ---- | 263.414ms | Single | A32nD | 1B000008 | 000000FF | D32 | Wr | Data | ----- | 1111111 |
| 240205 | ---- | 263.439ms | Single | A16nD | C310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240206 | ---- | 263.440ms | Single | A16nD | C310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240207 | ---- | 263.440ms | Single | A16nD | C314 | FFFFFFFF | D32 | Wr | Data | ----- | 1111111 |
| 240208 | ---- | 263.441ms | Single | A16nD | C310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240209 | ---- | 263.442ms | Single | A16nD | C310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240210 | ---- | 263.442ms | Single | A32nD | 1C000008 | 000000FF | D32 | Wr | Data | ----- | 1111111 |
| 240252 | ---- | 263.467ms | Single | A16nD | D310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240253 | ---- | 263.468ms | Single | A16nD | D310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240254 | ---- | 263.469ms | Single | A16nD | D314 | FFFFFFFF | D32 | Wr | Data | ----- | 1111111 |
| 240255 | ---- | 263.469ms | Single | A16nD | D310 | 10000 | D32 | Rd | Data | ----- | 1111111 |
| 240256 | ---- | 263.470ms | Single | A16nD | D310 | 10000 | D32 | Wr | Data | ----- | 1111111 |
| 240257 | ---- | 263.471ms | Single | A32nD | 1D000008 | 000000FF | D32 | Wr | Data | ----- | 1111111 |
| 240299 | ---- | 263.497ms | Single | A32nD | 18000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 240300 | ---- | 263.497ms | Single | A32nD | 19000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 240301 | ---- | 263.498ms | Single | A32nD | 1A000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 240302 | ---- | 263.499ms | Single | A32nD | 1B000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 240303 | ---- | 263.499ms | Single | A32nD | 1C000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 240304 | ---- | 263.500ms | Single | A32nD | 1D000018 | 0 | D32 | Wr | Data | ----- | 1111111 |
| 240305 | ---- | 263.501ms | Single | A32nD | 18000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 240324 | ---- | 263.528ms | Single | A32nD | 19000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 240343 | ---- | 263.553ms | Single | A32nD | 1A000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 240362 | ---- | 263.577ms | Single | A32nD | 1B000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 240381 | ---- | 263.601ms | Single | A32nD | 1C000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 240400 | ---- | 263.626ms | Single | A32nD | 1D000004 | FFFF8100 | D32 | Rd | Data | ----- | 1111111 |
| 240419 | ---- | 263.658ms | Single | A32nD | 18010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 240454 | ---- | 263.699ms | Single | A32nD | 19010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 240489 | ---- | 263.737ms | Single | A32nD | 1A010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 240524 | ---- | 263.776ms | Single | A32nD | 1B010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 240559 | ---- | 263.814ms | Single | A32nD | 1C010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 240594 | ---- | 263.853ms | Single | A32nD | 1D010000 | 016B9006 | D32 | Wr | Data | ----- | 1111111 |
| 240629 | ---- | 263.905ms | Single | A16nD | 2060 | ....01A0 | WORD | Rd | Data | ----- | 1111111 |
| 240630 | ---- | 263.906ms | Single | A16nD | 2060 | ....11A0 | WORD | Wr | Data | ----- | 1111111 |
| 240631 | ---- | 263.916ms | Single | A16nD | 2030 | ....00C0 | WORD | Rd | Data | ----- | 1111111 |
| 240632 | ---- | 263.917ms | Single | A16nD | 2030 | ....02C0 | WORD | Wr | Data | ----- | 1111111 |
| 240633 | ---- | 263.918ms | Single | A16nD | 2062 | ....10C6 | WORD | Rd | Data | ----- | 1111111 |
| 240634 | ---- | 263.919ms | Single | A16nD | 2062 | ....10C6 | WORD | Wr | Data | ----- | 1111111 |
| 240635 | ---- | 263.921ms | Single | A16nD | 2030 | ....02C0 | WORD | Rd | Data | ----- | 1111111 |
| 240636 | ---- | 263.922ms | Single | A16nD | 2030 | ....02C0 | WORD | Wr | Data | ----- | 1111111 |
| 240637 | ---- | 263.923ms | Single | A16nD | 2062 | ....10C6 | WORD | Rd | Data | ----- | 1111111 |
| 240638 | ---- | 263.924ms | Single | A16nD | 2062 | ....10C6 | WORD | Wr | Data | ----- | 1111111 |
| 240639 | ---- | 263.926ms | Single | A16nD | 2030 | ....02C0 | WORD | Rd | Data | ----- | 1111111 |
| 240640 | ---- | 263.928ms | Single | A16nD | 2030 | ....02C0 | WORD | Wr | Data | ----- | 1111111 |
| 240641 | ---- | 263.929ms | Single | A16nD | 2062 | ....10C6 | WORD | Rd | Data | ----- | 1111111 |
| 240642 | ---- | 263.930ms | Single | A16nD | 2062 | ....10C6 | WORD | Wr | Data | ----- | 1111111 |
| 240643 | ---- | 263.931ms | Single | A16nD | 2030 | ....02C0 | WORD | Rd | Data | ----- | 1111111 |
| 240644 | ---- | 263.932ms | Single | A16nD | 2030 | ....0280 | WORD | Wr | Data | ----- | 1111111 |
| 240645 | ---- | 263.933ms | Single | A16nD | 2030 | ....0280 | WORD | Rd | Data | ----- | 1111111 |
| 240646 | ---- | 263.934ms | Single | A16nD | 2030 | ....0683 | WORD | Wr | Data | ----- | 1111111 |
| 240647 | ---- | 265.294ms | Single | A16nD | IACK=6 | ......A0 | LBYTE | Rd | Data | IACK6 | 1011111 |
| 240648 | ---- | 266.653ms | Single | A16nD | IACK=7 | ......E1 | LBYTE | Rd | Data | IACK7 | 111111 |