Gain Ramping for Transverse Stochastic Cooling Systems in the Debuncher

Dave McGinnis

November 15, 2004

Transverse Stochastic Cooling Equation

For transverse stochastic cooling, the cooling term is given as:

(1)

(2)

where fo is the revolution frequency, pc is the momentum of the beam, Zpu and Zkr is the pickup and kicker impedance, pu and kr are the beta functions at the pickup and kicker, hpu is the effective height off he pickup, and gm is the electronic gain at the mth betatron sideband. The heating term due to other particles is:

(3)

where Np is the number of particles and fo is the spread in revolution frequencies. The heating term due to amplifier noise is:

(4)

where S((a2)rms) is the average signal to noise and is given as:

(5)

where kB is Boltzman’s constant (1.36x10-23 Watts K-1Hz-1) and Tpu is the effective noise temperature of the pickup and pickup pre-amplifier. If the gain of the electronics is flat over a bandwidth W, then the r.m.s. betatron amplitude is given as:

(6)

where M(t) is the mixing factor:

(7)

where fmax and fmin are the maximum and minimum frequencies of the cooling system.

Gain Ramping

The output power of the cooling system is given as:

(8)

where Pbo is the initial beam power, Pn is the noise power, and go is the initial gain. The noise power can be written as the initial beam power divided by the initial signal to noise:

(9)

The total initial power is:

(10)

The ratio of beam power to initial beam power is equal to the ratio of the emittance to the initial emittance:

(11)

Equation 8 becomes

(12)

The gain profile as a function of power is:

(13)

Example

The gain ramping in the following example is set so that the total cooling system power is kept constant throughout the entire cycle. The parameters used in the example are shown in Table 1.

| fmin | 4.5 | GHz |
| --- | --- | --- |
| fmax | 7.5 | GHz |
| Production | 15 | x10-6 |
| MI Beam | 5 | x1012 |
| fo | 590020 | Hz |
|  | 0.006 |  |
| pco | 8801 | MeV |
| pcinit | 80 | MeV |
| pcasym | 5 | MeV |
| pc | 1 | Sec |
| 95init | 20 | -mm-mrad |
| init | 1.3 | Sec |

Table 1.

The revolution frequency spread for the mixing factor is computed from the following:

(14)

The parameter init is the initial cooling rate which is used to determine the initial electronic gain:

(15)

Figure 1 shows the emittance as a function of time for an initial average signal to noise of three with and without gain ramping. Using the same average initial signal to noise ratio, Figure 2 shows the ratio between the cooling to heating term with and without gain ramping. For this example, the heating term does not contribute substantially to the cooling rate. Figure 3 shows the emittance at the end of two seconds of cooling as a function of the initial signal to noise ratio. If the initial signal to noise ratio is three, then using gain ramping reduces the emittance by 35%.

Figure 1. Emittance as a function of time for an initial average signal to noise of three with and without gain ramping.

Figure 2. The ratio between the cooling to heating term with and without gain ramping.

Figure 3. The emittance at the end of two seconds of cooling as a function of the initial signal to noise ratio