# IBS Experiment In Tevatron

### Vladimir Shiltsev, Alvin Tollerstrup, FNAL/AD, PO Box 500 Batavia IL 60510

Abstract: In this paper we analyze data on intrabeam scattering (IBS) in the Tevatron.

15 proton bunches with various intensities were accelerated to 980 GeV and squeezed on the proton helix at Low-Beta.

Experimental data are presented in the following Table:

#  E_v_0  	E_v_f 		dE_v		 N_p	        Sig_z_0  Sig_z_f

1	  14.12		16.879		2.759		51.066		1.889	0.5095

2	  15.63		18.267		2.637		44.419		2.066	0.34794

3	  15.466	17.519		2.053		44.089		2.1	0.34518

4	  15.543	18.825		3.282		116.14		1.707	1.1103

5	  14.711	18.24		3.529		114.884	1.75	1.1634

6   15.797	18.822		3.025		115.309	1.761	1.0429

7	  15.739	19.335		3.596		138.225	1.723	1.2848

8	  16.232	29.585				144.518	1.73	1.27737

9	  16.34		20.173		3.833		140.589	1.724	1.23463

10 16.473	27.59				186.631	1.723	1.62009

11 16.414	20.749		4.335		184.062	1.783	1.55236

12 16.454	20.823		4.369		186.606	1.796	1.55673

13 20.539	24.529		3.99		221.647	1.846	1.28992

14 21.218	30.074				219.191	1.802	1.24455

15 21.339	25.068		3.729		225.643	1.846	1.24002

Bunches 8, 10 and 14 were blown up by several occurances of a transverse  instability which took place over 3.1 hr store.

Distribution of bunch intensities is at the start of the store is given in Fig.1:

Fig.1: Initial bunch intensities N_p

Emittance changes over 3.1 hrs are presented in Fig.2 and 3:

Fug.2: Vertical emittance increase vs IBS factor F

Fug.3: Longitudinal emittance increase vs IBS factor F

Theory and simulations of the IBS in the bunches with small longitudinal velocity spread compared to the transverse one predict growth of transverse and longitudinal emittances [1]:

and    (1),

CL and CT are constants determined by machine parameters. From (1), one expects that observed emittance increases to be proportional to the factor   (we picked vertical emittance as its systematic error and uncertainty for the current Tevatron Flying Wires system are much smaller than for the horizontal emittance, while it’s known from the experience that usually the two emittances are proportional to each other). As seen from Figs.2 and 3, the observed increases can be approximated by:

and

(2).

The intercept in the transverse emittance growth gives an estimate on the growth due to vacuum (equivalent to average room-temperature N2 vacuum pressure of 1.6(+-0.2)e-9 Torr) and/or external noises; the intercept in the bunch length growth is proportional to lengthening due to RF noise (equivalent to PSD of RF noise of S(f_s)= 136(+-30) 1/Hz).

Theory of  Touchek scattering also predicts linear dependence of a bunched lifetime on the same factor F , and one can see measured intensity decay vs F in Fig.4:

Fig.4: Intensity lifetime vs the IBS factor F.

Linear fit suggests that

. (3)

Again, the intercept corresponds to vacuum lifetime of about 800(+-500) hours and equivalent average room-temperature N2 pressure of  0.41(+-0.30)e-9 Torr.

The Table below summarizes predictions of the approximations (2) and (3) for beam parameters at injection and in collisions. E.g., a typical HEP store parameters are  N_p=250 e9, proton emmittances are about 20 pi and initial bunchlength is of about 1.7 ns rms  yielding F=1.64 for protons; for high intensity pbar bunchs N_a=50 e9, emmittances are about 12 pi and initial bunchlength is of about 1.6 ns rms  that gives F=0.43 for protons.

F

Low intensity		0		3.8			0			800

@ Injection

…compare with [2]	0		2.9			n/a			1000

Pbars @ Inj		0.43		3.86			0.09			540

…compare with 3717	0.27		4.3			shaving			shaving

Protons @ Inj		1.64		4.0			0.36			270

…compare with [3]	1.9		3.0			shaving			shaving

Low intensity 		0		0.58			0.05			800

@ Low-Beta

…compare with Alvin 12/01/2004	n/a			n/a		     	2100

…compare with [1]			n/a			0.02			n/a

Pbars @ LB		0.43		0.80			0.12			620

…compare with [1]			0.7			0.08		      NLL~100

Protons @ LB		1.64		1.43			0.28			360

…compare with [1]			1.1			0.33		      NLL~150

Other experimental results are given in bold font for comparison. One can see that results of the presented IBS study are close to what used to observe, that makes noise and vacuum estimates believable. That also makes us to believe that few occurencies of the coherent instability happened during the study did not mess the study results much.

At 150 GeV, the proton bunches stayed for 280 sec on a helix orbit before the ramp, and that allows us to calculate bunch lifetime with acceptable accuracy (but not emittance growth rates). Resulting plots are given below. One can conclude from them that neither IBS factor nor bunch intensity nor vertical emittance correlate with the los rate. The only definite correlation is seen between the loss rate and bunch length. Thus, the longitudinal effects (diffusion, chromaticity and dynamic aperture) play the major role for protons at injection energy.

Fig.5: Intensity lifetime at 150 GeV vs the IBS factor F

Fig.6: Intensity lifetime at 150 GeV vs bunch intensity.

Fig.7: Intensity lifetime at 150 GeV vs bunch emittance.

Fig.8: Intensity lifetime at 150 GeV vs bunch length.

## Conclusions

The study results allow to separate vacuum and noise effects from the IBS.  One can conclude that noise and vacuum contribution to the transverse emittance growth  is comparable with the IBS; at the start of HEP store, noise contribution to the bunch lengthening is ¼ of the IBS one for protons and ½ for pbars; Touchek lifetime for protons is about the vacuum lifetime at both energies.

### References:

[1]  V.Lebedev, beams-doc-1509 (2004), see also D.Finley, FNAL-TM-1646 (1989); V.Lebedev, in Proc. IEEE PAC 2003 (Portland).

[2]  V.Lebedev, L.Nicolas, A.Tollestrup, beams-doc-1155 (2004).

[3]  M.Syphers, N.Eddy, beams-doc-1199 (2004).