- 8 - Clock Outputs PhaseLocked to the 53.10468Mhz Clock

  - Currently Clock outputs are 7/5 x the RFClk

- 8 - ADCSync Outputs  are Timed from the BSync input w/

  - One common Pretrigger delay (delay by # turns)

  - Number of ADCSync’s generated (once per turn) per output

  - ADCSync delays per output are accurate to a ½ bucket resolution

  - All Timing and Delays are configurable by VME

- 2 - VME Interrupts (level 5 or 6) can be generated, typically for

  - From on BSync events

  - From on TClk events (up to 16 events)

- Time Stamp counter (64-bits) with ½ bucket resolution

  - Cleared on a  BSync start event

  - Records the First Turn Register after a start event

  - Records Bsync Time Stamp event

  - Records TClk Time Stamp event

- Stores the occurance of all Bysnc & TClk events

  - Used to verify that events are present at a particular location

- Controls diagnostics for inhouse designed filter cards

- Contains an ID Rom for version control

# Text boxes

Vtt

SMB

TTL

Driver

24ma

Y

Clock Generation

(74Mhz)

Clock Fanout  Section

Clk7

Clk6

Clk5

Clk4

Clk3

Clk2

Clk1

Clk0

.01uF

SMB

50 Ohm

Vtt

Vtt

N

50 Ohm

Y

Generates TClk

Interrupt

SMB

MiniCircuits

SALF_78

MiniCircuits

ADTT1-1

50 Ohm

Vtt

Vtt

Vtt

ADCSync

Count

Done

?

Vtt

BLM Control

EDB

(Parallel TTL)

A

Vtt

Vtt

SMB

BSync

State Machine

BPM VME Timing Generator Fanout (TGF)

RFclk

(53.10468Mhz)

:

:

:

:

:

7

0

Clock

Multiplier

and

FanOut

:

:

:

:

:

Digitizer Clock

(79.65702Mhz)

7

0

SYNC

OUT

CLOCK

OUT

MDat

OE

OUTn

OUTp

1K

Vtt

Locked

Digitizer Clock

(74.34655Mhz)

ClkIn

Connor Winfield

Synchronous Clock Generator

SG743465

MAX901

SMB

N

50

Y

50

TClk Event

Equal

x”7C”

?

Vtt

VCC

50

RFClk

TClk

PECL

R

C

V

R

Vtt

Calibration

Relay Control (PSI)

VME

Interface

V

M

E

B

u

f

f

e

r

s

Altera  Stratix

EP1S25

Vtt

50 Ohm

Vtt

.01uF

SMB

50 Ohm

A

N

Y

.01uF

.01uF

SMB

Vtt

Vtt

.01uF

Vtt

.01uF

SMB

50 Ohm

Vtt

Vtt

.01uF

SMB

50 Ohm

Vtt

Vtt

.01uF

SMB

50 Ohm

Closed Orbit

Mode

Y

ADC

ADC

ADC

ADC

ADC

Relay

Relay

Relay

Relay

Relay

CPU

Relay

ADC

Fanout

N

Echotek

Readout

Done

?

4

4

4

4

4

4

7

4

4

4

4

4

4

CPU

Generate ADC Sync

To Echotek Card

Y

N

Bucket Delay

Done

?

Clk7

14-Bit DAC

Analog Out

Clock Fan Out

Trigger I/O

Bucket Delay

Done

?

N

Y

Pretrigger

Done

?

TurnEvent

Occur

?

500Hz

Time Out

?

N

Y

N

N

Y

Y

BPM VME Timing Generator Fanout (TGF)

Features

Setup Echotek & Timing Card for

Close Orbit

Closed Orbit

Mode

Pretrigger

Done

?

N

Y

Turn Event

Occur

?

N

Start Event

Occur

?

N

Y

Closed

Orbit

Finished

?

Setup Echotek & Timing Card for

Turn-by-Turn

Turn by Turn

Mode