- Shemyakin

Recycler department meeting

January 11, 2006

Notes about an operation at 600 E10 level

- (Very) approximate scenario

- Possible hindrances for 600 E10 operation (with the last shot as an example)

- Summary

- Assumptions:

- Antiproton production rate increases by factor of 2

- Phase density in Accumulator is the same

- Store length is the same

Hence, the transfers should be twice more frequent.

| Parameter | units | Last 3 shots | 2007 |
| --- | --- | --- | --- |
| Max number of pbars | E10 | 300 - 370 | 600 |
| Time between shots | hour | 34 | 30 |
| Amount of pbars per transfer | E10 | 50 -70 | 60 |
| Number of transfers |  | 5 - 6 | 10 |
| Time between transfers | hour | 6 | 3 |
| RR transfer time | hour | 0.5 - 1 | 0.5 |
| Transverse cooling time | hour | 1.5 - 2 | 2 |
| Longitudinal cooling and squeeze time | hour | 0.5 - 1 | 0.5 |

Possible problems

Store #4587 (10-Jan-06) as an example

Cooling + transfer time might be too long.

So far no dramatic problems with transverse cooling.

Note that before a transfer, the transverse emittance R:EMVANM = 3-4 (, the longitudinal emittance R:LEMITA = 60 eVs.

The life time drops with longitudinal cooling/ squeezing. The value of R:LIFE immediately before transfers decreases with number of pbars.

The total additional loss ~ 10 E10, i.e. ~3%. It seems that the effect exists at modest intensities as well.

Density before the shot approximately corresponds to the density of a fully extended beam at 600 E10.

Losses are high during transfers at a large stash.

| Transfer# | 1 | 2 | 3 | 4 | 5 | 6 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| End | 243.0 | 261.4 | 275.8 | 285.5 | 293.0 | 297.5 | 299.7 |
| Beginning | 261.9 | 276.4 | 286.3 | 293.8 | 298.4 | 300.9 |  |
| Transferred | 19.0 | 15.0 | 10.5 | 8.3 | 5.4 | 3.4 |  |
| Lost | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.2 |  |

Total transfer:	61.5

Total loss:		4.7 		(7.7 %)

The loss depends on the total number of pbars, in the previous transfer the numbers were 68.3/2.1.

Emittance growth in the time of mining

R:EMVANM grows from 2.5 to ~ 8 (.

Initial phase density

For 600 E10, it might be a comparable number if the initial transverse emittance is twice larger.

Summary of difficulties and questions

- Cooling + transfer time

- Is the present stochastic cooling system adequate for 600 E10 and 5 - 6 (?

- Can we use a gated cooling?

- Shall we cool at higher e-beam currents?

- Poor life time at large intensities

Seems to be the critical issue. We need more studies of the phenomenon.

What we can try:

- optimization of e-current/ offset

- optimization of e-cooling procedure (minimizing the time at a high pbar density)

- RF & stochastic cooling optimization

- a different working point in the tune space

- a larger electron beam size

- a higher magnetic field in the cooling section

- Losses at transfers

- Shall we lower the number of parcels per transfer at higher intensities?

- Can improvements of the Recycler optics help?

- Emittance growth during mining

There are indications that with the electron beam being off axis or completely off during shots the growth rate might be acceptable.

Keeping pbars at a lower density during shots (e.g. “morphing”) may help.

Can we e-cool faster?

Cooling of a transfer on 20-Dec-2005 with a 0.3 A electron beam on axis

Total cooling time was ~ 70 min.

… but the life time recovered in another ~ 1 hour.

From Lionel’s RR talk on 30-Nov-05

Summary of the measurements of the emittance growth during mining

[11/14 & 11/22-11/23 measurements]

Indications that with the electron beam off axis or completely off the growth rate might be acceptable.

# Text boxes

R:LIFE

R:BEAM

9 hours

10 min

30 min

Ie = 0.3A

1h

10 min

107e10

97e10

180e10

pbars intensities:

114e10

9 hours