Geometry of Kicker
C.Y. Tan
20 Mar 2007

---
Geometry
Calculation is for infinitely long kicker
For Zeven =73 and R=50, next reflection is 27dB lower, so should be OK.
Basically because of 2 reflections:
{{V_{m}} over {V_{m-1}}}= left( {{1 - R/Z_0}over {1 + R/Z_0}}right)^2
Distance between plates 35mm

---
Calculation Using Poisson Sum Mode
Equipotential Lines shown

---
Calculation Using Poisson Difference Mode