Kicker Design Discussions Held at PAC 2007
C.Y. Tan
26 Jun 2007

---
People I have talked to
Mark Palmer (Cornell University)
Junji Urakawa (KEK)
Fabio Marcellini (IFN)
Giancarlo Sensolini (IFN)
Stefano de Santis (LBNL)

---
The kickers which are being designed right now
KEK will have 4 sets of kickers which work at 10kV. The aperture will be 12 mm.
  - Naito
Two sets of kickers being designed by Stefano for KEK (24 mm aperture)
  - Simulations only. Not quite complete because feedthru dimensions not known.
The most mature design is from Frascati. Prototype ready for testing next week.

---
Frascati Design
1 m long.
Race track aperture: 43mm x 60mm.
Tapered design. Only 3 mm between feedthru and plates.
  - The use of a tapered design has 3 advantages
    - No sparking between feedthru and plate because of short distance
    - Smooth impedance change seen by beam.
    - More uniform field seen by beam?
Feedthru' design has been fixed by the Frascati team.

---
Frascati Design (cont'd)
High voltage cables come from FID technologies.
Pulser is from FID technologies.
  - 50kV, 300 ps rise time, 5ns flattop, 2ns fall time. No secondary pulse! Rep rate? Frascati repetition requirements are not the same as the ILC kicker specs.
They will start doing RF measurements next week. They will send us the measurements once it is done.

---
What I have right now
Drawings of the Frascati design.
  - Bill of Materials will be sent out to us.
  - We also have the feedthru' design

---
Cartoon of our kicker dimensions
3.4cm
19.2cm
26cm
30cm

---
Bellows shorten length by about 10cm!

---
For 20 mrad kick
Original specs: If l = 25 cm, then pd = 7kV.
If I = 15 cm (for 19.2 cm, assume 20% for taper), then pd = 11.6 kV.
If I = 7 cm then (for 9.2cm, assume 20% for taper), then pd = 23.7 kV.

---
Plan
Do HFSS simulation (Ding) for current Frascati design.
Do HFSS simulation for our kicker. Dimensions to be decided.
Build prototype for electrical measurements.
  - Use the same feedthru's as Frascati.
Build prototype for high power test.
  - Material: stainless or aluminium?
Build final design for NML.