Survey of RFAs
C.Y. Tan
26 Feb 2008

---
Goal
To see what other people have done
  - Especially RFAs with microchannel plates or electron multipliers.
Some preliminary design and requirements
  - What calculations do we need to do
    - Efield profile of retarding field and analyzer.
    - Parameters required for microchannel
  - What do we want to measure?

---
Microchannel Plate/Electron Multiplier RFAs
This is really not new. People have designed this type of RFAs before circa 1971!
  - Reference: P. Stalb, “An Improved Retarding Field Analyser”, J. Phys. E, 484, 5, 1972.
People have used Electron Multiplier Tube (EMT) rather than Microchannel plate for detector. c.f. mass spectrometer. MCPs have higher gain. This also depends on geometry, will the design have a small hole?

---
1971 Design with Channeltron EMT
A sophisticated design with focusing and defocusing grids for energy selection.
Focusing
Field
screen
Retarding
Field

---
CERN Design (used for IPM)
MCP
Uses dipole field as energy selector
A. Arauzo, “First results of the Beam Gas lonization Profile Monitor (BGIP) tested in the SPS ring”, BIW2000.

---
BNL Design (APS)
Called pillbox or bessel box analyser. All parts coated with graphite to reduce SEY.
Circular Stop

---
Present RFA in MI
Very noisy if retarding fields used because of lower signals.

---
Commercial EMT
Designed for vacuum use.
Cost is $3700. This is called “Channel Electron Multiplier” by the manufacturer Amptek. Gain is about 107 per electron.
3.6 to 10mm hole

---
What we need to decide/discuss
I think having an EMT or MCP is the way to go.
Do we need sophisticated lens geometry a la 1971 design? Or simpler geometry like APS.
What I'd like to measure
  - Energy distribution as function of beam intensity and bunch pattern.
  - Can this form base line for answering whether changing RF frequency will fix problem. This will probably need computer simulation, so what are the input params?