Painting modeling using ORBIT for Project-X

L.G. Vorobiev, APC/FNAL

- Painting  generates phase space distributions by a controlled offsetting of injected beams

- Project-X presumably requires a KV-like will be the optimal one to mitigate Space Charge in RR.

ORBIT Features:

- 1st and 2nd order transfer matrices.

- Self consistent inclusion of SC  and wakes.

- Foil scattering:

  - Repeated single scattering model borrowed from (ACCSIM,TRIUMF-made).

  - Small-angle Coulomb scattering.

  - Rutherford scattering.

- Different bump magnet wave forms (Exp. Bump form + interpolated from Table).

Draft Examples for FNAL MI

SC-on:                                   , νx =6.69,  νx=6.8:

Phase ellipses off-setting during painting. Closed orbit ellipses (no bumps).  Foil is not at a crossover.

10 turns                                         10 turns

20 turns                                         20 turns

30 turns                                         30 turns

Draft Examples for FNAL Booster

For zero SC, νx =6.69,  νx=6.8:

SC-off (blue)

Non-resonant, SC-off (green)

Non-resonant, SC-on (red)

40 turns                                         40 turns

TODO

- Studies and optimal chice of painting scenario:

correlated/anti-correlated, something else…

- Analysis of sensitivity to errors, resulting in halo formation, mismatching, particle losses.

- Visialization using ROOT package to evaluate the painting.

- Cross-checking with available codes (STRUCT, ACCSIM)

- Foil scattering, heating & lifetime realistric estimation (MARS routins adaptation in C++ to ORBIT)

- New blocks will be added to ORBIT if necessary along with further ORBIT debugging (MAD-generated Twiss/Transfer matrix input to be 100% accommodated by ORBIT, self-consistent 6D phase distribution, ECloud incorporation,…).