Title
Upgrading Electronics for the LLRF
Electronics Design Efforts
Craig Drennan, April 16,2009

---
Product general
Goals in Upgrading the LLRF Electronics
Eliminate outdated, difficult to replace components.
  - Mixers in phase shifters, comparators and amplifiers.
Provide a cleaner more robust layout of the racks and individual modules.
  - Reduce the tangle of interconnecting coax cables.
  - Reduce the number of modules.
  - Replace post soldered modules with printed circuits.

---
Product general
Goals in Upgrading the LLRF Electronics (cont.)
Provide more flexibility in the Main Injector phase lock process.
  - The current MI phase lock electronics are rigidly implemented with analog electronics from 20+ years ago.
The upgrade effort currently does not propose to change the basic structure of the LLRF control loops.
  - The acceleration phase lock and the radial position control loops will initially be replicated in their function and basic static and dynamic parameters.

---
Product general
Challenges
Understanding the function and parameters of the existing system is essential.
  - Operators expect to have the same control over the new system as they do the existing one.
  - Re-writting console applications cannot be done is many circumstances.
  - Closed loop static and dynamic parameters nust be understood, appreciated and able to be implemented in any new system.

---
Product general
Challenges (cont.)
New electronics must facilitate controlled integration into a working system.
  - Testing and eventual implementation of new modules must not interfere with the normal operation of the Booster.
  - Reliable multiplexing of signals between the new and existing electronics must be implemented.
  - Long term evaluations of the new modules will be performed.

---
Product general
Specifications
It is important to understand what exists now and have a detailed specification for the new system.
Specification documents:
  - “Requirements for the Booster LLRF DDS Module”, Beams-doc-2828-v4.
  - “Mathematical Description of the Booster LLRF Controls”, Beams-doc-2974-v2.
  - “Implementation of the Paraphase Curve in the BGDSPM”, Beams-doc-1289-v2.
  - “Characterization of the Fast Phase Detector in the Booster LLRF System”, Beams-doc-3367-v1

---
More Specifications
Other Sources for System Requirements
  - Links for “Papers” and “Presentations” on the Booster www page, http://www-ad.fnal.gov/proton/booster/booster.html
  - Historical documents:
    - L.C. Teng, “Booster Low-Level RF Feedback System”, NAL TM-311, 1971.
    - C. Kerns, et.al., “New Low-Level rf System for the Fermilab Booster Synchrotron”, FNAL TM-1447 0331.000, March 1987.
    - These documents reference others.

---
Existing LLRF System
Examine prints of system block diagram

---
Acceleration Phase Lock Loop

---
Phase Feedback Time Delay
(Latency)
From L.C. Teng 1971 (TM-311) the acceleration phase lock loop is expected to remain stable as long as the phase loop delay remains below	3 microseconds.
This delay in the existing system is estimated at 1.48 microseconds.
Digital data processing and digital signal synthesis will add latency.
  - ADC digitizer latency = 0.100 microseconds.
  - Processing latency = 0.100 microseconds.
  - DDS (DAC) output latency = 0.170 microseconds
Processing latency should remain below the 1 microsecond update rate

---
Product
Frequency and Phase
Block Diagram

---
Product
AD9910 Evaluation
1 us update of frequency and phase for all channels is achievable.

---
Product
DDS VME Module
Early Layout Estimate

---
I/O Specification (initial)

---
Integrating More Controls

---
Dual Phase Detector

---
Possible MI Phase Lock Approach

---
Another Trial
Dual phase detector used in a feed forward application.