Pre-injector Upgrade Updates
(29 Sep – 13 Oct 2010)
C.Y. Tan
13 Oct 2010

---
Storage Area of our documents
\\Beamssrv1\booster.bd\public\RFQ Project

---
Source Status

---
35 kV extraction

---
Pulser with 2 caps

---
LEBT Status

---
MEBT Status

---
RFQ Status
- PA being assembled.
- Schempp (05 Oct 2010)
  - Received PARI debug file
    - Differences between my output and his. Needs investigation.
    - Output energy is 760.8keV and not 750keV. Why?

---
Right vs Wrong Energy
Right Energy
Wrong Energy

---
Test Stand
- Room has been cleaned up.
  - Beam line layout in progress
    - Water – Bob Slazak
    - Electrical – Jim Ranson
- Need to test LEBT before RFQ connection
  - Wires, toroids at the end of the LEBT, same position as the RFQ.
- Design diagnostic line.
- Are drawings from Schempp sufficient to build table?

---
Test Area

---
Instrumentation
Vic will give status.

---
Safety
When can the beam line layout in test area be done?

---
Controls
Elmie has been asked to make the first pass at putting in the required monitoring devices for the RFQ.

---
RFQ reminders
- Schempp is vendor
  - Make sure that the vanes are cleaned! See ISIS email.
    - Some cleaning details supplied by ISIS.
  - Review and verify on site mechanical design and construction (already in contract).