## Slide 1: Booster Magnet Status
How Many Magnets Operational?
Spares Situation?
General Condition?

## Slide 2: What makes up the Booster? (Magnet wise, that is . )
1 – 400 MeV transport line.
  8 Bends (including Chop and Lam), 16 Quads, 17 H & 15 V Trims.
  – Linac Beam Dump transport lines.
  1 Spectrometer, 2 Quads, 3 H & 3 V Trims
    1 – Combined Function, 15 Hz, 8 GeV Synchrotron
      96 Gradient Magnets, 48 Trims (H,V,Q, SQ,S, SS), 6 Oct, 10 Kickers
      4 Dogleg, 1 Septum, 3 OrBumps, 3 Bexbmps
1 – 8 Gev transport line.
    The Proton Source is responsible for the first ~110 meters of the MI8 Beamline.
      10 Quads, 7 Dipoles, 6 H & 4 V Trims (a mixture of styles)
    MI8 Dump Line.
      3 Kickers, 1 Septum, 1 H & 1 V Trim

## Slide 3: 400 MeV
400 MeV Line | Concern | Number in Use | Task/Solution
Chopper | No spare | 1 | 1 spare HV terminal, designed to be repaired in place. 15 hz capable
Lambertson | None | 1 | 1 New spare stored in Linac enclosure
Loma Linda Quads | None | 8 (2) | 2 spares
Green Quads | None | 8 | 4 spares
MH1, MH2 | None | 3 | 3 spares, one mounted on stand
MV1, MV2 | None | 2 | 4 Spare coils plus complete spare magnet is being rebuilt from old MH1 (requires new poletips, beampipe and LCW manifolding.) Coils can be replaced in place, has been done.
Trims | None | 12 | 3 Spares
Spectrometer | None | 1 | Spare Coils Built-in
TOTAL Operational |  | 38 | 

## Slide 4: Accelerator
Booster | Concern | Number in Use | Task/Solution
Gradient Magnets | 96 operational/ old / rad damaged? /mechanical damage . Only failure modes to date are vacuum and external LCW leaks. Never any coil insulation failures. Before 1973 there were some"?" ceramic insulator failures and some magnets were changed out. | 96 | Prepping spares -- Short term: 1 of each class of magnet to be electrically tested and put under high vacuum. -- Long term: prep, test and put under high vacuum as many as can be made into operational spares,. -- 15 hz capable. 3 - presently under high vacuum 2 – “D” magnets 1 – “F” magnet 5 - presently under rough vacuum
Trims | None | 48 | All new Spares 15 hz capable.
Total Operational |  | 144 | 

## Slide 5: Injection / Extraction
Injection/Extraction | Concern | Number in Use | Task/Solution
Orbump Magnets | None | 3 | 2 operational spares under high vacuum , a third had had a vacuum leak repaired, 15 hz capable.
Extraction Septa, MP02 & MP03 | None | 2 | 2 tested spares, 1 under high vacuum, the 2nd will be put under high vacuum , 15 hz capable.
Dogleg Dipoles | None | 4 | 8 spares in storage
VBC0 | None | 1 | 1 Tested spare in storage
VBC1 | None | 1 | 1 Tested Spare in Storage
EDWA dipoles | None | 4 | 1 spare in storage
Quads | None | 9 | Pbar SQA - SQE style, spares exist
Kicker Magnets | Radiation Damage to Insulation | 13 | 8 new spares, TD ready to build more. 15 hz capable.
Total Operational |  | 35 | 

## Slide 6: Concerns
‘Useable’ Gradient Magnet Spares
Have 2 presently under high vacuum, 1 under rough vacuum.
Two under going repair at Tech Div. IB2.
Have devised workable skin leak repair
Developing replacement bellows/flange
Acquired 8 each, US and DS Candy Cane assemblies
Extraction Kickers
Primary hard failure due to radiation damage to insulator (potting material).
Extraction Septa
  Have had 1 failure – no autopsy done, magnet too hot to work on.
  MP02 and MP03 PS’s modified to reduce voltage to ground stress

## Slide 7: Conclusions
Present Condition | After Gradient Magnet Spare Work
Bad | Bad
S0-So | S0-So
Reasonable | Reasonable
Good | Good
Excellent | Excellent

## Slide 8: Backup Slides

## Slide 9: Radiation Dose to Gradient Magnets
Gradient Magnet radiation dose
The Booster has never lost a gradient magnet due to coil failure.
  (No turn-to –turn or pancake to ground shorts. Insulator failure & glow discharge arcs in the region of the insulator due to marginal vacuum)
Yet this remains a source of concern since some of the magnets have seen very high levels of beam loss and the losses around the extraction region and collimator regions continue to be very high.
Insulation specifications - Engineering Specification -- 0322-ES-2157-A -- Figure 4: Copy of Magnet Specification Insulation - Epoxy

## Slide 10
‘ Radiation issues In the Fermi lab Booster Magnets*
E. Prebys#, Fermilab, Batavia, IL 60510, U.S.A.
Conclusions
Our studies indicate that the epoxy resin used as an insulator in the magnets of the Fermilab Booster may have received integrated radiation doses as high as 100 kGy over the life of the machine. The increased proton flux needed by the neutrino program could mean that some areas will receive as much as 1 MGy over the next ten years.
While these numbers are within the range where epoxy resins have been shown to work in the past, they are definitely at a level which causes some concern, particularly given our lack of details about the exact epoxy used. It is therefore extremely important to keep beam loss at a minimum in the coming years and to try to keep it as uniform as possible to avoid excessive localized dosage.
Further study is warranted, and should a magnet fail for other reasons, it will be iportant to inspect the condition of the epoxy. ‘