Plans for a New Front-End for the existing FNAL Linac
Linac Frontend Upgrade Report
C.Y. Tan
8 Dec 2010
Proton Source Retreat

---
People (Additional Help – Needed/Requested)
People (Additional Help – Needed/Requested)
AD people:
  - W. Pellico (head of proton source), C.Y. Tan, J. Lackey, D. Bollinger, K. Duel, R. Riley, V. Scarpine.
TD people:
  - G. Velev, V. Kashikhin, A. Makarov
Thanks to BNL pre-injector group
  - J. Alessi, D. Raparia, M. Okamura, V. Lodestro.

---
Present Injector – Vintage 1968 Hardware
Present Injector – Vintage 1968 Hardware
Magnetron Source
35 keV ribbon beam
Current about 50-60mA
Cockcroft Waltons
750keV
Current about 45 - 55 mA
MEBT section
Quads and buncher before Tank 1
Dipole to accommodate another H- source + Cockcroft Walton

---
Reasons for Upgrade
Reasons for Upgrade
The components are getting harder to maintain
  - Critical personnel have retired.
  - Components getting harder to find and replace
    - Critical failure of I- column in early 2010 which required a rebuild.
- As system ages, more time and attention required to maintain reliability of system.
- Going to RFQ system should increase beam quality and system reliability.
  - Very good results from BNL when they switched from Cockcroft-Walton to RFQ system. Done in 1989. (21 years late to the party)

---
Quote from D. Lowenstein (BNL)
“We have been very pleased with the operational reliability of the BNL RFQ. It has worked very well since day one. In fact, the
downtime attributed to the RFQ has been negligible (less than 10 hours) since it was commissioned.” – D. Lowenstein (former chairman of C-AD) , BNL. Source: Fermi Today 30 Nov 2010 edition.

---
Objectives
Objectives
- This is not an R&D project
- Copy as much as possible from an existing injector
  - BNL injector is used as basis of design.
Use as much as possible existing infrastructure, technology and expertise.
  - Convert slit magnetron source to round magnetron source
    - BNL style source. Very good reliability and performance > 90mA at 500 us, more than 6 months before any change required.
    - 750keV RFQ 60mA 200MHz (not technology limited)
Better performance
  - At least 10-15% improvement in efficiency to Booster.
Support future operations – Nova, Mu2E, MicroBooNE, G-2, RunIII

---
Overall Design
Overall Mechanical Design
BNL MEBT (old design)

---
Test Stand Setup

---
Why Round(Dimple) Source
BNL improvements in magnetron power efficiency
Cathode	H- (mA)	Arc I (A)	Arc V (V)	Pwr effic (mA/kW)	Lifetime (months)
Slit/flat	50	150	150	2.2	N/A
Slit /grooved	50	50	150	6.7	N/A
Circular/dimpled	100	10	150	67	6-9 months
FNAL magnetron power efficiency
Cathode	H- (mA)	Arc I (A)	Arc V (V)	Pwr effic (mA/kW)	Lifetime (months)
Slit/flat	50	150	150	2.2	N/A
Slit /grooved	50	50	120	8.3	3.5 (average)
Cathode material blocking the cesium inlet opening in anode
We have to run high arc currents ~ 50A in order to get 50mA+ of H- out of the source for Linac operations. This causes increased cathode erosion and reduced source lifetime.
BNL needs only 10A of arc current to get 100mA of H- beam current. Their cathode erosion is greatly reduced which leads to longer source lifetimes.
New anode showing cesium inlet

---
The H- Source
The H- Test Source
H- source test source (modified from HINS) source at 35keV
40mA at extraction
Wrong cone.
Should get 90mA at 35kV extraction.
Scraping
Volts (*103)
Extractor

---
Chopper
Chopper
Suggested by D. Raparia (BNL)
Present experiments have shown that Einzel lens will not spark at 37kV with or without H-
Reason for chopper
Want rise/fall time of H- < 1us.
Want control of length of pulse.
Want to neutralize the LEBT before chopping.

---
First results
Green: Faraday cup
Red: toroid
Blue: Extractor voltage
Magenta: chopper pulser
16 averages
Chopper letting beam through
Arc current off

---
Zoomed in view
Slow rise from scraping
Ranges from 2 to 20us
Ringing from mismatch
Fast rise < 50ns
20A
15mA
15A
10mA
5A
~5mA
Note: no solenoidal focusing. Beam is blowing up from space charge

---
LEBT
LEBT
LEBT < 1.2 m long
2 sources for reliability.
Will probably use Xe gas neutralization of H-
Solenoids are being built right now. Delivery expected by early 2011.

---
RFQ
RFQ
750keV RFQ.
60mA beam current
1.3m long.
Rod design.
Alwin Schempp designer
Expected delivery, early 2011

---
RFQ Params
60mA beam
1. Input:  = 1.5, =5.1 cm/rad =210 pi mm mrad
2. Output:
  - x = -0.18, x = 12.5 cm/rad, x (rms norm)= 0.37
  - y = 0.07, y = 5.5 cm/rad, y (rms norm)= 0.35
  - z = 0.21, z = 1170 deg/MeV, z (rms unnorm) = 0.14  MeV deg.

---
RFQ Tank Waiting to be Copper Plated
“Grooves” are an artifact of compression. Not there in real life.

---
MEBT
1. The beam is approximately round coming out of the RFQ
  1. Use doublets to focus the beam before and after buncher
  2. Must be very short from BNL experience
  3. Use some of BNL's design
  4. Quads are a problem because they run very hard.
    1. 2 designs available
      1. BNL quads are 45mm (~55 physical length) water cooled.
        1. Don't know whether can run at our rep rate of 15Hz
      2. FNAL quads are 70mm (105mm physical length) but includes dipole correctors and air cooled.
      3. Both give comparable capture at the end of Tank 1
      4. Note: work is being done at TD to shorten the quads to ~55 physical length and use water cooling with built in dipoles.

---
MEBT Quad Strengths
1. FNAL doublets (using 70mm magnetic length)
  1. Quad1: 26.8 T/m
  2. Quad2: 22.9 T/m
  3. Quad3: 17.6 T/m
  4. Quad4: 16.7 T/m
1. BNL doublets (using 45mm magnetic length)
  1. Quad1: 54.0T/m
  2. Quad2: 47.3 T/m
  3. Quad3: 40.3 T/m
  4. Quad4: 37.9 T/m

---
MEBT
MEBT Quads
BNL style
FNAL style

---
Buncher
Buncher
Pictures from BNL. Thanks to M. Okamura (BNL).

---
FNAL Doublets
After buncher
Exit of RFQ
Capture is 94.2% at end of Tank 1
Tails are much longer than when we use BNL doublets
Before Tank1
End of Tank1

---
FNAL Trace3D
Transverse horz barely fits in beampipe

---
BNL doublets
After buncher
Exit of RFQ
Capture is 97.5% at end of Tank 1
Before Tank1
End of Tank1

---
BNL Trace3D

---
Conclusion
Conclusion
  - Goal is to complete testing of injector before the shutdown of 2011.
    - Installation will probably take 3 months in 2012.
  - Lots of things to do before then
    - Complete commissioning of the H- source
    - Complete testing of Einzel lens as chopper.
    - Check and condition buncher.
    - Check and condition RFQ
    - Have test stand ready for beam test
    - Build and complete solenoids.
    - Build and complete quadrupoles.
    - Choice has to be made between BNL and FNAL quads