## Slide 1: Laser Notcher Status
Dave Johnson
PIP Meeting
June 26,2012

## Slide 2: Laser Notcher Location Update
Relocated laser notcher from 400 MeV area to 750 keV MEBT just after the RFQ.
  Smaller (shorter) interaction cavity
  Laser system located close to interaction cavity
  Does not require external H0 dump
  Minimized beam line & magnet modifications
Laser system same as 400 MeV option
  Same pulse energy (2mJ) fewer reflections

## Slide 3
Laser Notcher
1.25 ns
RFQ
Tank 1
Laser Notcher in the 750 keV MEBT
9.6 mm
Quads

## Slide 4: 750 keV Notcher Insert Concept
RFQ flange
Cavity diameter 33.77 mm
Cavity length 25.65 mm
29.7 mm
HR mirrors
Bellows
1.92” (48.7 mm) Max
H- envelope (<10 mm H&V)
9.6 mm
1.1 mm
Laser Beam
Plan View
Laser dump
AR viewport
9.5 mm
9.5 mm
Reduce RFQ flange thickness from .5 to .3” OR increase thickness to create a laser transport through the flange
Register the mirror holder
to end of RFQ
Rectangular beam pipe

## Slide 5: Program Goals
2012
  Demonstrate the creation of low intensity optical pulses
    David Johnson, Andrea Saewert, Vic Scarpine, Jinhao Ruan (consultant)
  Build a prototype transverse pulse shaping system and optical cavity
    Todd Johnson
  Create a viable preliminary design for the vacuum chamber
    John Sobolewski (M/S co-op) (Bradly Durant/Kevin Duel)
2013
  Demonstrate the creation of optical pulses through the fiber amplifier chain
  Integrate the final pulse generator into the system
  Build a prototype vacuum chamber to integrate the optical cavity
2014
  Build final vacuum chamber integrating the pulse shaping and optical cavity
  Integrate final free space amplifier into system
  Be ready for installation of system early in 2015.

## Slide 6: Projected FY2012 Expenses
Modulator components $12,750
  Photline
Seed source < $10 K
  Innovative Photonics/NP Photonics
Optical components ~ $5K
  Spherical/clynderical optics, mirrors, optical holders,etc
Misc. components ~ fewK
  Chassis, fiber connectors, isolator, dc power supplies
Test equipment ~ $5K
  Fast photodiode detector, IR scope,
Pulse generator ~$20K
  Picosecond Technologies