## Slide 1: Linac Laser Notcher Status
David Johnson and Todd Johnson
PIP Meeting
October 10, 2012
Beams doc 4237

## Slide 2: Basic Components
Pulse Generator/timing system
Laser system update
Beam shaping update
Optical cavity update
Vacuum interface update
Control system (LabView?)
Reduce losses in Booster tunnel generated by the creation of the Notch
Create notch at 750 keV
Utilize photo-neutralization (laser system to match temporal structure of H-
Prototype for fast bunch by bunch chopping system
Reminder: The purpose of the Linac Laser Notcher:

## Slide 3: Location Status
Initial concept utilized 400 MeV area.
  Required significant beam line changes
  Required new H0 absorber (beam dump)
Back in April decided to focus on 750 keV
Laser Notcher

## Slide 4
MS co-op (John Sobolewski) started looking at potential designs of the vacuum system interface. To be continued at a low level effort by MS (co-op)/University collaboration, or other resource.
AR viewport
To reduce laser power: create laser pulse to match spatial and temporal structure of H- beam
And increase interaction time for photo-neutralization through use of zig-zag cavity.
9.6 mm
1.1 mm
Laser Beam
RFQ flange
Bellows
1.92” (48.7 mm) Max
Plan View
Laser dump
29.7 mm
9.5 mm
Cavity diameter 33.77 mm
Cavity length 25.65 mm
HR mirrors
Register the mirror holder
to end of RFQ flange
Rectangular beam pipe
750 keV Notcher Insert Concept
(In flange option)

## Slide 5: Expected Beam Dimensions
Phase space simulation at end of RFQ (figure 4.40 of 750 KeV Upgrade Plan)
Trace 3D back calculation of beam size at exit of RFQ based upon emittance measurement at 178 kW power August 9, 2012 CY Tan.
Laser beam vertical profile (1/e2) ~ 5 mm.
Initial design assumed that the vertical laser beam dimension of 1 cm.
Beam measurements indicate vertical laser size could be reduced to 6 mm
This is a variable parameter in the beam shaping optics.

## Slide 6: Burst mode seed pulses to Fiber Amplifier followed by Free Space Amp
l1=1064nm
120 mW CW
SW=0.1 nm
10 GHz Mach-Zehnder
Modulator
Pulse Generator
Amplifier, Timing
PM Fiber
Lins ~5dB
Li~1.8dB
15 Hz
Pockels cell
Updated 10/3/2012
Generate 24 us burst at 15 hz
TRANSPORT BEAM SHAPING OPTICS &
OPTICAL CAVITY
Fiber Pre-Amp
Fiber Amp 1
Fiber Amp 2
Free Space Amp
Output modulator/Input fiber pre-amp:
201.25MHz pulses (1.25 ns pulse), 458kHz burst
 | EP | PP | P200* | P450*
FPA IN | 26 pJ | 21 mW | 5.3 mW | 1243uW
FPA OUT G= 20 dB | 2.6 nJ | 2.1 W | 0.53 W | 14.3 mW
FA 1 IN | 1.8 nJ | 1.4 W | 0.44 W | 10 mW
FA 1 OUT G=23 dB | 360 nJ | 288 W | 972W | 2.0 W
FA 2 IN | 300 nJ | 240 W | 60 W | 1.6 W
FA 2 OUT G=11.5 dB | 4.2 uJ | 3.4 kW | 1.1 kW | 23 W
FSA IN | 4.0 uJ | 3.1kW | 795 W | 22 W
FSA OUT G=27-29dB | 2.0 mJ 3.1 mJ | 1.6 MW 2.5 MW | 400 kW 630 kW | 11 kW 17 kW
Clean up filter
Isolator
Line filter
Free
Space
Grumman CEO DPSS OEM
Diode + TC
controlled
*Notch 12 bunches -> 60 ns
10 notches/linac pulse

## Slide 7: The Plan (as of today)
Due to lack of major M&S funding for FY13, we accelerated purchases (with available FY12 funding) planed for FY13 and moved the schedule forward.
To date we have purchased:
  Seed laser and controller
  Modulator system (borrow pulse generator)
  First 2 stages of fiber amplifier system ***
  Fiber to free space port
  Beam shaping optics (532 nm and 1064 nm)
  Optical cavity components (532 nm and 1064 nm)
What would we like to accomplish this year (FY13) ?
  Certify operation and parameterize the following:
    Optical Pulse Generator
    1st two (of three) stages of the fiber amplifier system
    Beam shaping and transport optics with 532 nm laser
    Beam shaping and transport optics with the output of the (1st 2 stages) fiber amplifier system (IR)
    Prototype optical cavity (532 nm in fluorescent cell)
    Optical cavity with IR
  Demonstrate 15 Hz burst of the 201.25 MHz and 458 kHz QCW laser pulses with Pockels cell.

## Slide 8: Beam shaping and optical cavity tests

## Slide 9: Test setup
In order to evaluate the uniformity of the laser beam profile in the transverse cavity, a dye cell was employed. Water in a clear container is weakly doped with a fluorescent dye which absorbs 532nm from the test laser and re-emits at longer wavelengths, allowing any scattered portions of the primary beam to be filtered out and rejected from the analysis.

## Slide 10: Two initial approaches:
Fill aperture with a “staircase” of overlapping elliptical gaussian beams to present a uniform optical field to the ion beam.
Utilize a “PiShaper”; an optical device which converts a gaussian profile beam to one with a flat-top profile, to produce a vertically uniform beam which fills the aperture.

## Slide 11: Dye cell test setup
Laser &
Telescopes
Dye Cell
Analyzing camera

## Slide 12: Telescopes
The test optics consist of two variable magnification cylindrical telescopes and the PiShaper device.
The PiShaper function depends critically on proper input beam characteristics, so the first telescope is used to deliver an appropriately sized elliptical beam to the PiShaper. The second telescope is used to expand the 6mm output of the PiShaper to any desired vertical size up to 25mm.

## Slide 14
532nM laser
First telescope
PiShaper
Second telescope
Dye Cell

## Slide 15: Dye cell detail

## Slide 16: Response of the dye was tested to ensure linear behavior with varying primary beam intensity

## Slide 17
Aligning cavity mirrors in the dye cell with unexpanded beam

## Slide 18
Profile of unexpanded staircase trajectory
(Spiricon camera with 600nM lowpass filter)

## Slide 19
Beam expanded vertically with first telescope (no PiShaper)
and propagated in the overlapping staircase configuration

## Slide 20
Resulting profile of staircase configuration
(Spiricon camera w 600nM lowpass filter)

## Slide 21
Beam expanded through both telescopes and processed with PiShaper

## Slide 22
Profile of overlapping PiShaper output
(Spiricon camera with 600 nM lowpass filter)

## Slide 23
Single pass expanded PiShaper beam
(Fine adjustment of the input beam parameters will
reportedly remove much of the observed structure.)

## Slide 24: Conclusions
                Variable beam shaping telescopes performed as expected.
                The PiShaper is very sensitive to input conditions. Additional tuning is needed to take full advantage of this device.
                Both methods of producing a vertically uniform optical field in the zig-zag cavity showed promising results.