## Slide 1: Muon Campus Plans
Mary Convery
Accelerator Division, Muon Department
1/10/13

## Slide 2: Muon Campus layout

## Slide 3: Looking toward the Muon Rings

## Slide 4: View from Wilson Hall

## Slide 5: Thanks and disclaimers
Thanks in advance to everyone I “borrowed” content from
  including Russ Alber, Jerry Annala, Brendan Casey, Brian Drendel, Doug Glenzinski, Arkadiy Klebaner, Ioanis Kourbanis, Tom Lackowski, Nikolai Mokov, Jim Morgan, Hogan Nguyen, Chris Polly, Ron Ray, Dean Still, Steve Werkema, …
I have been involved with g-2 for a little over a year, and the broader Muon Campus planning for about 2 months
  I am not at all an expert on Mu2e

## Slide 6: Mu2e

## Slide 7: Mu2e
Muons regularly decay to electrons and neutrinos m- e-nenm
Mu2e will search for charged lepton flavor violation (mNeN)
  Neutrino flavor oscillations already observed
Conversion rate distinguishes between different theories
_
m
e
n
p
n
p
p
n
n
?
~
~
~
~
~
~
~
~
~
~
~
~
~
~
Sleptons Squarks
c
c
Gauginos
Not Yet
Thought
Of
Extra Dimensions
Super Strings
Super Symmetry

## Slide 8: Mu2e
Generate beam of low-momentum m-
Stop the muons in a target
  Aim to improve sensitivity by 104 over previous experiments
  requires ~1018 stopped muons
Stopped muons are trapped in orbit around the nucleus
  Using Aluminum target (nucleus):
    characteristic time tmAl=864 ns
    conversion-electron energy 104.97 MeV
    (maximum decay-e energy 52.8 MeV)
Extinction system (AC dipole) to prevent prompt background from out-of-time protons hitting production target

## Slide 9: Mu2e Apparatus
about 75 feet end-to-end
Production
Target
Stopping
Target
Tracker
Calorimeter
Collimators
Production
Solenoid
Transport
Solenoid
Detector
Solenoid

## Slide 10: Mu2e Apparatus
Production
Solenoid
Transport
Solenoid
Detector
Solenoid
Proton Beam
Production
Target
Stopping
Target
Tracker
Calorimeter
Collimators
Proton Beam delivered to the production target via the former Pbar beamlines followed by an external beamline

## Slide 11: Mu2e Apparatus
m-, p-
Production
Target
Stopping
Target
Tracker
Calorimeter
Collimators
Production
Solenoid
Transport
Solenoid
Detector
Solenoid

## Slide 12: Mu2e Apparatus
e-
Production
Target
Stopping
Target
Tracker
Calorimeter
Collimators
Production
Solenoid
Transport
Solenoid
Detector
Solenoid

## Slide 13: Mu2e schedule

## Slide 14: g-2

## Slide 15: The anomolous magnetic moment and g-2
g2 but higher-order corrections
  QED, EW, hadronic, new physics?
proposed exp. precision
Currently ~3s discrepancy between theory and experiment
New muon g-2 experiment at Fermilab expected precision could yield ~5s

## Slide 16: Measuring g-2
  Polarized muons in magnetic field precess with Larmor spin precession frequency
  Measure g-2 using cyclotron
  Requires precise measurements of and of the magnetic field
g = 2
g > 2

## Slide 17: Measuring
One more trick:
  Polarized muons in storage ring with vertical focusing by electrical quadrupole field
  At magic momentum pm = 3.094 GeV/c (g = 29.3), g-2 precession frequency wa independent of electric field
Distribution of decay electrons as function of time
Intensity at a single detector station shortly after injection
Phys. Rev. D73 (2006) 072003

## Slide 18: g-2 apparatus
Reusing storage ring from BNL g-2 experiment
New calorimeters and straw-tube tracking

## Slide 19: Planned improvements
Rebunch high-intensity beam into multiple bunches to lower the instantaneous rate
Increase the detector segmentation to reduce the instantaneous rate in a given cell
Modify secondary beamlines to store as many muons from pion decays as possible
Remove pions and protons from muon beam to prevent hadronic flash in calorimeters
  Allows analysis of more (earlier) decay e+
  Longer beamline for pion decay
  Let heavier protons separate in time from pions/muons and kick them out
Improve beam dynamics in storage ring
Improve storage ring field uniformity and the measurement and calibration system

## Slide 20: g-2 schedule
Preparing for CD1 review this spring
MC1 building complete early FY14
g-2 storage ring ships early FY14
Ring reassembly starting FY14
Cryo ready to cool ring early FY15
Ring magnetic field shimming starting mid FY15
Recycler and Muon beamline work FY14-15
New beamline enclosure beneficial occupancy mid FY15
Beam to g-2 early 2016

## Slide 21
Beam to Mu2e
Primary (8 GeV) proton beam resonantly-extracted from Debuncher
Extinction of out-of-time beam
Original plan for increased flux involved “threading” Mu2e batches between NOnA batches, stacking proton bunches in Accumulator, and rebunching / resonant-extraction in Debuncher
Beam to g-2
Rebunch primary (8 GeV) protons so that rate in detectors is not too high, bunch length < ring revolution time of 147ns
Create 3.1 GeV secondary pions off a target
Beamline long enough for ~all pions to decay
Capture 3.094 GeV (“magic momentum” muons)
  aim for 40p acceptance
Limit secondary pions and protons making it into g-2 storage ring (cause “hadronic flash” in calorimeters)

## Slide 22: Original Mu2e and g-2 plans for former Pbar beamlines
8 GeV protons bypass target
Abort
8 GeV protons to Accumulator
AP3 line connects to Accumulator
stacked proton bunch to Debuncher
stacking of p bunches in Accumulator
8 GeV protons to target (rebunched in Recycler)
3.1 GeV secondaries to Debuncher (need high quad density to capture decay muons)
new connection Debuncher to AP3
bring 40p beam back thru target bypass
to g-2 ring
resonant extraction to Mu2e target

## Slide 23: g-2 near Mu2e in “Muon Campus”
Locating g-2 experiment near Mu2e has advantages
  Both g-2 and Mu2e circulate in same direction
    No need to switch polarity, just energy
    Frees some magnets in AP2 line for reuse, no conflict with Mu2e plans for primary beam abort in AP2
    Can use Mu2e abort to remove proton contamination from g-2 secondary beam
  New building location also much better
    Old location jammed between road and berm
    Utility corridor to be rerouted
    Don’t have to pass g-2 secondary beam back through AP0
  Can share cryo and other infrastructure
  Time-dependent stray magnetic fields at g-2 ring smaller near Booster than near Main Injector

## Slide 24: Mu2e Accelerator Task Force Cost Savings
6  2
Booster
Batches
Re-bunch
in RR
Bypass Accumulator Ring
Reduced Shielding
Relaxed timing specs, no threading between NOvA batches
Synergy with g-2
Eliminate kickers, RF, power, cooling loads
Reuse magnets
Trade Mu2e rate for run time (3 yrs running vs 1 yr)
Elimination of Accumulator removes almost every g-2/Mu2e conflict
Over $100M in savings in the combined program

## Slide 25: Muon Campus beamline plan for Mu2e and g-2
(where M2 line joins M3 line not yet finalized)
3 GeV p,p+,m+ to Delivery Ring for g-2
8 GeV protons to Delivery Ring for Mu2e (target station bypass)
3 GeV p,p+,m+ to M3 line for g-2 (“p decay line”)
8 GeV protons to target for g-2
8 GeV protons to M3 line for Mu2e
M3 line connects to Delivery Ring (Debuncher)
After ~5 turns, p separated in time from m+, kick into abort
Primary abort for Mu2e
3 GeV p,p+,m+
After ~5 turns essentially all p+ decayed
m+ to g-2 ring
Extract m+ for g-2
Resonant extraction for Mu2e
p to Mu2e target

## Slide 26: Shared infrastructure
Any shared infrastructure needs to be ready in time for g-2
  Make use of Accelerator Improvement Projects (AIPs) and General Plant Projects (GPPs)
  MC-1 building houses cryo refrigerators and beamline power supplies in addition to g-2 storage ring / future expts (GPP)
  Cryo work moves to AIP
  Extraction-line tunnel moves from Mu2e to GPP
  First part of extraction line moves from Mu2e to g-2
  Recycler work was on g-2 project (g-2 drives specs), later moved to AIP at recommendation of Mu2e CD-1 review committee
  Proton abort and other Delivery-Ring work moved to AIP
  P1, P2, M1 line 8-GeV aperture improvements moved to AIP
  Controls and common instrumentation(?) on g-2 project
Yes, partly this makes Mu2e look less expensive, but there is also a limit on the total cost of the Muon campus program

## Slide 27
Recent modifications to Muon Campus plan
Program
Coordinator
M Convery
likely scope change
need additional AIP to cover costs?
AIP’s and GPP’s have hard cap at $10M

## Slide 28: Packaging into AIPs/GPPs
Actually the packaging of the work is still in flux
  Except for MC1 building GPP which is already in progress
DOE recommendation resulted in acceleration of Mu2e civil construction schedule, had to shuffle work between Mu2e and other Muon Campus projects
AIPs and GPPs have a hard cap of $10M, don’t include conceptual design
  As designs are becoming more mature and in some cases work is pushed later, cost estimates indicate that the work may not fit in the planned packages
Internal AD review later this month to make sure nothing is missing between all these packages and to look for ways to reduce costs
Following the review, we will propose how to package the individual pieces into AIPs and GPPs

## Slide 29: Rough funding plan for GPPs and AIPs
The additional site power feeder that was part of site-prep GPP ($1M) is not included here, may be needed in 2017 or 2018
on critical path for g-2
on critical path for g-2
longer lead time for RF

## Slide 30: Protons to the Muon Campus

## Slide 31: Protons available
(Mu2e and g-2 cannot run simultaneously)
Main Injector
Energy
Booster
Cycles
Protons to NOvA
Protons to g-2
Protons to MicroBooNE
{
Need 2 Booster cycles
to manipulate g-2 beam
in Recycler
Protons to Mu2e

## Slide 32: Re-bunching beam in Recycler
53 MHz bunches (4x1012 protons) reformed into 4 bunches (1x1012 protons) at 2.5 MHz
  Reduce pile-up in detector
  Build new cavities for 2.5MHz system
g-2 needs beam pulses out of Recycler not longer than ~100ns
  Muon storage ring revolution time 147ns
  Balance efficiency, momentum spread, and longitudinal extent
  Achieve pulses with 95% of beam within 120ns
Beam pulses should be separated by ~10ms for the muons to decay in the g-2 storage ring and data to be recorded
Mu2e specs are less stringent than g-2

## Slide 33: Recycler AIP
Allows 8 GeV proton beam to be rebunched in the Recycler and extracted to the P1 line for transport to experimental areas
  2.5 MHz RF for re-bunching beam
  Extraction kickers
  Beamline connection from Recycler to P1 line
  MI52 building extension for kickers (civil – move to separate FESS project?)
RF cavity production
  Cavities must have active cooling
  Reuse ferrites from MI coalescing cavities
  Labor intensive
  7 RF systems (cavities + PA’s) for Recycler
  2 cavities for Mu2e to be installed in the Delivery Ring
33

## Slide 34: Simulation of rebunched beam
E-E0 (MeV)
RF voltage (kV)
0
20
40
-40
-20
95% contour
96
-96
0
-4 -2 0 2 4
120 ns
-4 -2 0 2 4
Counts per bin
95% capture efficiency, 95% of captured beam w/in 120ns
phase (1 deg = 31 ns)
phase (1 deg = 31 ns)

## Slide 35: Beam distributions from test in Main Injector
Very good agreement between simulations and beam data at low intensities
Beam loading will be much less of an issue in Recycler
10 Booster batches
~4x1012
1 Booster batch
~0.4x1012

## Slide 36: Recycler extraction kicker system
2 new kicker magnets of the new RKB style designed for ANU
Re-use the beam tubes from the recently decommissioned Recycler kicker magnets
Re-use the PFLs from the Recycler kickers
Build two new 25 Ohm loads capable of up to 250 W ave power
Fluorinert cooling skid to cool the loads
  Extend existing building at MI-52 for kicker power supplies
Kicker angle | 1.37 mrad
Flattop | 200 nsec
Field Rise Time | 120 nsec
Field Fall Time | 400 nsec
Average Rate | 12 Hz
Burst Rate | 100 Hz
ANU RKB Kicker Magnet

## Slide 37: Transporting proton beam to Muon Campus
New connection from Recycler to P1 line

## Slide 38: MI-52 Extraction Region
P1 Line
MI
RR

## Slide 39: Muon Campus beamlines

## Slide 40: New Mu2e and g-2 plans for former Pbar beamlines
(where M2 line joins M3 line not yet finalized)
3 GeV p,p+,m+ to Delivery Ring for g-2
8 GeV protons to Delivery Ring for Mu2e (target station bypass)
3 GeV p,p+,m+ to M3 line for g-2 (“p decay line”)
8 GeV protons to target for g-2
8 GeV protons to M3 line for Mu2e
M3 line connects to Delivery Ring (Debuncher)
After ~5 turns, p separated in time from m+, kick into abort
Primary abort for Mu2e
3 GeV p,p+,m+
After ~5 turns essentially all p+ decayed
m+ to g-2 ring
Extract m+ for g-2
Resonant extraction for Mu2e
p to Mu2e target

## Slide 41: Aperture improvements in P1, P2, M1 lines
120 GeV Pbar production
MI to Target Station
8 GeV protons
RR to Target Station
MI-52 Lam. / V701 C-magnets (?)
V714 C-magnets
Tev. F0 Lambertsons
F-17 C-Magnets
HV100 dipoles
HV102 dipoles
HT105 trim
need changes to final focus for g-2

## Slide 42: M2 and M3 lines
M2 line
  Secondary beamline for g-2
  Add quadrupoles to create a regular lattice with smaller b functions to capture more muons from decays
  Beamline magnets from BNL g-2 experiment, also from Accumulator
M3 line (target bypass section)
  Acceptable for Mu2e as is but must match to incoming M2 line for g-2
M2 to M3 connection
  Need connection that accommodates Mu2e 8 GeV proton beam down M3 while preserving small β functions for g-2

## Slide 43: M3 line into Delivery Ring
New connection to Delivery Ring
  Two elevation changes and a 5 horizontal bend
  Confined area for magnet supports in area over Delivery Ring
  Need enough room between DR and M3 to allow use of existing pbar magnets
  Match injection into DR and acceptance must be at least 40p for g-2
AP3 line
Debuncher

## Slide 44: Delivery Ring Modifications
DR aperture improvements
  Removal of unneeded devices such as stochastic cooling tanks
DR abort
  Beam abort for Mu2e
  Proton removal for g-2
    Need a fast-rise kicker
Electrical infrastructure improvements

## Slide 45: Delivery-Ring injection/extraction strategy
Keep injection and extraction regions separated (D30 straight)
Maximum flexibility between g-2 and Mu2e at least expense
  Reuse existing equipment
  New devices should be based on existing designs where practical
Work around Mu2e extraction devices
  Resonant extraction more difficult to design
  Requires use of Lambertson
  Placement of extraction channel defined by resonantly extracted beam
  Electrostatic septa added for Mu2e operation
Maximizing acceptance for g-2 (40p)
  Kicker placement
  Large vertical(horizontal) bump across injection(extraction) region
    Motorized quadrupoles (existing) used to create bump for g-2
  C-magnet used in addition to magnetic septum(Lambertson)
  Some specialized large aperture quads (existing)

## Slide 46
g-2 operation and Mu2e commissioning
Horizontal bend (5)
Injection kickers
Injection Septum
and C-magnet
Extraction Lambertson
and C-magnet
Extraction kickers
Vertical bends
Vertical bend

## Slide 47
Dual running mode configuration
Horizontal bend (5)
Injection kickers
Injection Septum
and C-magnet
Extraction Lambertson
and C-magnet
Vertical bends
Vertical bend
Extraction septa (Mu2e)
Extraction kicker (g-2)

## Slide 48: Extraction lines
M4 and g-2 beamline design in progress
g-2 line splits from M4 line in the middle of the left bends
Momentum collimation will be integrated into Left Bend
g-2 line is roughly 50 m long
Vertical dogleg will make elevation change to g-2 storage ring
  BNL magnets and other components will populate most of the g-2 line
Final focus and matching to Storage Ring will be designed in collaboration with Ring Team
Split between the M4 and g-2 lines

## Slide 49: Beamline enclosure and site plan
Details depend on beamline lattice which is not complete yet

## Slide 50: External beamline enclosure design
Main Injector type enclosure
  10 feet wide x 8 feet high (typical except near MC-1 where higher ceiling will be required.
  Painted walls and ceiling, sealed floor. Floor to have 3” cover over rebar to enable stand anchorage.
  Channel inserts walls and ceiling @ 8’ o/c. (no inserts 5’ from floor on aisle side)
Shielding
  16 feet of earth/concrete for M4 beamline. (w/ beamline 4’ from clg.)
  6 to 9 feet for g-2 beamline. Shielding needed within enclosure between MC-1 building and M4 / Delivery Ring.
Access for magnets is provided directly from Ring enclosure; lift provided for magnet installation. Shielded hatch provided for magnet installation / replacement.

## Slide 51: Beamline enclosure timeline
CUMULATIVE

## Slide 52: g-2 target station

## Slide 53: g-2 target station
Use existing Pbar target station at AP0
Fermilab expertise, existing spares, and radioactivity of target vault make it desirable to maintain current setup as much as possible
  Rotating, air-cooled target
  Lithium lens for focusing
  Pulsed magnet for momentum selection
Simulations indicate that the current setup can deliver the desired yield of ~10-5 pion/POT
  Conducted beam tests to confirm

## Slide 54: g-2 beam tests and simulations
Study plan
Expected number of particles
for 1x1012 protons on target (g-2 single pulse)
MARS simulation of target station
  g-2 mode: yield per POT: ~10-5 p+, ~2x as many protons, ~10-8 m+
G4beamline simulation of start of pion decay line (C Yoshikawa, Muons Inc)
120 | 8.9 | - | Stacking mode
120 | 3.1 | - | Change magnet strengths in secondary beamlines
8.9 | 3.1 | - | “reverse proton” mode beam to target
8.9 | 3.1 | + | Change polarity of lens, magnets in secondary beamline; g-2 mode
Step from stacking to g-2 mode
collimator
momentum-selection dipole
Chart: Start of AP2 line
| 120->8- | 120->3- | 8->3- | 8->3+
total | 10050000000 | 5475000000 | 49750000 | 222000000
pi | 8256160000 | 2557650000 | 48112600 | 99391200
e | 1633570000 | 2858200000 | 657168 | 788358
mu | 85013600 | 54502700 | 974816 | 1741120
p | 73669900 | 4792810 | 1051 | 120031000
proton
mom.
(GeV)
secondary
mom.
(GeV)
charge

## Slide 55: Results of beam test
Intensities track beam on target
Current monitor at beginning of AP2 line shows expected scaling from 1208-/120  3-
Ion chamber at end of AP2 line shows order-of-magnitude agreement with predictions: 109 particles for 120  3- and 107 particles for 8  3- and 8  3+ per 1012 protons on target
Protons on target (1012)
Ion chamber at end of AP2 line
SEM at end of AP2 line
SEM at mid of AP2 line
Intensity
Time
3
2.25
1.5
0.75
0
Beam profiles seen on Secondary Emission Monitors (SEMs)
Existing target and lens appear to provide sufficient yield
Smaller spot size on target will increase yield

## Slide 56: Lithium lens in g-2 mode
Higher pulse rate, more complicated cycle than for stacking
Will need new power supplies for lithium lens and pulsed magnet
1
2
3
4
5
16
120 nsec
10 msec
Pulse #
Cycle length 1.33 sec
Pulse separation
Bunch length
of 1 pulse
Begin cycle
End cycle
100Hz
920 msec
97.8 msec
~
~
6
7
8
9
10
11
12
13
14
15
30Hz
Train propagation
Lens pulse length 400 µsec
822 ms
97.8 ms

## Slide 57: Lithium lens modeling and testing
Lens ANSYS model predicts higher temperatures and stresses for g-2 but fatigue parameters are better
  Less difference between max and min stresses in cycle
  Can reduce stresses by reducing pressure of lithium “preload”
Currently pulse-testing lens in test stand at full gradient (230 T/m) and average 12 Hz repetition rate
  Running 24hrs/day
  Have integrated ~18M pulses
  Pulse lens for months or until we find its limits
lithium lens
in test stand
back of power supply

## Slide 58: Cryogenics for g-2 and Mu2e experiments

## Slide 59: Experiment Cryogenics Requirements
Cryogenic loads:
g-2 storage ring
  Liquefaction load – 1.4 [g/sec]
  Refrigeration load – 300 [W]
  LN2 Shield flow rate – 1.6 [g/sec]
The Cryogenic System shall support simultaneous steady state operation of both experiments, Muon g-2 and Mu2e. It shall provide for independent operation of the two experiments, including transient modes, e.g. warm-up, cooldown, etc.
It should be possible to connect and/or isolate Mu2e magnets from the transfer line while under cold conditions
Mu2e solenoids
  Liquefaction load – 0.8 [g/sec]
  Refrigeration load – 350 [W]
  LN2 Shield flow rate – 20 [g/sec]

## Slide 60: Cryo compressor system
A0 compressors (four skids)
Each skid consists of the following:
  Two-stage oil injected screw compressor
  300 kW motor
  60 g/s capacity
  Compression from 1 atm to 20 atm
  Slide valve for capacity control
  6 kW oil pump
  Oil cooler heat exchanger
  Aftercooler heat exchanger
  Oil separator
  Oil removal system
  Entire system is contained on a single,
  fabricated steel base skid, oil removal
  on separate skid
Two-stage compound oil flooded
screw compressor Mycom 2016C

## Slide 61: Piping headers
from A0

## Slide 62: Refrigerator room

## Slide 63: Refrigerator room (cont)

## Slide 64: Transfer line

## Slide 65: Transfer line (cont)

## Slide 66: Cryo AIP timeline
Plant and g-2
g-2 cryo distribution
2017
2015
2014
2013
2016
Compressors
g-2
Mu2e distribution
Mu2e cryo distribution
Mu2e
Refrigerators
g-2
Refurbishment and installation
Procurement and installation
Cooldown
Engineering and design

## Slide 67: MC-1 Building

## Slide 68: MC-1 Building GPP
MC-1 building designed to house g-2 and future experiments, cryo system for g-2 and Mu2e, and power supplies for some beamline components
  80’ x 80’ high-bay with 30 T crane
  internal loading dock
  floor stable, load-bearing to 700 T
  good temperature control
  70’ x 70’ low-bay for staging, assembly, control room

## Slide 69
MC-1 Building – Site Plan

## Slide 70
MC-1 Building – First Floor Plan

## Slide 71
MC-1 Building – Second Floor Plan

## Slide 72
MC-1 Building – Cross Sections

## Slide 73: MC-1 Building site prep in progress
Construction split into two packages to expedite construction
Goal of site prep package is to 1) relocate all utilities out of building excavation, and 2) perform all shutdown work during current shutdown
  Relocate/tap into utilities
  Relocate Well Pond Road (shutdown)
  Install cryo line supports and under-road piping (shutdown)

## Slide 74: MC-1 Building
Building construction will be out for bid in next few months

## Slide 75: A look ahead and conclusions

## Slide 76: Muon Campus offers many advantages
Chris Polly, Muon g-2 Briefing, November 26, 2012
76
Distinguishes between project-specific and more general upgrades, needed for g-2 and Mu2e this decade…opportunities for Stage 1 Project X
Allows GPP/AIP pieces to move forward quickly and meet the combined specifications and timelines
Recognized over $100M in savings in the total cost of the muon program, Mu2e run time extended to 3 years, added capability for muon g-2

## Slide 77: Possibilities for Muon Campus experiments using Project X
Mu2e upgrade, muon EDM experiments, …

## Slide 78: Conclusions
Plans for accelerator and civil work needed to support g-2, Mu2e, and future Muon Campus experiments are maturing
Still determining how to best package the work into Projects: g-2, Mu2e, Accelerator Improvement Projects, and General Plant Projects
Shared infrastructure between Mu2e and g-2 as well as reuse of existing infrastructure enables us to do these projects for significantly lower cost
Aiming for g-2 beam in early 2016, Mu2e in 2019