## Slide 1: Linac Laser Notcher Status
David Johnson
Todd Johnson, Vic Scarpine, Andrea Saewert,
John Sobolewski
PIP Meeting
March 6, 2013
Beams Doc 4306

## Slide 2: Laser Notcher System
Major Components of the system
  Optical pulse generation
  Fiber amplifier system (2 + 1 stages)
  Macro pulse generation (at 15 Hz) (Pockels cell)
  Free space laser amplifier
  Laser transport and beam shaping / optical cavity
  Vacuum chamber and integration into MEBT
    Prototype using 3D printer in TD
  Timing and controls

## Slide 3: Burst mode seed pulses to Fiber Amplifier followed by Free Space Amp
l1=1064nm
120 mW CW
SW=0.1 nm
10 GHz Mach-Zehnder
Modulator
Pulse Generator
Amplifier, Timing
PM Fiber
Lins ~5dB
Li~1.8dB
15 Hz
Pockels cell
Updated 10/3/2012
Generate 24 us burst at 15 hz
TRANSPORT BEAM SHAPING OPTICS &
OPTICAL CAVITY
Fiber Pre-Amp
Fiber Amp 1
Fiber Amp 2
Free Space Amp
Output modulator/Input fiber pre-amp:
201.25MHz pulses (1.25 ns pulse), 458kHz burst
Clean up filter
Isolator
Line filter
Free
Space
Grumman CEO DPSS OEM
Diode + TC
controlled
*Notch 12 bunches -> 60 ns
10 notches/linac pulse
Measurement point

## Slide 4: Status of the OPG and Fiber Amp
We set up the optical pulse generation/fiber amplifier system in the new A0 instrumentation laser laboratory.
We now have the seed laser and fiber amplifiers connected to the safety interlock system and have procedures in place and permission to operate the equipment on hand.
We have started characterizing the characteristics of the system using a borrowed pulse generator and scope/spectrum analyzer in the A0 lab.

## Slide 5: OPG Fiber Amp Components
Diode/TEC power supply
Safety System interface
Modulator Bias Controller
Fiber Pre-amp
Fiber Amp 1
P.S. for RF Amp

## Slide 6: Optical components
Seed Source
RF Amp
FBG / isolator
& fiber holder
Modulator
Narrow band
Optical filter
Photodiode
detector
All this to be mounted inside a chassis

## Slide 7: Current support equipment
Borrowed from Peter Preito
  HP 8131A 500 MHz pulse generator
  RF splitter
Instrumentation (Carl Lundberg)
  Power supply for RF amplifier
Equipment in A0 Instrumentation laser lab (Vic Scarpine/Andrea Saewert)
  Tektronix TDS7104 1 GHz/10 GS/s oscilloscope
  Agilent 86142B Optical Spectrum Analyzer
  Thorlab’s fiber coupled photodiode DET01CFC
  Miscellaneous lab supplies…

## Slide 8: 200 MHz Laser Pulses
200 MHz pulsed from:
HP pulse generator input into
modulator RF amplifier
200 MHz Laser pulses (1.25 ns flattop) out
of fiber pre-amp with (band pass filter included)
* I didn’t have a blank floppy disk with me
200 MHz pulses
450 kHz
I need to add another pulser to trigger the HP
at 450 kHz to create the burst structure

## Slide 9: Picosecond Pulse Labs Model PSPL 12020 Screen Shots
Burst rep rate of 450kHz
Seven 200MHz pulses
Decreasing time/division
1.5ns FWHM pulse width

## Slide 10: Seed Source
Seed source 50 mW with 1.6 dB isolator -> 34.75 mW
Measured 34.8 mW with Thorlabs PM20CH (15.4 dBm)
Factory Calibration
11.4 dBm
User calibration
Installed user calibration based upon power meter.
This gives a closer result 15.26 dBm (33.5 mW) - <4%
15.26 dBm
Line broadening of seed?
Measured power in seed source with OSA
Found: 11.4 dBm (13.8 mW) ---way too low ???

## Slide 11: Modulator and Preamp
DC extinction ~ 25 dB
Pump 600 mA
Seed on/off
Spectrum from pre-amp thru the Band Pass filter
Span 100 nm
Span 5 nm
22.8 dBm
~190 mW
(~ nJ pulse energy)
Note: operating seed
at half power
Modulator

## Slide 12: Vacuum chamber
The vacuum flange and beam pipe containing view ports and zig-zag cavity will prototyped using the 3D printer in TD.
  Make new RFQ flange (thicker) with view port and internal optical cavity supports.
Must fit in this space

## Slide 13: Summary
We have assembled and starting to characterize the first components for the Laser Notcher.
Will continue to learn how to operate the OPG and fiber amplifiers.
We would like to put the OPG equipment inside a chassis to protect fibers and get rid of external power supply for RF amplifier.
We will add another pulse generator to create 450 kHz burst.
The temporal pulse structure out of the borrowed pulse generator is not as uniform as needed, but will work till we get the final pulser.
We have not spent much time on the beam shaping optics since we demonstrated beam shaping and zig-zag cavity last fall. We need to add in an anamorphic prism pair to better shape the horizontal beam out of the piShaper to move forward with the design.
Todd has been working on the free space amplifiers at NML which are very similar to those we will be using next year for the final amplification stage.
John Sobolewski (MS co-op) is beginning to look at the vacuum holder for the optical cavity. We are planning to prototype this using the 3D printer.
This summer add in the Pockels cell to create 15 Hz burst of pulses.
By end of FY13 we should be ready to add new pulse generator, final fiber amplifier, and free space amplifier.