## Slide 1: Linac Laser Notcher Project in the Proton Improvement Plan (PIP)
David Johnson, Todd Johnson, John Sobolewski, Fred Mach, Kevin Duel, Andrea Saewert
February 11, 2014
Accelerator Physics and Technology Seminar

## Slide 2: Topics
Booster Notching
Current Booster Notching System
Laser Notching (concepts and benefits)
Location of current notching experiment
Photoneutralization
Requirements/Techniques for Laser Notching System
Laser System – design and status
Beam Shaping
Optical Cavity
Installation concept
Current Plans
Issues
Cost/Schedule
Summary

## Slide 3: Booster Notching
Booster utilizes multi-turn injection of H- ions where the Linac pulse length is determined by N*tREV .
A “notch” must be created in the continuous Booster bunch structure to allow for the rise time of the extraction kicker. We need approx 40-50 ns notch.
Current technique is to use fast kickers in the Booster to remove a section of the Booster beam (40-50 ns out of ~2.2 ms) at an energy of 400 to 700 MeV and deposit it in a shielded absorber in the ring.
  New system installed 2013… commissioning underway…..
  Next slide….

## Slide 4: New Booster Notcher Tunnel Devices
Pictures courtesy of Salah Chaurize
Installed just this last shutdown (2013)
Commissioning underway
Kickers - Long 12
Absorber Long 13
We would like to create notches outside the Booster tunnel at an energy low enough to eliminate the activation of components entirely (i.e. 750 keV, the energy of the Linac RFQ). This is the basis of this presentation…
Since the Booster must increase its
throughput (x2) to satisfy new demands…

## Slide 5: Laser Notching of Linac H-
Concept/History:
  Removal of weakly bound outer electron by photodetachment using appropriate laser wavelength, temporal and spatial profile.
  Concept proven by Ray Tomlin (circa 2001). Next slide…
  Additional notcher proposals were described in 2005 by Xi Yang to notch the linac beam at the Booster injection RF frequency (FN-0765-AD) and at the revolution frequency utilizing a pumped recirculating cavity (FN-0767-AD). Neither of these proposals were implemented.
  Most recently proposed by Bob Zwaska and further developed with input from a number of Fermilab colleagues , laser experts, and manufacturers.
Benefits:
  Laser pulses may be formed to match bunch pattern (broad band
  Fast rise time (may be tailored to individual bunches)
  Doesn’t require high power pulsers /delay lines to create ns pulses
  System can have a reasonably small footprint
  Advances laser technology for accelerator applications (laser stripping, laser notching, laser chopping, photoinjector, laser diagnostics, etc…
  ++++

## Slide 6: First Laser Notching Experiment
In 2001, Ray Tomlin reported on a successful experiment to create notches in the CW linac beam in the H- 750 keV beam line and have this notch survive at Booster injection.
He created a 25 ns notch utilizing a 200 mJ 5 ns laser pulse.
To create multiple notches in the linac pulse he
proposed a
  “4 pass bow-tie cavity some 665 meters
  long (with a storage time of 2.22 ms)”. Large Pockels
  cells would shuttle the laser to and from the delay line.
A disk gain section would restore optical losses.
Average laser pulse energy of 103 mJ
Peak power of ~20 MW to strip 99.9% of the ions.
This was not implemented.

## Slide 7: Location of Linac Notcher in PIP Era
Move loss due to notching OUT of the Booster tunnel
Minimum transverse size – bunched at 201.25 MHz
RFQ
MEBT

## Slide 8: Location of Notcher
Must fit in this space

## Slide 9: Expected Beam Dimensions
Phase space simulation at end of RFQ (figure 4.40 of 750 KeV Upgrade Plan)
Trace 3D back calculation of beam size at exit of RFQ based upon emittance measurement at 178 kW power August 9, 2012 CY Tan.
Laser beam vertical profile (1/e2) ~ 5 mm.
Initial design assumed that the vertical laser beam dimension of 1 cm.
Beam measurements indicate vertical laser size could be reduced to 6 mm

## Slide 10: Photoneutralization (1)
The fraction of electrons that are detached from the moving H- ions is:
The photon flux (generated by the laser)
in the lab frame [photons/cm2/sec]
The photon flux in the lab frame is transformed into the
rest frame of moving ion as:
The interaction (crossing) time is just the ion path length/ ion velocity
The neutralization factor for an ion crossing on axis
of the laser beam may be written in terms of lab frame parameters
For q ~ 90o term -> ~g

## Slide 11: Linac Beam Bunch Structure
24.2 us (~ 11 Booster turns)
2.2 us
67 ms
~22-25 us
~5 ns (bunch spacing)
~bunch length
200 MHz bunch spacing
450 kHz “notch” spacing
15 Hz macro pulse rep rate
MACRO
MINI (11 turns)
MICRO
2.2 us
10-12*5ns = 50 -60 ns

## Slide 12: Photoneutralization (2)
Rest frame energy 1.16 eV for
1064 nm laser
Cross section 3.66x10-17 cm2
To maximize the neutralization probability->maximize the product
fixed
To maximize
increase pulse energy -> minimize
reduce pulse length -> bunch length
reduce laser spot size -> ion size
To maximize t for a given H- ion energy
increase horizontal laser beam size or
increase the number of laser interactions
with the ion bunch
20-30 mJ
Assume:
Laser size 0.6x6mm
Assume:
Laser size 0.6x6mm
~1J
1.5 ns
60 ns

## Slide 13: Reduction of Pulse Energy
To reduce the required pulse energy we can effectively increase the interaction time by utilizing an optical cavity such that the laser interacts with the ion beam multiple times.
H-
Linear cavity (zig-zag)
Laser follows ion to interact many times (increase t)
Cavity length proportional to number of interactions
Laser pulse length = notch length
Cavity dimensions determined by ion velocity and bunch spacing
Reduces required laser pulse energy by ~ number of interactions
R. Shafer , 1998 BIW
2 mJ for 99.92%
Assume mirror reflectivity 99.95%
20 reflections

## Slide 14: Requirements and Technique of Laser Notching of H-
Requirements
  All ions in bunch should see the same photon density
  The 201.25 MHz laser pulses must be phased with the RFQ
  The laser pulse length > bunch length
  Uniform temporal profile
  The burst of 201.25 MHz pulses must match the Booster inj rev. freq.
  The 450 kHz burst must have appropriate timing within the linac pulse
  The pulse energy should neutralize > 99% of ions in each bunch
Technique
  Utilize a CW seed laser and wave-guide modulator to create required laser pulse pattern (both 200 MHz and 450 kHz) at low pulse energies (pJ)
  Amplify pulse pattern using a three-stage fiber amplifier (nJ to uJ)
  Further amplify using a free-space solid state amplifier (mJ)
  Create a spatially uniform photon beam
  Insert laser pulse into a linear zig-zag interaction cavity where the laser reflections inside the cavity match the ion velocity
    to reduce required pulse energy by the number N of reflections in the cavity.

## Slide 15: Burst mode seed pulses to Fiber Amplifier followed by Free Space Amp
l1=1064nm
120 mW CW
SW=0.1 nm
10 GHz Mach-Zehnder
Modulator
Pulse Generator
Amplifier, Timing
PM Fiber
Lins ~5dB
Li~1.8dB
15 Hz
AOM
Generate 24 us burst at 15 hz
TRANSPORT BEAM SHAPING OPTICS & OPTICAL CAVITY
Fiber Pre-Amp
Fiber Amp 1
Fiber Amp 2
Free Space Amp
Output modulator/Input fiber pre-amp:
201.25MHz pulses (1.25 ns pulse), 458kHz burst
Clean up filter
Isolator
Line filter
Free
Space
Grumman CEO DPSS OEM
Diode + TC
controlled
*Notch 12 bunches -> 60 ns
10 notches/linac pulse
Pulsed at 15 Hz

## Slide 16: Optical Pattern Generator
Input: 100 mW CW
Output: 54 pJ (1.5 ns/200 MHz)
294 uW avg power at 450 kHz
Pulse on/off extinction 30 dB

## Slide 17: OPG Fiber Amp Components on Bench
Diode/TEC power supply
Safety System interface
Modulator Bias Controller
Fiber Pre-amp
Fiber Amp 1
P.S. for RF Amp

## Slide 18: New OPG module
Andrea Saewert

## Slide 19: Optical Pattern Generation
450.75 kHz burst of 201 MHz pulses
One set of 201.25 MHz pulses
Individual 201.25 MHz temporally uniform pulses
Pre-distortion of EOM pulses
Yellow- AWG
Purple- RF Amp out
Green – signal form 1.2 GHz (free-space)PD laser pulses out of fiber pre-amplifier
AWG: Chase Scientific DA12000 & CG6000 module

## Slide 20: Fiber Pre- Amplifier System
Input 54 pJ
294 mW
Gain 23 dB
Gain 17.2 dB
Output 100 pJ
590 mW
Output 385 nJ
2 W
PriTel
Gain fiber is Yb doped
6mm core/125 um cladding
System to be re-package in 19” rack mount with
Computer control/readback and “auto shutdown” for YbFA-33 amplifier.
amp
filter

## Slide 21: Fiber Amplifier System
Input 363 nJ 1.96 W
Gain: 14.5 dB
Optical Engines
Micrograph of PCF fiber
Single mode, single polarization
Small NA (~0.03)
Large mode area
High peak power levels
High pump absorption (~10 dB/m)
High reliability
System on order- due for delivery later this month.
Output to include mode
stripper (to remove any pump
light) and optics to match
into first FS amp.

## Slide 22: Free Space Amplifier System
Pulsed at 15 Hz
Gain: ~ 23 dB (total for both modules)
Output: 2 mJ 10 kW (450 kHZ) 3.2 mW (15 Hz)
Faraday Isolator
to protect previous
stage and aid in
double pass operation.
Input: 10 uJ 55W (450 kHz) 16 mW (15 Hz)
To Optical
Cavity
1D & 2DPSD
Class 4 laser system
Difficult to operate
with lid off
Need to heavily
instrument
Current design -> could change depending of fiber amp performance
80
9

## Slide 23: Beam Shaping (modification of the transverse beam profile in the optical cavity)
We would like to demonstrate > 99% neutralization efficiency for all ions in the bunch, therefore we would like all ions to “see” the same photon flux regardless of their transverse amplitude. (i.e roof-top laser profile)
  The vertical size of the laser beam should be ~ > 6s of the ion bunch or about 6 mm (the horizontal size should be < 1 mm
We have investigated two techniques to create this roof-top profile through the interaction cavity.
  pShaper – refractive beam shaping optics
  Beam stacker – splitting a Gaussian beam into H and V polarized beams with a birefringent crystal, a technique proposed by Todd Johnson

## Slide 24: pShaper (AdIOptica GmbH)
Refractive optical system
Output beam is free of aberration
Collimated output beam
Resulting beam profile is stable over large distance
Galilean design

## Slide 25: Beam Shaping w/ pShaper… the layout
Input pShaper
Output pShaper
Output Anamorphic prism
Cylindrical telescope
532nm diode
pShaper

## Slide 26: pShaper Propagation
Intensity distribution varies with distance due to diffraction effects.
For visible light and flattop beam diameter of 6 mm the distance where the deviation in uniformity doesn’t exceed +/-10% is about 200-300mm.
This distance is inversely proportional to wavelength -> for 1064 nm we should expect only 120 to 180 mm.

## Slide 27: pShaper Propagation
We think this would work, but…
We would like to do better that this for propagation of a uniform profile….

## Slide 28: Beam Stacker Concept (Todd Johnson)
Based upon a birefringent
crystal where the index of
refraction is dependent on
polarization
Here the half-wave plate
rotates linear polarized
beam to 45o and the crystal
displaces V pol and H pol
remains un-deflected.

## Slide 29: Layout of the Beam Stacker

## Slide 30: Telescope to Match Diode to Stacker
We use CW diode to test the beam stacker concept.
Ultimately the input to the Stacker will be from the Free Space Amplifier.
Since the output of the Free Space Amplifier will have a 1/e2 diameter
of 5.1 mm we will need a telescope to match the stacker.

## Slide 31: Beam Stacker – merging beamlets

## Slide 32: Beam Stacker - Propagation
Represents 6 mm
vertical dimension
with constant intensity

## Slide 33: Add Cylindrical Telescope to Stacker

## Slide 34: Optical Cavity
Mirrors at 2.288o wrt H- beam
showing 21 interactions
John Sobolewski and Fred Mach
H-
Laser output to dump
Laser Input
Mirror separation matched to ion velocity

## Slide 35: Optical cavity tests
Fixed mirror
Moveable mirror
Test set-up

## Slide 36: Optical Cavity prototype
We printed a 3D model to test design
This was very useful as it pointed out several
improvements/modifications to the design.

## Slide 37: Installation
Issues:
Moveable for MEBT maintenance
Electrical requirements
Cooling requirements
Effects of ion source sparking
Optics Box sits on top of rack
Free space laser
completely enclosed
……. Currently set for April 2015

## Slide 38: Near term Plans
Goal complete laser in LAB end of FY14
Finish packaging OPG and test end of Feb
Repackage Fiber pre-amps(s) end of Feb
Receive Fiber Amplifier end of Feb
Test Fiber stages with OPG mid March
  Determine FA output to determine FS
Finalize design of Free Space Amplifier end March
  Order components for amplifier (14 week delivery for amp modules)
Continue optimization of Beam Shaping on going
Start diagnostics electronics design May
Finalize mechanical design of Optical Cavity
  Generate manufacturing prints mid April
Construct optics box stand and relay rack mid March
Continue discussion on timing system

## Slide 39: Issues
Notch survivability in Booster (see next slides)
  Start of RF capture
  Capture parameters
Not achieving design pulse intensity (next slides)
Reliability of system
Impact of ion source sparks on electronics - TBD
Portability and alignment
Pre-distortion of laser pulses for fiber and DPSS stages
Impact of optical cavity in quad fringe field
  Estimation shows it to be not a problem
  Simulation electron trajectories by Vladimir Kashikhin

## Slide 40: 200 MHz bunches in Booster
Evolution of 200 MHz bunches
during 17 turn injection
Assume full energy spread
of injected beam +/- 0.6 MeV
Momentum Spread*
Total time ~ 53 ms
injection
Chandra Bhat
*Measured value in Booster

## Slide 41: Evolution of the Notch in Booster
Total of 17 turns injected
over ~ 34 us
Total time ~ 53 ms
of simulation

## Slide 42: Neutralization vs Pulse Energy
Design value

## Slide 43: Budget
WBS | TASK | M&S* | contingency
.01.02.03.01 | Initial Design | $0 | 
.01.02.03.02 | Optical Pulse Generator | $35,000 | $6,000
.01.02.03.03 | Fiber Amplification Stage | $100,000 | $16,000
.01.02.03.04 | Free-Space Amplification and optics | $160,000 | $40,000
.01.02.03.05 | Optical cavity and vacuum chamber* | $20,000 | ---
.01.02.03.06 | Beam shaping/transport/diagnostics | $25,000 | $5,000
.01.02.03.07 | Timing and Controls | $24,000 | $10,000
.01.02.03.08 | Installation | $18,000 | $6,000
.01.02.03.09 | R&D Lab supplies and materials | $7,750 | ----
 | TOTAL (*unburdened) | $389,750 | $83,000
We have obligated ~$192K to date. The next largest purchase will be for
the free-space amplifier and associated optical components (est. to be ~< $100K).
“Contingency” numbers are amounts above what we “expect” to spend
in each of the Tasks… but then there are unforeseen expenses

## Slide 44: Schedule

## Slide 45: Summary
We have described our motivation for moving the process of notching outside the Booster tunnel.
We have described the requirements for the laser system to create the notches.
We have described the laser system design to accomplish the goal of creating notches.
We have described the status of the components and system.
We have the front-end laser system with the final fiber amplifier on order and are in the process of R&D on beam shaping and working on the final design of the optical cavity.
We would like to have laser system operational in lab by end FY14.
The current plan is to install the system in Q2 of Fy15.

## Slide 46: Acknowledgements
Dave Baird
Dan Bollinger
Ken Domann
Fernanda Garcia
Mike Kucera
Ray Lewis
Bill Pellico
Peter Prieto
Matt Quinn
Jinhao Ruan
Jamie Santucci
Vic Scarpine
C.Y. Tan
Bob Zwaska

## Slide 47: Thank you

## Slide 48: Laser Parameters
Laser Parameter Requirements entering interaction chamber:
Laser Energy 2.0 [mJoules]
Pulse length 1.500000e+03 [ps]
Spot size: H 0.0600 [cm] V 0.6000 [cm]
Laser beam area 3.600000e-02 [cm^2]
Lab Frame Photon wavelength 1064.00 nm
Lab Frame Photon Energy 1.868068e-19 [J] 1.165139e+00 [eV]
Photons per pulse 1.070625e+16
Photon rate 7.137500e+24 [photons/sec]
Photon fluence 2.973958e+17 [photons/cm^2]
Photon flux 1.982639e+26 [photons/cm^2/sec]
Laser Peak pulse power 1.333333e+00 [MW]

## Slide 49: Optical Cavity Parameers
Distance between crossings 1.188000e-01 [cm]
Distance between reflections on mirror 2.376000e-01 [cm]
distance laser travel between crossing 1.487310e+00 [cm]
cavity radius 1.486124e+00 [cm]
cavity diameter 2.972247e+00 [cm]
Incident angle 2.288880e+00 [degrees]
Crossing angle 87.71 [degrees]
Lorentz Factor 9.992022e-01
Rest frame photon energy 1.164210e+00 [eV]
Rest frame wavelength 1.064850e+03
Cross section in rest frame 3.660952e-17 [cm2]

## Slide 50: Laser/cavity Parameters
crossing time 5.015246e-11 [sec]
Number of passes 20.000000
Photon flux in H- rest frame 1.981057e+26 [p/cm^2/sec]
Mirror Reflectivity 9.995000e-01
Average Neutralization factor per interaction 3.024028e-01
Total Neutralization 9.992551e-01
Multipass insertion length 2.257200e+00 [cm]
Total laser path length 5.651779e-01 [m]

## Slide 51: DPSS output for pump timing

## Slide 52: Cavity in Quad fringe field

## Slide 53
K.E. (H-) 750 keV
Electron energy 409 eV
Velocity 1.198E7 m/s
Electron bend radius in field B r 
H- 1s ~ 0.83 mm -> 3s < ~ 2.5 mm
Field at particle amplitude -> G*amplitude
~30 mm
5 mm
First quad in doublet is
H focusing for H- and e-
Assume end-field shape
is the same as between
pole tips
mirrors
Electron in fringe field