More coupler calculations + what's next
C.Y. Tan & R. Madrak
11 Nov 2014

---
Updates
- Robyn discovered a mistake that I made in the coupler calculations
  - Impedance seen by the tube is smaller than what I had originally found because I was calculating it at the wrong point! Oops!
  - Unfortunately, does not change the essential result that 25 – 30% of the power will be reflected due to impedance mismatch.
- Location of coupler has to moved from the middle to nearer the gap for better matching.
- More calculations were done, this time double checking with SSC published results.
  - Checked R/Q and Rs (cool trick to use R/Q = 2(ω0 dB/dω)-1, B is susceptance of the model)
  - They match!

---
Calculating Rs and Q of the cavity+coupler
- The calculation involved using Robyn's AL800 measurements of Q, and m' from which μ'' can be derived μ'' = μ'/Q.
- Use transmission line model
  - Include copper losses
    - Decreases both Q and Rs
- Calculate matching to coupler
- Calculate power required for PA taking into account both PA efficiency in class B operations and reflections.

---
Move coupler closer to gap
Coupler shifted so that the non-garnet part is divided into 3:1 parts.
Note that coupling capacitor is a lot smaller than what I drew. See SSC cavity.

---
Results for shifted coupler
• cavity + garnet
• garnet only
Q of cavity is higher because more energy is stored outside the garnet

---
At the tube
By moving the coupler closer to the gap, the reflected power goes from 35% at the centre to 27%. This assumes that the tube has 1.4 kΩ impedance (J. Dey)
Robyn checked that the step up voltage from tube anode to the gap is correct using SPICE.

---
Is this 27% reflection ok? Can the tube handle it?
- Let's work at 76% where the reflection is the worst at 27%.
  - Assume class B operation, efficiency is about 75%.
    - Thus overall efficiency is η= 0.75*(1 – 0.27) = 0.55.
  - In the ideal case, if all power goes into the cavity, the required power to get 100 kV across the gap is
    - Prf = Vgap2/(2 Rs) = 100e32/(2*55.6 kΩ) = 90 kW @76 MHz
    - Taking into account the inefficiency, I will require Prf/η = 164 kW from the tube.
    - This implies that (164 – 90) kW = 74 kW will be reflected into the tube.
      - This should still be ok. Tube anodes, depending on model can dissippate between 100 kW to 150 kW.
  - Must check this with a more proper load line calculation. See next slide.

---
Grounded grid, class B operation
Top left point of red line (plate to grid voltage=1 kV, anode current = 60 A), bottom right point (plate to grid voltage 11 kV, cathode to grid voltage = 320 V).
1 kV from minimum anode voltage is 1 kV.
Maximum current:
the required tube voltage 10 kV (assuming step up of 10 to get 100 kV in gap) + 1 kV for screen voltage and the required power of 164 kW.
DC anode current = 164 kW/(10+11)kV = 15 A.
The peak current for class B operation Ipeak = 4*15 = 60 A. (Using 4 rather than π to take into account non-linearity of tube)
Min cathode to grid voltage:
320V comes from Recycler cavity requirements. Checked with J. Dey.

---
Create anode current plot vs phase (θ = ωRFΔt) curve
The shows ideal class B anode current. The Fourier components of the anode current gives the DC current and the RF current
These are the points read off from the load-line curve. This gives the points from 0 to π/2.
Reflect about θ = 0 to get curve that looks the similar to the ideal class B anode current curve.

---
Fourier analysis of the anode current derived from the load line plot
- IDC = 15 A.
  - DC input power Pdc = 15.275 A * (10+1) kV = 168 kW (think of Pdc as the average power going into the tube)
- IRF peak = 26.3 A
  - RF power Prf = 1/2*(26.3 A)*(10 kV) = 131 kW
- Thus efficiency Prf/Pdc = 131/168 =0.78 which is close to 0.75 assumed earlier.
- Power lost in anode from class B operation = (168 – 131) kW = 37 kW
- Power lost from reflection 0.27*131 kW = 35 kW
- Total power that is dissipated on the anode is (37+35) kW = 72 kW < 100 kW power that can be dissipated by the tube. So we are OK!
  - This is the same as what was calculated using the back of the envelope earlier!

---
Summary for coupling calculations
- The coupler needs to be moved from the middle to a point that is closer to the gap. This reduces power reflection from 35% to 27% when tube is 50% closer to the gap.
- Tube cooling should be ok.
  - Within power cooling specifications of tube.
    - Depending on tube model, it is either 100 kW or 150 kW > 72 kW of expected power loss on anode.
- Required power is within the power output of tube.
  - Output power specs is 100 kW to 250 kW > 163 kW
  - Tube can be run reliably at 220 kW (source: J. Dey, c.f. MI).

---
Next comes the HOM dampers
Re-entrant cavity HOM damper.
Modified cavity HOM damper with HPF.