## Slide 1: Update on Model/Mock Cavity
Robyn Madrak
02/03/2015

## Slide 2
Current superfish model of the MODEL cavity
Current superfish model of the REAL cavity
Ratio of OD/ID in this region the same
l1
l1
l2
l2
L1: 13.000 → 19.685
L2: 47.400 → 39.915

## Slide 3
“outer conductor”
“inner conductor”
solenoid
Garnet
(ferrite)
0.43” Stack of 10:
3” OD,
1.853” ID
Critical dimensions for RF:
Generally, the volume enclosed between the outer and inner conductors
Inside length
OD of outer conductor
ID of inner conductor
Geometry in the gap
OD/ID/length of ferrite
The gap
“shorted end”
Inner conductor is connected to outer conductor
Cavity uses solenoid as a support (sits on it)

## Slide 4
The solenoid we need to use:
(spare solenoid from RR cavity tuner)
Tuner:
1 goes inside of 2 (center and outer)
2 goes inside of 3
1
3
2
Center is shrink fit with LN2 to fit in ferrite

## Slide 5
For scale, assuming Bob Wilson was 6 feet tall:

## Slide 6: Issues (Kevin is working on)
What material for the center and outer conductors : copper? Aluminum? /tubing? Sheet metal?
How to attach various pieces (bolts? Brazing/welding/soldering? copper tape?)
How to fit the center conductor in the garnet and the garnet in the outer conduc tor minimizing any gaps (it changes the results)…shrink fit for inner?....
How to attach the HOM coupler/ how to model the HOM coupler?
The good part
No vacuum
Only low power
Strategy
First measure fundamental, HOM’s, effect of (model) HOM coupler
Later – add input coupler (or make additional mock cavity)

## Slide 7: Effect of gaps for clearance in garnet part
No gaps => no gaps at all
With gaps => outer conductor (3.027”) is 0.027” bigger in diameter than ferrite OD;
inner conductor (1.818”) is 0.035” smaller in diameter than ferrite ID
Chart: f(MHz)
| 77.879159999999999 | 153.08569 | 283.45109000000002 | 403.07171 | 488.58031 | 632.35748999999998 | 710.81575999999995 | 752.95690999999999 | 837.59271000000001 | 940.44485999999995
Real cavity with garnet | 48.58 | 142.27 | 7.634 | 62.46 | 9.022 | 14.227 | 22.208 | 0.347 | 7.287 | 15.962
Model - NO GAP | 32.87 | 122.17 | 8.36 | 23.75 | 20.9 | 11.21 | 9.5 | 23.94 | 6.65
Model - WITH GAP | 93.879 | 64.5075 | 37.6065 | 28.548 | 22.509 | 28.8225 | 12.078 | 37.881 | 6.3135
Chart: f(MHz)
| 77.879159999999999 | 153.08569 | 283.45109000000002 | 403.07171 | 488.58031 | 632.35748999999998 | 710.81575999999995 | 752.95690999999999 | 837.59271000000001 | 940.44485999999995
Real cavity with garnet | 1278.76 | 2994.6 | 1277.95 | 3156.67 | 1468.34 | 1829.75 | 2282.33 | 1099.83 | 1615.34 | 2280.05
Model - NO GAP | 969.977 | 2429.37 | 1165.89 | 1784.06 | 1733.97 | 1630.18 | 1596.05 | 2321.82 | 1592.37
Model - WITH GAP | 1574.42 | 2271.92 | 2317.57 | 2312 | 2449.91 | 2838.47 | 2185.83 | 3969.58 | 1921
We have in the past done a shrink fit on using one solid piece of ferrite for inner conductor
Outer conductor – wrap around and clamp?

## Slide 8
Regions 1 and 3:air, e=1
Region 2: ferrite; ef ~ 14
r1 (cm) (d1 = 1.818”)
r2(cm) (d2 = 1.853”)
r3 (cm) (d3 = 3”)
r4 (cm) (d4=3.024”)

## Slide 9
Viewed as 3 cylindrical capacitors in series, where C (capacitance/length)
C1=2pe0/ln(d2/d1) = 2.92 nF/m
C2=2pefe0/ln(d3/d2) = 1.62 nF/m
C3=2pe0/ln(d4/d3) = 6.98 nF/m
Then Ctot = C1*C2*C3/(C1*C2+C1*C3+C2*C3) = 0.9 nF/m
Then defining Ctot = 2peeffe0/ln(d4/d1)
I can solve for an “effective epsilon” for the entire region
(between d4 and d1)
If I set ef = 14 and solve for eeff, I get eeff = 8.28
So we should pay attention to miminizing the gaps

## Slide 10: Progress
We have a design
Ferrite is ordered
We are thinking about how to implement the design

## Slide 11: Appendix Slides (not shown)

## Slide 12: Examples of Other Model Cavities: RR Model Cavity
Inner
conductor
outer
conductor
Sheet metal, connected with screws and nuts
Seams along length of cavity (direction of current flow, does not decrease Q)
Home insulation
The inner and outer were connected with
a donut shaped piece of home insulation and a very large hose clamp
Inner
conductor
outer
Hose clamp
insulation
Gap end cover
Tabs bend out

## Slide 13: Examples of Other Model Cavities: Joe Dey’s
Made out of copper sheet metal
Supported by wood
Joints are soldered

## Slide 14
Examples of Other Model Cavities: Dave Wildman’s old cavity
Copper sheet metal
All soldered
Presumably some support was used while soldering

## Slide 15
Examples of Other Model Cavities: Using standard coax hardline