Coupler
C.Y. Tan
11 June 2015

---
LANL Coupler
LANL design
Rescaled for our cavity

---
Simion calculation
Simion calculation says LANL capacitance is 8 pF. But ssl-preprint-067.pdf claims their cap is 13 pF, so it is about 50% off. Needs to be checked with a better program. I am going to assume that SIMION is correct for now.
Using the reduced size for our cavity, the scale reduction is α=0.5
And C ~ A/d, rescaling everything by α, A→α2 A and d→αd, thus C→αC.
Thus the capacitance of the reduced size coupling capacitor is 4 pF. This is too small for us.
1.5”

---
Move cap closer
I checked two cases:
0.2” gap: 28 pF
0.1” gap: 42 pF
These are probably underestimates.
Again, for our smaller sized cap, it will be:
0.1” gap: 14 pF
0.05” gap: 21 pF
Therefore, the gap for us is probably going to be between 0.1” and 0.2” to get 10 pF, if we leave the gaps on the sides as is.
0.1” – 0.2” is probably too small a gap to hold off 100 kV.

---
Summary of dimensions used in calculations
0.35 m
0.09625 m
0.112181 m
0.28875 m
l_f
Parameter	value	comments
Z1, Z2	61.299 Ω	Non-ferrite characteristic impedance
Zc	20.9269 Ω	Characteristic impedance of coupler
Parameter	value	comments
Cc	10 pF	Coupling capacitance
Ct	60 pF	Tube capacitance
Cg	3.4 pF	Gap capacitance
rfi	0.105 m	Inner radius of ferrite
rfo	0.170 m	Outer radius of ferrite

---
The new measurement of μ'' vs μ' used in calculation
The data is from 21 May 2015 talk.
Steel Plug experiment data is used in Mathematica calculation.
%mu'' = 0.136341 times 10^{-4} e^{ 1.14534 %mu' }

---
The following are results from Mathematica
Shunt impedance at 76 MHz = 151 kΩ, Q = 4347
R/Q at 76 MHz = 35 Ω

---
Rs comparison
Note: I divided Gennady's results by 2 because RF group's definition is always from rms, i.e.
Prms = Vrms2/Rs
 => Rs = Vrms2/Prms=Vpeak2/2Prms = Veff2/2Pthermal = Rgennady/2

---
Interesting points
- Transmission line (TL) model predicts Rs has a much higher Q at higher frequencies. Similar Rs at 76 MHz ~100 kΩ
  - For high frequencies, does this mean that losses are much higher from non-uniform B-field in MWS than uniform B-field in TL model?
- I'm not sure this makes sense:
  - MWS has lower losses at low frequency compared to TL model and yet its Rs is smaller than TL? Note: Rs is “poportional” to Q. Recall R/Q = ω0L.

---
Anode impedance
Zanode at this point
At 76 MHz = Ranode = 1.2 kΩ

---
Voltage along the cavity
Location of coupling capacitor
In terms of phase
In terms of position

---
Step up ratio
This is highly dependent on the coupling capacitance that we have chosen. Can be changed later.
Assume step up is 10 for now.
SSC etc. using step up of 8.
This choice affects the load line and thus the DC power losses.

---
Y567 Grounded Grid Load line
The two points that were chosen are:
Right hand point (Vanode = 11 kV – assuming stepup of 10, 1 kV screen voltage, and Vcathode = 250 V cathode to grid bias)
Left hand point (Vanode = 1.025 kV – screen to grid bias,
I peak = 4 * I0 = 15.97 A)
I0 = takes into account the inefficiency of class B operation, Vgap = 100 kV and Rshunt = 151.8 kΩ.

---
Fourier components
Idc = 4.88 A, and thus DC input power Vanode = 11 kV => Pdc = 54 kW.
I@76 MHz = 7.73A gives Prf = 38 kW
Efficiency = 0.72
The load resistance (which I assume is the anode resistance) = 1.3 kΩ
This number is consistent with the anode resistance calculated earlier = 1.2 kΩ
Latest numbers of anode resistance of 1.2 kΩ works very well for the Y567 where we want the number to be about 1.5 kΩ.

---
Y567 Grounded Grid Load line (Gennady's Rs=105.9 kΩ)
The two points that were chosen are:
Right hand point (Vanode = 11 kV – assuming stepup of 10, 1 kV screen voltage, and Vcathode = 250 V cathode to grid bias)
Left hand point (Vanode = 1.025 kV – screen to grid bias,
I peak = 4 * I0 = 22.89 A)
I0 = takes into account the inefficiency of class B operation, Vgap = 100 kV and Rshunt = 105.9 kΩ.

---
Fourier components (MWS numbers)
Idc = 6.5 A, and thus DC input power Vanode = 11 kV => Pdc = 71.4 kW.
I@76 MHz = 10.4A gives Prf = 52 kW
Efficiency = 0.73
The load resistance (which I assume is the anode resistance) = 0.96 kΩ
Don't know anode resistance yet from MWS. Need to put in coupler to get value.
0.96 kΩ works for the Y567.

---
Todo/Summary
- Is 10 pF a realistic choice for the coupling capacitor?
  - Impacts design of the coupling capacitor. Simple rescaling of LANL design gives 4 pF. (← This number needs to be checked with some other program)
  - Looks like coupling capacitor will need to hold off about 100 kV. I think this is doable. SSC cavity gap voltage is 127 kV. (PAC1993_0753.PDF)