## Slide 1: The LHC in Context & the Current Status Chandra Bhat Accelerator Division, Fermilab
January 12-16, 2015 CMSDAS, Fermilab
Abstract: Physics behind the CERN Accelerators and general aspects of circular accelerators is explained with an introduction to “collider luminosity“ as an introduction to the HEP graduate students. Current status of LHC operation for Run II and future upgrades for HLLHC is also outlined.

## Slide 2: Important Collider Parameters
Collider Luminosity
  Instantaneous and
  Integrated Luminosity
Types of beam, & Collision Energy (CM Energy, s )
Beam Parameters
  Number of Bunches
  Bunch Intensity
  Beam emittance (Transverse & Longitudinal emittance)
Lattice Parameters
  * (Beta function after squeezing of the beam at IP)
Beam Crossing Angle

## Slide 3: Luminosity Formula for a Collider
Beam Revolution Frequency
# of Bunches/beam
Transverse Beam sizes
For Beam-1 & Beam-2
* @ interaction point
(Lattice parameter)
Beam Transverse
Emittance
Instantaneous Luminosity
# of protons/bunch
for Beam-1 & Beam-2
Relativistic Factor
Correction term

## Slide 4: Luminosity
Luminosity relates the cross-section p and event rate
  For Fixed Target case depends on
    Flux of Incident beam
    # of target nuclei/unit area
L
L
Time variable
Kinematic factor
  In the case of the Collider
    the target is also moving. Assuming bunched beam, the L per bunch crossing is,
v1=1c
v2=2c
N1 and N2  number of particles /bunch
Lfix-Tgt=  T l 
x
s
y
Goal of the Accelerator is to maximize the Event Rate

## Slide 5: Collider Luminosity
Assume
  Head-on collision with magnitudes of velocities |v1|=|v2|
  Densities in all coordinates are uncorrelated:
    (x,y,s,s0)= x(x)*y (y)* s(s±s0) ; x Horizontal, y Vertical
  Density distribution function is Gaussian in each coordinate
  Transverse size: 1x 2x and 1y 2y, but bunch length 1s= 2s
  Then
; *x,y : Lattice beta-functions at interaction points &
x,y : Transverse Emittance of the beam
 2x,y =x,y *x,y
As the # of bunches increase the cross talk between in-coming and out-going bunches (beam-beam interactions) becomes an issue.
Solution: Crossing angle

## Slide 6: Collider Luminosity with Crossing Angle & other corrections; the case of LHC
Beam 2
Beam 1
= C
Instantaneous Luminosity with other Corrections:
For the LHC
(nb)Max= 2808 @25 ns bunch spacing,
N1=N2=1.15E11ppb, fo= 11.24kHz, *x= *y=0.55m,
c=285r, *x= *y=16.6m, s=7.5cm
W  Beam offset
S  Crossing angle
 Crossing angle and beam offset
H  Hour-glass factor from bunch length
LHead-on =1.2x1034cm-2s-1
LS =1.01x1034cm-2s-1
LS&H =1.00x1034cm-2s-1
Luminosity per Crossing
If N=N1=N2 L  N2 and linearly with nb .
L also depends on beam filling pattern
x

## Slide 7: Components of Accelerators
Magnets: Dipole (for bending), Quadrupole (for focusing), Sextupole, Octupole, Decapole, etc.,  These elements guide the beam, i.e., they control Transverse Beam dynamics
RF cavities  They help to accelerate the beam, i.e., they control Longitudinal Beam Dynamics
Beam Diagnostics and other instrumentation  They are essential constituents of any accelerator - help to monitor properties, behavior and control of the beam. Without beam diagnostics we are blind.
Example of beam diagnostics are
  Beam current monitors, Profile monitors, Loss monitors, Schottky noise monitors, quench protection systems, dampers, etc.

## Slide 8: Accelerator Lattice
A single “quad” can provide focusing of charged particle beam only in one plane. Hence, two quadrupole magnets are needed to achieve overall focusing.
fF= focal length of focusing quad
fD= focal length of de-focusing quad
L = Distance between two quads
Optics
fF
fD
L
Focusing
Sextupole
k(s)
Nomenclature
Symmetric FODO
FODO Lattice:
A lattice comprising symmetric quadrupole triplets that can focus beam in both X and Y planes
1/2QF
1/2QF
QD
FODO Period
A Lattice is formed by a series of magnetic elements which guide the charged particle beam from one point to another through a vacuum beam pipe.
Lattice may be for
  Beam transfer line
  Circular accelerator and Storage ring
  Linear accelerator

## Slide 9: Betatron Motion
The particles in a FODO lattice oscillate within an ENVELOPE in the transverse plane. The number of such oscillations around a ring is called Transverse Tune
  Horizontal tune (QH or H)
  Vertical tune (QV or V)
These oscillatory motion are governed by,
General solutions to the Hill’s equations are given as,
H = 64.28 at inj., = 64.31 at collision
V = 59.31 at inj., = 59.32 at collision
for the LHC
One can combine these two into one equation as,
0 is bending radius and
K(s) is focusing strength
or spring constant
“Hill’s equations”
Transverse Emittance Beta-function
Tune 
phase advance
Envelope function

## Slide 10: Aspects of Transverse Beam Dynamics
FODO Lattice
Trajectory of a particle on several successive revolutions
Beam Pipe
Straight Section
Bending Magnets
(Main Dipoles
with correctors)
LHC SC Dipoles
IP. QuadMagnets
Quadrupole Magnets
Envelope
Function=A(s)
Add Beam diagnostics:
Loss Monitors
Position Monitors
Profile monitors
Special Devices
Injection Devices
Extraction Devices
Beam Abort System
Scrapers
IP
Beam
Envelope
Function
=E(s)
Close Orbit
LHC SC Quad

## Slide 11: LHC x@Inj. & @Collision
<x,y> ~86m
Max ~4.5km
* ~0.55m

## Slide 12: Components of Accelerators - RF
RF Cavity: A device used for
bunching, beam capture,
acceleration,
rf manipulation like bunch
  compression, rotation,
  shaping beam bunches,
  bunch splitting, coalescing
  multiple bunches,
  and many rf gymnastics.
Synchronous beam from
one accelerator to another
To keep up with the energy losses
during storing (loss ~7keV/turn)
in a collider like LHC,
and many more.
Single-Cell
SC cavity
TM010 mode
Multi-Cell SRF
LHC 400MHz 4-SRF cavity/cyro-module with 2MV/cavity
LHC 400MHz SRF in the LHC tunnel
at 4.50K

## Slide 13: What an RF system can do? Aspects of Longitudinal Beam Dynamics
Coasting Beam with Energy E0±E
Beam Pipe &
the Beam
RF Bucket
Boundary
Beam
Vrf

t
A contour of
constant Hamiltonian
Synchronous Particle
Phase-space Area of a Bunch is
Longitudinal Emittance
Measured in eVs
Closed Orbit
Beam
Storage Ring
RF Cavity


Bunched Beam
AC
rf= hrev
harmonic number h=1
Vrf
t
Sinusoidal
Vrf
t
Sinusoidal
AC
rf= hrev
harmonic number h=2
RF Buckets
Vrf
E
WCM Data
t
RF
Buckets
E
WCM Data
Vrf
t
Sinusoidal
AC
rf= hrev
harmonic number h=2
Bunch Compression
E
WCM Data
Buckets of higher harmonic RF system
Beam Acceleration
Vrf
t
Sinusoidal
AC
rf= hrev
harmonic number h=2
Accelerating RF Buckets
and
Accelerating Beam Bunches
E
Accel. /turn=EAcc=V0sin 
WCM Data
h=35640 for the LHC, frf=400MHz (Vrf)peak=16MV
Max. No. of Bunches =2808 @25nsec bunch spacing
Max. No. of Bunches (2012)=1383 @ 50 ns bunch spacing

## Slide 14: CERN Accelerators
LHC (Lum. upgrade) I worked on these
SPS (single bn. Instability) accelerators
PS (bn. Int. & e-cloud) during my sabbatical
at CERN
from 2010-2013
50 MeV
26 GeV
450 GeV
450 GeV
450-7000 GeV
LINAC-2 50MeV
PSB 1.4GeV
PS 26GeV
SPS 450GeV
LHC 7TeV
1bn x4
6bn(h=1?)
36bn (h=84?)
144bn(h=4620)
1380bn(h=35640)

## Slide 15: A Schematic of LHC Operational Cycle
LHC Turn around: 2-3 hours on a good day
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
450 GeV
3.5 TeV
Beam loss during
squeeze
12-SPS batch Injection

## Slide 16: PS Produces the Bunch-Filling Pattern for the LHC 25ns, 50 ns or 12.5 ns
LHC50
36 bunches
Bunch intensity was limited to <1.8E11ppb on LHCINDV prior to 2010
PS Acceleration 3.4 sec
Six PSB Bunches at 1.4 GeV
A
B
C
During June-August 2010 lots of effort were made to produce high-intensity bunches in the PS with >3.5E11ppb with LE(4)< 0.29 eVs & x,y <3 m
LHC25
72 bunches
PSB to PS injection at 1.4 GeV and triple splitting at injection.
1.4 GeV  26 GeV acceleration
  Double splitting for
  50 ns LHC fill
  Quadruple splitting for
  25 ns LHC fill
  Octuple splitting for 12.5 ns if needed

## Slide 17: High Intensity Bunches in 2010-12
Issues with high intensity bunch-trains:
  Prepare PS for acceleration,
  Transfer and acceleration in the SPS and LHC
    The SPS-Q23 lattice(old) was abandoned.
    A new SPS-Q18 lattice became operational.
High intensity single bunches were used to investigate
  SPS:Transverse Mode Coupling Instability (TMCI) and
  Single Bunch Longitudinal Instabilities (SBLI)2010-11
  LHC: Test runs with high intensity bunches 2010-12
    event pile-up & beam-beam tune shift (W. Herr et. al.)
    TMCI and SBLI (E. Shaposhnikova et. al.)
Ultimately, PS batch of 36 stable bunches with 50ns spacing & ~1.7E11ppb were used in the LHC for the HEP during 2011-12 operation.
LIU (Leader: Roland Garoby): A massive effort is being put to upgrade PS, SPS to handle high intensity beam.
Malika Meddahi

## Slide 18: Peak performance through the years
 | Nominal | 2010 | 2011 | 2012
Energy [TeV] | 7 | 3.5 | 3.5 | 4
Bunch spacing [ns] | 25 | 150 | 50 | 50
No. of bunches | 2808 | 368 | 1380 | 1380
beta* [m] ATLAS and CMS | 0.55 | 3.5 | 1.0 | 0.6
Max bunch intensity [protons/bunch] | 1.15 x 1011 | 1.2 x 1011 | 1.45 x 1011 | 1.7 x 1011
Normalized emittance [mm.mrad] | 3.75 | ~2.0 | ~2.4 | ~2.5
Crossing Angle (urad) | 285(H&V) |  | ~100 (H&V)? | 145(H&V)
Peak luminosity[cm-2s-1] | 1.0 x 1034 | 2.1 x 1032 | 3.7 x 1033 | 7.7 x 1033
Ave. Pileup at Start | 26 | 8 | 17 | 38

## Slide 19: Typical LHC pp-store-Week Eight Nice Fills (Mid Oct., 2012)
Fill # 3188, Store Length= 6:56 h,
Lpeak=6.7x1033cm-2s-1, LInt= 0.105fb-1
Fill # 3192, Store Length= 10:39 h,
Lpeak=6.8x1033cm-2s-1, LInt= 0.154fb-1
Fill # 3194, Store Length= 12:34 h,
Lpeak=6.5x1033cm-2s-1, LInt= 0.167fb-1
Fill # 3200, Store Length= 8:17 h,
Lpeak=6.5x1033cm-2s-1, LInt= 0.105fb-1
Fill # 3201, Store Length= 10:17 h,
Lpeak=7.4x1033cm-2s-1, LInt= 0.133fb-1
Fill # 3203, Store Length= 11:42 h,
Lpeak=7.1x1033cm-2s-1, LInt= 0.175fb-1
Fill # 3207, Store Length= 4:10 h,
Lpeak=7.7x1033cm-2s-1, LInt= 0.fb-1
Fill # 3185, Store Length= 7:45 h,
Lpeak=6.8x1033cm-2s-1, LInt= 0.122fb-1
B1
B2

## Slide 20: Summary of 2010-12 LHC – pp Luminosity Performances
2010: 0.04 fb-1
  7 TeV CM
  Commissioning
2011: 6.1 fb-1
  7 TeV CM
  Exploring the limits
2012: 23.3 fb-1
  8 TeV CM
  Production
Higgs
Discovery
July 4th, 2012

## Slide 21: Main Challenges during Run I
2010-2013 the LHC was running with  50 ns bunch spacing for “Physics Runs”. However, was unable to run with nominal 25ns bunch spacing. Identified challenges were,
  Electron Cloud
  UFO (Unidentified objects) near injection regions  Unintentional beam aborts
  Potential equipment damage
  Beam induced heating
  Collective effects and impedance
  Magnetic field perturbations & field quality
  Triplet aperture and beam-beam
72x 2.2E11ppb(25ns)
36x 3.5E11ppb(50ns)
Emax=239.5 eV
T =2.5 m

## Slide 22: Buildup of Electron Cloud at the LHC & consequences
Primary Source of electrons in the LHC
  At Injection (450 MeV) gas ionization
  At 7 TeV Synchrotron Radiation
Possible consequences:
  - instabilities, emittance growth, desorption bad vacuum
  - excessive energy deposition in the cold sectors
The critical energy of the photons at
7 TeV ~ 44 eV

## Slide 23: What e-cloud can do to the Beam?
~33% Horizontal
~110% Vertical
Associated beam loss
Measured Emittance Growth
Injection Intensity
End of fill Intensity
Fill: 2249 (2011)
25 ns Bunch Spacing
Energy = 450 GeV
Time between Injection to End ~10 min
Dumped by BPM
1020 Bunches
Intensity
Bunch #

## Slide 24: Mitigation of e-cloud in the LHC
Electron bombardment of a surface reduces secondary electron yield (SEY) of a material
Observed Reduction of SEY by beam scrubbing
2011 Scrubbing
G. Iadarola, G. Rumolo
Commissioning with beam
13/03
05/04
75ns physics run (nominal)
12/04
21/02
First 1380 bunches in LHC
28/06
18/07
30/09
ex,y decreasing towards 1.1mm
Nb increasing towards1.45 x 1011 ppb
50ns beams
1.1x1011ppb
Scrubbing run 50ns
Physics run 50ns
30/10
An example of scrubbing 2011
2012 Scrubbing
However, scrubbing with beam with 25 nsec bunch spacing alone probably is insufficient to fully suppress e-cloud

## Slide 25: LHC: Coming up from a 2 years shutdown Main Repairs
A 13kA splice has a resistance of about 300 pΩ, which can be measured with a precision ~20pΩ. The acceptance criteria is 10 nΩ. Any splice does not meet this criteria is replaced/repaired.
The resistance acceptance criteria at the Cu - superconducting splice joints was 5 Ω. Any joint does not meet this criteria is replaced or repaired.

## Slide 26
« Old Splice » « Machined Splice » « Consolidated Splice »
« Insulation box »
« Cables » « New Splice »
Total interconnects in the LHC:
  1,695 (10,170 high current splices)
Number of splices redone: ~3,000 (~ 30%)
Number of shunts applied: > 27,000
And a lot more besides…
(from Mike Lamont, 11/2014)

## Slide 27: Current Status of the LHC
PS: Restarted in 3rd week of June 2014
SPS: Beam to SPS during 3rd week of September, 2014
LHC: All the sectors are completely repaired. The magnets have been "trained" and tested to full current only in 2 sectors (12 & 67), 56 and 81 are being trained, 4-more to go. (info from Bob Flora).
LHC Commissioning with beam is planned to start on week 11 of 2015 (i.e., 2nd week of March)
Beam for physics – Late Spring 2015?
12
45
34
81
78
56
67
23
1.9K
1.9K
1.9K
1.9K

## Slide 28: LHC – 2015-2017
When the LHC is turned on this year, this will be a brand new machine.
Beam Energy: 6.5 TeV
Many Challenges are expected
  All magnet circuits are tested before and during installation.  Need adjustments during operation
  Potential equipment damage in case of failures during operation. In case of failure the beam must never reach sensitive equipment!
  Requires good optics and orbit control!  feedback loops
  May need Tighter Collimation than design!
  Design: 6 for primary collimators & 7 for secondary collimators
  Beam with 25 ns bunch spacing. Long range beam-beam effects will be larger than that observed in 2010-2012
  + All the problems encountered during Run 1.
    e-cloud, UFO and etc.
summary from Mike Lamont

## Slide 29: LHC Performance Goal 2015-…
 | LHC nominal 25ns | LHC 2012 50 ns | LHC2015 25ns | LHC2015 25ns (BCMS)
Beam Energy (TeV) | 7 | 4 | 6.5 | 6.5
# Bunches | 2808 | 1380 | 2748( or 2736) | 2508( or 2496)
p/bunch [1011], I[Amp] | 1.15, 0.58 | 1.6,0.42 | 1.2,0.59 | 1.2, 0.54
gex,y [mm] | 3.75 | ~2.5 | 3.1 | 1.7
eL [eV.s] | 2.5 | 2.5 | 2.5 | 2.5
Effective beam size (m) | 22 | 19 | 24 | 18
sz [cm] | 7.5 | 7.5 | 7.5 | 7.5
sdp/p [10-3] | 0.1 | 0.1 | 0.1 | 0.1
b* [cm] ,Xing Angle[rad],b-b sep [] | 55 | 60,145,10 | 80,290,11 | 80,290,11
Ultimate in 2015  |  |  | 40 | 40
Peak lumi [1034] | 1.0 | 0.76 (peak) | 0.85 | 1.29
Lumi loss Factor/Geometric Factor | 0.84 | 0.96 | 0.87 | 0.79
Tleveling [h] @ 5E34 | No Leveling | No Leveling | No Leveling | No Leveling
#Pile up | 25 | 35(max) | 22 | 36
Max Stored Energy[MJ] | 362 | 140 | 342 | 311
PS: Bunch splitting schemes 

## Slide 30
LHC for next 20 years
Very preliminary and very likely to change
HL-LHC era
peak =7.7nb-1/s
total =30fb-1
Pileup(Max)~35
Bunch spacing=50ns
peak =17nb-1/s
total =100-200fb-1
Pileup(Max)~42
Bunch spacing=25ns
peak =20nb-1/s
total ~250fb-1
Pileup(Max)~42
Bunch spacing=25ns
peak =50nb-1/s
total ~3000fb-1
Pileup(Max)~140
Bunch spacing=25ns
30
Run 1
Run 2
Run 3
Long Shutdown-1( )

## Slide 31: HL-LHC Official Beam Parameters
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 2.2E+11 | 3.5E+11
nb | 2808 | 2808 | 1404
beam current [A] | 0.58 | 1.12 | 0.89
x-ing angle [mrad] | 300 | 590 | 590
beam separation [s] | 10 | 12.5 | 11.4
b* [m] | 0.55 | 0.15 | 0.15
en [mm] | 3.75 | 2.5 | 3.0
eL [eVs] | 2.5 | 2.5 | 2.5
energy spread | 1.20E-04 | 1.20E-04 | 1.20E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02
Piwinski parameter | 0.68 | 3.1 | 2.9
geom. reduction | 0.83 | 0.35 | 0.33
beam-beam / IP | 3.10E-03 | 3.9E-03 | 5.0E-03
Peak Luminosity | 1E1034 | 7.4E1034 | 8.5 1034
Virtual Luminosity | 1.2E1034 | 21E1034 | 26 1034
Events/Crossing | 26 | 210 | 475
(Leveled to 5x1034 cm-2 s-1)
140
One can regain the lost Luminosity due to crossing angle by introducing Crab-cavity

## Slide 32: Collider Luminosity with Crab Crossing
Beam 2
Beam 1

Crossing scheme
c=
Beam 2
Beam 1
Crab Crossing scheme
With transversely
Deflecting cavities
Crab Cavity
Crab Cavity
Crab Cavity
Crab Cavity
For the HL-LHC Beam parameters
LH =21x1034cm-2s-1
LS&H =7.4x1034cm-2s-1
Crab-Xing
Gain by
Reduction due
to Xing angle
Luminosity Leveling 5x1034cm-2s-1 at pileup~140/collision
Changing the * - Transverse offset
Manipulating the crossing angle - Use crab cavity to change the beam overlap
Old Dominion University
Bob Palmer 1988
Added gain in Luminosity by a factor 2 using crab-kissing
(flat bunches with
crab-cavity)

## Slide 33: Acknowledgements
Frank Zimmerman, Oliver Bruning, Mike Lamont, E. Prebys
Elena Shaposhnikova, G. Rumolo, Roland Garoby, and
Gianluigi Arduini
PS Collaborators:
  Heiko Damerau, Steven Hancock, Edgar Mahner,
  Fritz Casper
SPS Collaborators
  T. Argyropoulos, J. Esteban Müller,T. Bohl, W. Hofle,
  E. Metral, G. Iadarola, B. Salvant, M. Taborelli,
  J. Tuckmantel, H. Timko
LARP and Fermi Research Alliance under U.S. DOE Contract.
Special thanks are due to Bob Flora

## Slide 34: Summary
I have given you a simple overview of the physics of CERN accelerators and operating scenarios.
LHC started in 2008 with a glamorous start – but a disaster strikes!
  2008-10 LHC was fixed partially, learned a lot of lessons.
Restarted in 2010 and had a phenomenal run providing Lintg~30 fb-1 to CMS and ATLAS collider detectors during 2010-12
   Discovery of the Higgs Boson in 2012
Further “consolidation” 2013-15: repaired and replaced all of the defective electrical connections (several thousands!) and many more.
Currently, testing of the accelerator components underway, to run the LHC with beam energy of 6.5TeV
Run 2 (2015-17):
  Run at CM energy of13TeV – may start with 50 ns bunch spacing?
  25 ns bunch spacing with~ 2736/2496 bunches, *=80cm and going to *=40cm (in 2015)
Contact: cbhat@fnal.gov

## Slide 35: References
Practical Accelerator Physics,
http://www-ap.fnal.gov/users/cbhat/
Particle Accelerator Physics, H. Wiedemann (Springer, 1999)
An Introduction to Particle Physics High Energy Accelerators, D. Edwards and M. Syphers (John Wileyand Sons, Inc, 1993)
Accelerator Physics, S.Y. Lee (World Scientific, 1999)
Hand Book of Accelerator Physics and Engineering - Edt by A. Chao and M. Tinger , World Scientific (1999)
CAS CERN Accelerator, Accelerator Physics Courses
http://cas.web.cern.ch/cas/CAS%20Welcome/
Previous%20Schools.htm

## Slide 36: Backup-Slides

## Slide 37: Introduction: Terminology in Accelerator Physics
Units: I will try to stick to the MKS system.
Energy Units:
eV: It is the amount of kinetic energy gained by a single unbound electron when it passes through an electrostatic potential difference of one volt,
keV=103*eV, MeV, GeV, TeV etc.
Momentum:
Measured in units of [MeV/c], [GeV/c], [TeV/c]
Beam Current: ; Unit of current = Amp
= 1 Coulomb/sec
  Beam Transport: Beam particles pass only once
  Circular Accelerator: Same particle goes through the same section f times/sec
e-
1Volt
1 eV
At low energies Total energy >> KE
At high energies KE~ Total energy
Charge passing through/unit time

## Slide 38: Some History of LHC Startup – Bright Startup
~4km of the LHC Ring was badly damaged
SC splices at the joints
Complex connections
between two dipoles
Public display of the
Dipole magnet
2008: Accelerator complete. Ring cold and under vacuum.
Sept. 10th 2008 by 14:59 hr
  First beam around the ring
Sept. 19th 2008 around noon: DISASTER while ramping Sect. 3-4 to 5.5TeV
2008–2009: 14 months of major repairs
  Replaced ~50 SC magnets in that sector
  Inspected all the sectors
  New Quench Protection System for online monitoring and protection of all joints.
However, uncertainties existed about the splice quality through out the 2010-2013 runs
  Because of this Risk
   decision: limit the beam energy to 3.5 TeV
  “This is HISTORY & we learned a lot

## Slide 39: Crab Kissing Scheme
Using crab cavities to level luminosity and lower peak interaction density

## Slide 40: Pile-up or # of Interactions/Bunch Crossing
For Example during the 2012 LHC run:
(Pileup) Max Lumi = (7.7E33cm-2s-1/ 1380 bunches/11245Hz)x(70mBarn)
= 34.7
Special Run with high intensity bunches had pile-up~75
CMS Ave. Pile-up, pp, 2012,
s=8 TeV

## Slide 41: Components of Accelerators
Magnets: Dipole (for bending), Quadrupole (for focusing), Sextupole, Octupole, Decapole, etc.,  Control Transverse Beam dynamics
RF cavities  Control Longitudinal Beam Dynamics
Beam control and Monitoring Systems
LHC Dipole Magnet: A device used to bend the path of charged particles during beam transport.
1.90K, Nb-Ti, 8.4Tesla (max),
14.3 m long, 56mm opening
Monochromatic
beam
Field-free region
& Beam
LHC Quadrupole Magnet: A device used to focus charged particle beam during beam transport.
Ni-Ti, 1.90K 223T/m
3.2 m long
56mm opening
Mag. Field Lines
Examples of LHC Magnets

## Slide 42: Components of Accelerators
Sextupole Magnet: Beam will have #0 (~10-4 for LHC). Beam needs chromatic corrections. Sextupole magnets are devices used for chromatic corrections.
Similarly, ring needs Octupole corrections. And other high-order corrections….

## Slide 43: LHC 400MHz SC accelerating module
Cryo-module

## Slide 44: LHC collimators (87 in number)
Fig. 1. An illustration of multi-stage cleaning in the transverse beam planes. Primary collimators intercept the protons that are lost from the beam core. The leakage from this single-stage cleaning would be well above the quench limit of superconducting magnets. Secondary collimators and absorbers are used in insertion regions IR3 and IR7 to intercept halo protons and hadronic showers produced by beam particles interacting with the collimator jaws during the multi-turn process. Additional tertiary collimators ensure further protection close to the experiments.

## Slide 45: LHC Beta-function at Injection & Collision
Max~4.5km
-function @ IR is after squeeze is *

## Slide 46: Hour-glass Effect (Back up slide)
Significant effect on long bunches when * is small: * ~ s
Behavior of the lattice
 function abound
interaction points
in the LHC
Envelop of the
beam in the vicinity
of interaction point of the LHC
A short bunch
A long bunch

## Slide 47: LHC Beam & Loss during Squeeze

## Slide 48
Some issues in LHC 2011-12 operation
UFOs
20 dumps in 2012
time scale 50-200 µs
conditioning observed
worry about 6.5 TeV and 25 ns spacing
Radiation to electronics
concerted program of mitigation measures (shielding, relocation…)
premature dump rate down from 12/fb-1 in 2011 to 3/fb-1 in 2012
T. Baer
Beam induced heating
Local non-conformities (design, installation)
  injection protection devices
  sync. Light mirrors
  vacuum assemblies

## Slide 49: Layout of the LHC
The LHC is a technological marvel
The Accelerator is 27 km around
Consequently, the commissioning and operation of this accelerator could be very challenging!
– a lot of safety measures should be taken.
Design:
150 tonnes Helium, ~90 tonnes at 1.9 K
363 MJ/beam stored beam energy
2012 : 140 MJ/beam stored beam energy
@4TeV 450 MJ magnetic energy/sector
HL-LHC: ~700 MJ/beam stored beam energy
@7TeV ~800 MJ magnetic energy/sector
~9000 magnetic elements
1720 Power converters
7568 Quench det. systems
1088 Beam position monitors
4000 Beam loss monitors

## Slide 50: LHC Inner Triplet Quad-Magnets used in four IRs
Beam size by
~100 times
Field Strength= 215-230 T/m Operate at 1.90K