## Slide 1: Beam Injection and Capture
Chandra Bhat
Fermilab
Acknowledgements
W. Pellico, B. Chase, S. Chaurize,
C. Drennan, F. Garcia, B. Hendrick, J. Nelson*, K. Seiya,
T. Sullivan, C. Y. Tan, K. Triplett, M.-J. Yang
and
MCR Operation Group
“Workshop on Booster Performance and Enhancements”
Fermi National Accelerator Laboratory
November 23-24, 2014

## Slide 2: ABSTRACT
The Fermilab Booster is going to play very significant role for nearly next two decades in view of recent accelerator upgrade proposal, PIP-II. In this context, it is extremely important to measure and understand as found properties of the Booster from beam injection to the extraction. In this talk we present results from a recent measurement on momentum acceptance and beam energy spread for multi-turn beam in the Booster. We also discuss results from the early beam injection scheme that has a high potential to increase the beam intensity output from the Booster even before the PIP-II era and also help mitigate beam losses from the Booster.

## Slide 3: The Proton Improvement PlP
Goal
The Proton Improvement Plan, when executed, should enable Linac/Booster operation capable of
  delivering 2.25E17 protons/hour (at 15 Hz) safely to the ongoing neutrino programs “next decade or two”.
The Proton Improvement Plan-II Strategy
  Deliver  1.2MW beam power to the LBNF. PIP-II still uses current Booster
Booster would play a very significant for next two decades
“Yes, Booster is in its Forties. Still it has lot more juice”
  Revisit: Injection, Acceleration, Tran. Xing, Extraction &
S. Henderson,
Proton Source Retreat,
Dec. 7-8, 2010
S. Holmes,
P5/BNL,
Dec 16, 2013

## Slide 4: (Schematic)
Issues: A limited time for Beam Capture & Acceleration. RF manipulations are non-adiabatic  ~50% emittance dilution, ~7-8% beam loss and large RF power
~60s-200 s debunching
 40s
injection
Begin Inj.
Capture & Acceleration using
37-52 MHz RF system in 360s
Current Scheme (CIS)
LINAC
Beam
Booster
Booster
Synchrotron
Beam Injection in the Booster

## Slide 5: Beam Injection and Capture
Needs a good understanding of
  Properties of the beam from the LINAC
    Beam Energy Spread, E (full)
    H and V Transverse Emittances
  Acceptance at Injection
    Momentum Acceptance
    Transverse Acceptance
  Beam capture and Acceleration
    Current Operation
    Future Plans – “Early Injection Scheme”

## Slide 6: Measurement of Beam Energy Spread
H- beam of 0-40µsec from the LINAC is injected into the Booster
(Booster revolution period To ~ 2.216µsec).
We have measured the E of the beam
  Downstream of the LINAC
    Using the magnetic spectrometer
    Using the multi-wire data from 400 MeV transfer line and fitting to the known lattice
  Partial turn beam in the Booster
  Multi-turn circulating beam in the Booster by creating a notch

## Slide 7: Multi-wire data with MAD overlay
Data is consistent with
E(full) = 1.56 MeV
H = 7 -mm-mr
V = 7 -mm-mr
But, this measurement does not give info. on multi-turn beam in the Booster.

## Slide 8: E at Injection on Multi-turn Beam
Principle of Measurement
(schematic of WCM data)
At Notch formation
After some Revolutions
High and Low meet
Some more Revolutions later
D
D
D
D’
Beam before
a Notch
A1
A2
A1
A2
A1
A2
A1’
A2’
A=A1+A2
A=A1+A2
A=A1+A2
A>A1’+A2’
Wnotch = Width of the Notch
Tgraze = Time for grazing touch
<E>(full) = 1.360.11 MeV
<dP/P>(full)=0.20 0.02 %
B96
WCM data
Notch at
formation

## Slide 9: Measurement of Momentum Acceptance
Beam Momentum @Inj
E
Total Momentum
Acceptance
Beam
Bmin  B:VIMIN
Central Momentum
A
B
A
B
Beam loss at injection – small loss at the beginning & total loss later
Beam loss at injection – Continuous loss
P
t
RF OFF

## Slide 10: Measurement of Momentum Acceptance (cont.)
A
B
Beam at B:VIMIN=101.842 AMP
Standard Aperture Scan
Energy Acceptance of the Booster = E((Bmin)) + E(full)Beam
= 4 MeV (0.4 MeV)+1.36MeV (0.11 MeV)
= 5.4 MeV (0.4 MeV)
LOSS Monitors
Beam Intensity
Monitors

## Slide 11: (Schematic)
~60s-200 s debunching
 40s
injection
Begin Inj.
Capture & Acceleration using
37-52 MHz RF system in 360s
Current Operation
Beam Capture and Acceleration
Chandra Bhat
Paraphase Angle
Vrf
Vrf0
Vrf0

## Slide 12: Beam Capture in the Current Operation
WCM Data of 20151107 with 4.5E12p/Booster pulse
Starts Beam Capture
Represents “start” and “end” points of beam capture
Ends Beam Capture
Beam capture is carried out in ~30 turns (~70 µsec) in the current operation. This is mainly because the beam injection is done close to Bmin and there is not enough time to finish capture before acceleration commences.
Accel. Gate “ON”
Beam Feedback “ON”
Paraphase “ON”
B:VAPLON=2090 µs
B:TFBON=2130 µs
B:VXTPPP=2050 µs

## Slide 13: Current Operation RF Voltage during Capture
B:PARAT
(Operational)
Vrf
(Operational)
Vrf
(adiabatic)
Bucket Area
= 0.070 eVs
Bunch Area=0.04 eVs
by simulation
Bucket Area
= 0.096 eVs

## Slide 14: Simulation (ESME): Phase-Space Evolution during Beam Capture - 14 BT Beam
Operational Beam: injection at ~0 us before BDOT=0
Injection at -35s w.r.t. BDOT=0.0
L at the end of beam capture = 0.06 eVs (~60% dilution)
with ~5% beam loss

## Slide 15: Schematic of the
 40s
injection
capture for >260s (no debunching)
150s
Begin Inj.
Beam Acceleration using
37-52 MHz RF system
Change in
Es <0.24MeV
1/15Hz  0.0666 s
Impose Beam Capture in
Stationary rf Buckets (=0)
Start End
C. M. Bhat, IPAC2015
Early Injection in the Booster
with a pseudo front-porch
Energy Acceptance > 4MeV
Beam E  1.3MeV
fsy = 8kHz-27kHz @ Vrf=0.035-0.4MV
pseudo front-porch in the Booster

## Slide 16: Simulation (ESME): Phase-Space Evolution during Beam Capture - 14 BT Beam
Early Injection: injection at 175us before BDOT=0
Injection at -175s w.r.t. BDOT=0.0
L at the end of beam capture = 0.040 eVs (~ 6% delution)
no particle losses

## Slide 17: Beam simulations from Injection Extraction
with 12E10p/bunch

## Slide 18: Beam Experiments
New Radial-position, Paraphase and Simulated Vrf curves are used
Transition crossing  Needed additional tuning
(Preliminary)

## Slide 19: Future Plans
Beam capture soon after the completion of the beam injection,
A better frequency synchronization between the LLRF and real frequency,
Implement phase corrections/jump at transition crossing. This gives better match between bunch and the RF bucket,
Fast bunch rotation Gives lower beam energy spread at extraction. Hence, is better for slip-stacking in RR.
Make it Operational by next shutdown
We have done first attempt
LLRF is ready. Waiting for beam time
Module is ready to go into BLLRF
Not applied on the EIS

## Slide 20: Summary
Are learning a lot about the Booster in recent years: Identified several issues related to beam injection , beam capture, Tran Crossing & etc.... Come out with a new injection scheme, EIS, for the Booster.
If EIS is implemented then the implications are
Higher brightness beam to the downstream machines
One can increase the Booster beam power at extraction, because more number of Booster turns can be accommodated
Booster can be run with 20% less RF power per cycle  This is a great bonus.

## Slide 21: Backup Slides

## Slide 22: Early Capture – Measurements (Preliminary)
EIS
FWHM 10 nsec
FW 18 nsec
Vrf=0.72kV
Oper.
FWHM 13 nsec
FW 21 nsec
Vrf=0.72kV
Relative Beam
Mountain Range
For Capture
WCM
WCM
Beam
RF
Bdot
Single Bunch
@ the end of capture
Single Bunch
@ the end of capture

## Slide 23: IPM Data on the EIS and a comparison with Operational cycle (Nothing Unusual)
Average of H and V beam sizes
during the first 500 turns
Average of H and V beam sizes
during the entire beam cycle

## Slide 24: PIP parameters with EIS
Parameter | PIP | PIP-II (After 2022)
Injection Energy (KE) (GeV) | 0.4 | 0.8
Extraction Energy KE (GeV) | 8 | 8
Injection Intensity (p/pulse) | 4.52E12 (x ~1.4) | 6.63E12
Extraction Intensity (p/pulse) | 4.3E12 (~6E12) | 6.44E12
Number of Booster Turns | 13 (18) | 300
Efficiency (%) | 95 (97) | 97
Booster repetition rate (Hz) | 15 | 20
Booster Beam Power at Extraction (kW) | 94 (~130) | 184
MI batches | 12 every 1.33 sec | 12 every 1.2 sec
NOvA beam power (kW) | 700 (~950) | 1200
Rate availability for other users (Hz) | 5 | 8
Booster flux capability (protons/hr) | ~ 2.3E17 (3.2E17) | ~ 3.5E17
Expected by adopting Early Injection Scheme