Mechanical Design
C.Y. Tan
28 Jan 2016

---
Discussion topics
- Garnets
  - Size
  - Cooling
  - Glue the sectors
  - How to stack?
    - Glue
    - Grease
    - Compression
- Windows
  - Shape of window in the accelerating cavity
  - Shape of window in the power coupler

---
What we need to cover (cont'd)
- Assembly (weld?)
  - 3 parts
    - Garnet section
    - Neck section
    - Power coupler section
  - Needs to be done, but not yet ...
    - HOM section
    - Solenoid section

---
SSC LEB uses epoxy

---
Tuner Pros/cons
- Epoxy
  - One block, cannot fix bad garnets or alumina
  - Expansion?
  - Bubbles – caused SSC tuner to vapourize.
- Grease
  - Unknown decrease of Q
  - Unknown problems and performance in radiation area.
    - Mixed waste
- Braze cooling
  - Effect on garnet is unknown
  - Alumina is well known
- Compression stack
  - Like in Booster tuner
  - Bigger garnets (possible), but RF path?
    - Largest size is about OD 15.354 inches = 390 mm. Our garnet OD is 340 mm. Therefore we have an edge of (50/2 = 25 mm).
  - Also longer because of thickness of copper.
  - Bigger radially also causes problems for solenoid.

---
Booster cooling rings

---
Iouris' first pass