## Slide 1: NMG Visit and Mechanical Assembly Update
Kevin Duel
Booster 2nd Harmonic Cavity
7 April 2016

## Slide 2: NMG Visit
Overall a very positive visit
Spoke with machinist
  Excited about the challenge/opportunity
  Our tolerances call out +/- .005 – they can typically achieve better than +/- .002
  Have achieved even better tolerances in the past for special projects
  Chipping mostly occurs during handling
    Apply Teflon tape to work surfaces
    We should reconsider having them perform gluing
  Explained how pieces are chucked and supported
    For OD and ID, often glue on additional ferrite to grab onto which is later surface ground off
    Ensures piece will not be supported by alumina
  Making angular cuts to form ring without gaps will be the most difficult
    Might need to make final piece a “keystone”

## Slide 3: NMG Visit
Parts are inspected by QC department to verify specs are met
Packaging/shipping
  They will design and provide packaging for shipping back and forth
  Can use “shock sticker” if desired
  Will strap box to pallet

## Slide 4: NMG Visit
Cannon used to pressurize powder with water and form into pre-fired shape

## Slide 5: Mechanical Assembly Update

## Slide 6: Mechanical Assembly Update