Effect of coupling capacitance change
C.Y. Tan
05 Jan 2017

---
What happens when the coupling cap is changed by ±5% steps?
- Use the transmission line model to calculate the impedance seen by the tube.
- The changes in the real and absolute value of the impedance are small except at high frequencies. The imaginary changes quite a bit.
- For matching to the tube, not clear that changing the coupling cap is going to do a lot.

---
Interesting that Gennady’s impedance has the opposite curvature.