## Slide 1: PA test simulations.
2nd Harmonic cavity meeting
February 2, 2017
Gennady Romanov, Robyn Madrak.

## Slide 2: New model (Robyn, 2/2/2017)
Gennady and I measured dimensions of real (cut apart) tetrodes and Gennady made a model of this in CST
I took this model and inserted it into the test station model
Data:
  f0 = 71.7 MHz, Zanode = 1.3 – 1.4 k
CST:
  f0 = 70.016 MHz, Zanode = 1.5 – 1.6 k
The more simplistic model also did not agree with data, but gave a higher f0
What would be the effect on the real cavity? Presumably maximum shift of ~ 2 MHz but probably less
  Would effect be absorbable by tuning to lower f, or would we wind up with the garnet being too lossy?

## Slide 3: Minor corrections
Gap removed, resistor placed between electrodes
Removed
Added

## Slide 4: Result of corrections
Chart: L, length of coax, inches
| 0 | 1.925 | 2.9249999999999998 | 3.9249999999999998 | 4.9249999999999998 | 5.9249999999999998 | 6.9249999999999998 | 7.9249999999999998
Eigenmode | 72.885 | 72.476 | 72.2994 | 72.1851 | 72.0732 | 71.975 | 71.8888 | 71.814
Frequency domain | 72.322 | 72.162 | 72.027 | 71.912 | 71.817
L
The corrections increased frequency up to 70.9 MHz, still not enough.
The frequency is very sensitives to the port length, so it was decided to
check the waterload.

## Slide 5: Waterload
Line imp. 41 Ohms (D=2.976”, d = 1.325”)
Water

## Slide 6: Waterload simulations
The parameters of resistor were unknown.
0°
135°
45°
90°
1.6 S/m
Distribution of losses in the resistor
Electric field, TW

## Slide 7: PA model with waterload
No changes.
It has to be something else