Booster measurements
C.Y. Tan, K. Seiya & C. Bhat
14 Jun 2017

---
Tune scan with high intensity
Are the losses (left pic) from 3rd order resonance or from 1/2 integer resonances because they became thicker? Yellow region may be intersection of 1/2 integer lines.
Intensity: 4.6e12, pseudo-flat lattice 2. Skew quad current is zero for first 5 ms.

---
Lowering chrom (SXL=0) at injection
Vertical damper pickup used for measurements.
SXL=0 at injection

---
SXL=0, dampers ON
Sum increases because of shoulders in the |signal| at higher turn number.
Since beam loss is there with transverse dampers on, this means that instability is outside the bw of the dampers. Head-tail?
HEP
SXL=0

---
SXL=0, dampers on (cont’d)
SXL=0
Did a scan of the entire vertical data set.
Cannot see any head-tail.
Comparison between HEP and SXL=0 shows no difference in signal!
Every line is 6 turns which is approximately 1/4 to 1/3 of a synchrotron period. (assuming 25 kHz synchrotron tune)
Only solution is that the problem is in the horizontal.
Will take data again to verify.
HEP

---
Nothing is confirmed!
- 3rd order resonance from broken symmetry from CPL03 (not from doglegs) not conclusively proven experimentally.
- Transverse impedance causing head-tail
  - Certainly not in the vertical plane.
  - Will have to look at the horizontal plane.
- If the above two are confirmed this means that there are two causes for beam loss at injection.