Measurements with lower chromaticity
C.Y. Tan, C. Bhat & K. Triplett
28 Jun 2017

---
Effect of lowering chroms
- Dampers must be on
  - Previous attempts by setting SXL=0 and -3 made chromaticies POSITIVE!
    - This caused the beam to go unstable. In fact, if not for the dampers, the beam would completely fall out.
  - There is no head-tail instability.
- Does lowering chromaticity improve beam lifetime?
  - It does in MI and Tevatron. But what about Booster?

---
No head-tail with positive chroms
Clearly beam falls out but it is not from head-tail because I cannot tell the difference between nominal and positive chroms.
Using MADX, Cx = -31 and Cy = +26
SXL = -3 A
HEP

---
As found and new tunes and chromaticity
Notice that Ch (HEP) is -20 units ~3ms and Cv ~-30 units around 7 ms.
There is some weirdness going on at 8 ms for new settings. Hard to believe singple point chroms that behave like this.

---
SXL and SXS settings and results

---
Redid chromaticity assuming non-linear chromaticity
Chandra found that chroms were quite different for ROF=+1 mm vs -1 mm. So we did a 3 point fit to find Ch and Cv.
There is still an odd ball at 8 ms.

---
No change in injection efficiency
Used 12.4 turns like in $15.
No visible increase in efficiency ~90%.
No visible increase in losses.
Moving tunes UP away from 1/2 integer did not show improvement.
There is a limit of how much tune change is available even with dampers ON at this intensity:
Max horz tune change +0.08
Max vert tune change +0.04
Lowering chromaticity does not improve beam lifetime!

---
Kiyomi’s 3rd order resonance experiment
If the source of the 3rd order resonance is coming from the displaced CPL03, then:
Turning off CPL03 only could still give us a 3rd order resonance.
Turning off CPL03 and CPL15, shouldn’t 3rd order be diminished?
If 3rd order remains, does this mean source of 3rd order is not at CPL03 or there is no 3rd order?

---
Again, back to same old song ...
- Is this still a 3rd order resonance problem?
  - Do we really have a dynamics problem?
- Is this an aperture problem?
  - Is beam already too big?
- Or dipole ripple problem: what’s the switching frequency of the corrector dipole power supplies?
  - See JPARC paper where they have a 100 kHz dipole ripple on their injection bump magnets that causes halo: https://journals.aps.org/prab/pdf/10.1103/PhysRevAccelBeams.20.060402

---
JPAC twin peak losses from injection bump magnet noise

---
Measurements by R. Tesarek from fast BLMs at the locations indicated above.