Beam loading
C.Y. Tan & R. Madrak
28 Sep 2017

---
Is beam loading a problem?
- Assumptions:
  - 6e12 beam (which is a lot! PIP2 intensity)
  - δ-function bunches separated by 2*2nd harmonic periods.
    - IωRF = 2IDC for 106 MHz bunches (0.8 for gaussian beam ~ 1)
    - At 76 MHz, form factor is 0.06 for gaussian beam.
  - For simplicity, assume stationary buckets at injection and extraction
    - 100 kV peak gap voltage at injection
    - 30 kV peak gap voltage at extraction for bunch rotation.

---
RLC model
For a δ-function bunch, it is easy to show that the induced voltage for a single pass of the beam is
Notice Vb is dependent on R/Q and not R alone. So, naively, this would help with beam loading.
Example:
which is much smaller than 100 kV
I though we could be saved because of R/Q, but NO!!!

---
Infinite number of bunches
Impedance of the cavity in terms of magnitude and detuning angle ψ.
Assume drive is on resonance so δ = 0. The steady state induced voltage > 100 kV available at 106 MHz!
This is a lot of volts!

---
Detuning
There is a lot of volts from the beam.
There is a way to mitigate this problem by “detuning”, i.e. not running at the peak of the cavity impedance where the reactive part of the impedance is zero.
If we think of the beam as an impedance in parallel with the cavity impedance, we can calculate the required detuning to make the impedance look real for the generator or PA. But this only works at one fixed current.

---
At injection
Essentially, the beam is long enough that at injection, there is very little induced voltage on the 76 MHz resonance.
Measured by Chandra for 5.4e12 protons
So, there’s nothing to worry about at injection. However ...

---
Detuning angle at 106 MHz
This is a huge number!
This is for 30 kV extraction voltage and 6e12 protons above transition and assuming approximately stationary bucket
The sign is correct. We want the drive to be above the resonance for Robinson stability.
The huge detuning angle is not a problem if the beam is always there or the RF is always on. However, the plan is to turn on RF only at the end. This is probably a problem.

---
Required power for maintaining Vc=30 kV for 6e12 protons
Minimum required power is at -82.4 deg as expected

---
Stability
Robinson’s stability criterion
There is no margin for error!
Any small perturbations will get us to an instability.
But is this true? We have a double RF system. The stability criterion needs to be analyzed for this system.
My gut feeling is that this stability criterion is met with a double RF system. I need to prove this!

---
Mitigation
- Can we run with some small voltage on the cavity at the correct detuning angle and then ramp up when necessary?
- Beam loading compensation?
- Use the ideas from SCRF?
  - Don’t run at optimum ψ
  - Fractional ψ detuning, c.f. Griffin.
- Mitigation will need to be figured out.