## Slide 1
Matt Slabaugh
Fermilab Workshop on Megawatt Rings & IOTA/FAST Collaboration Meeting
7 May 2018
The Booster Replacement Cavity Program

## Slide 2: Outline
Recap
  Reduced losses at RF cavities
    Aperture limitations
    What diameter
    Reliability
  More beam for PIP-II (PIP-III ?)
Decision
  3.25” Beam Pipe
  RF design
  Related issues
Manufacture
  Status

## Slide 3: Why?
While the existing cavities have been refurbished, they are nearly 50 years old.
Future operations will leave no extra operating margin.
Uncertain operational impact of needing to run all cavities at maximum performance 24/7.
  Plan to run Booster till 2035.

## Slide 4: Cavity Voltage
Present
  830 kV – 950 kV, present operating range depending upon beam requirements and cavity repair status.
  < 850 kV, losses increase for 4.2E12/pulse.
    requires a minimum of 17 cavities at the nominal voltage 50 kV or 25 kV/gap.
Future requirement
  1.2 MV ( 1.1 MV total + 0.1 MV overhead )
Plan to run similar to MI, all cavities on, voltage fixed/regulated as needed.
 | Voltage per Cavity |  | 
# of cavities | Pre PIP 870 kV | Present 1005 kV | Replacement 1200 kV
19 | 45.8 kV |  | 
20 |  | 50.3 kV | 60 kV
21 |  | 47.8 kV | 57 kV
22 |  | 45.7 kV | 55 kV

## Slide 5: Other cavity performance factors
Beam Loading and Power Requirements
  Each cavity must meet the specified voltage while accelerating up to 1A of beam at a synchronous phase of ~40 degrees (synchrotron definition, 90 degrees at crest) with 2-3 of the 84 buckets empty.
  The loaded cavity shall be designed to operate with up to 150 kW RF power from a CPI (EIMAC) Y-567B tetrode power tube. Although rated to operate at higher power up to 200 kW, for lifetime considerations operating at a lower power is preferable.
Cavity Impedance and Spurious Modes
  The cavity shall be designed for R/Q = 50 ohms and the impedance of all higher order and spurious modes shall be ≤ 1000 ohms.
Multipacting
  The cavity must be able to turn on and run at any voltage between 25% and 100% of the specified operating voltage over the full frequency range without operationally significant multipacting at the nominal operating vacuum pressure.

## Slide 6: Aperture
57.17mm
57.17mm
Vertical aperture limited by magnets
Horizontal aperture limited by cavities
Inside view of Booster gradient magnet
2.25 Inch Cavity Aperture

## Slide 7: Aperture - Magnets and RF
Chart: 
Aperture Scan data
at Long 14
2.25" diam. aperture
RF and D Magnet

## Slide 8: Aperture - Conclusion
Ellipse | a (inch) | b (inch) | area (in2)
average | 0.9113 | 0.6519 | 1.87
max | 1.24 | 0.75 | 2.92
Ratio (max/ave) | 1.36 | 1.15 | 1.57
New aperture radius | 1.53 | 1.29 | 6.22
Equivalent Circle Radius = 1.4 in
3” beam pipe will provide 0.1” to 0.2” margin

## Slide 9
Aperture Options
  Existing aperture 2.25”
  Minimum aperture from study 3”
  Aperture chosen 3.25”
Aperture - Decision

## Slide 10
Aperture - Magnets and RF
Chart: 
2.25” diameter
3.25” diameter

## Slide 11: Aperture – Lattice
Chart: Booster Apertures
| 0 | 0.6 | 0.6 | 0.75350648750000004 | 0.75350648750000004 | 3.6425278875 | 3.6425278875 | 3.7960343750000001 | 3.7960343750000001 | 3.9558146624999999 | 3.9558146624999999 | 6.8449884624999999 | 6.8449884624999999 | 7.0047687500000002 | 7.0047687500000002 | 7.51476875 | 7.51476875 | 12.243715349999999 | 12.243715349999999 | 12.753715349999998 | 12.753715349999998 | 12.913495637499999 | 12.913495637499999 | 15.802669437499999 | 15.802669437499999 | 15.962449724999999 | 15.962449724999999 | 16.115956212499999 | 16.115956212499999 | 19.004977612499999 | 19.004977612499999 | 19.158484099999999 | 19.158484099999999 | 19.7584841
Vertical Aperture | 2 | 2 | 1.5 | 1.5 | 0.82 | 0.82 | 1.5 | 1.5 | 1.6 | 1.6 | 1.125 | 1.125 | 1.6 | 1.6 | 2 | 2 | 1.125 | 1.125 | 2 | 2 | 1.6 | 1.6 | 1.125 | 1.125 | 1.6 | 1.6 | 1.5 | 1.5 | 0.82 | 0.82 | 1.5 | 1.5 | 2 | 2
y beam size | 0.40496 | 0.40627 | 0.414 | 0.4303 | 0.45422 | 0.48465 | 0.532 | 0.5773 | 0.63616 | 0.69001 | 0.72733 | 0.76144 | 0.78673 | 0.79675 | 0.79609 | 0.79343 | 0.79109 | 0.79008 | 0.78941 | 0.78941 | 0.78941 | 0.78941 | 0.79008 | 0.79008 | 0.79176 | 0.79542 | 0.79675 | 0.79008 | 0.77658 | 0.75236 | 0.71115 | 0.66859 | 0.60853 | 0.55867 | 0.50913 | 0.47136 | 0.44122 | 0.41782 | 0.40886 | 0.40496 | 0.40365
Horizontal Aperture | 2 | 2 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2 | 2 | 1.125 | 1.125 | 2 | 2 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2 | 2
x beam size | 1.0222 | 1.0222 | 1.0183 | 0.99727 | 0.97038 | 0.92574 | 0.86672 | 0.80665 | 0.72733 | 0.66661 | 0.60853 | 0.56573 | 0.52449 | 0.50128 | 0.48246 | 0.46855 | 0.45712 | 0.44836 | 0.44122 | 0.4364 | 0.43519 | 0.43882 | 0.4454 | 0.45071 | 0.46287 | 0.47694 | 0.48899 | 0.50913 | 0.54429 | 0.58187 | 0.63407 | 0.69001 | 0.76283 | 0.83437 | 0.89671 | 0.94972 | 0.9866 | 1.0104 | 1.0209 | 1.0222 | 1.0222
new aperture - H & V | 2 | 1.625 | 1.625 | 2

## Slide 12: RF Design
With new aperture decided
  Maintain physical design
  Adapt RF to give
    Needed voltage
    Frequency sweep

## Slide 13: Adjustable parameters
Stem length
3.25”
Bore
Steeper Taper
Diameter
at center
# of ferrite and choice

## Slide 14: Changes to Optimize Design
Minor changes to the taper, central part of tuner, and ferrite selection

## Slide 15: Replacement vs Current Booster Cavities
 | Current Booster |  | Replacement Cavity | 
mu | 6.6 | 2.1 | 7.35 | 2.1
Freq [MHz] | 37.7 | 52.9 | 37.7 | 53.2
Adjusted Q | 208 | 1128 | 407 | 1544
E[mJ]-60kV | 243.80 | 98.32 | 283.53 | 104.93
R/Q | 31.17 | 55.08 | 26.80 | 51.32
Eave [mJ] | 171.06 |  | 194.23 | 
Ecycle [mJ] | 118.03 |  | 134.02 | 

## Slide 16
Modeling of Booster Cavity Temperatures – Max T up ~ 20%
With Convective Cooling Boundaries
Booster Cavity
Replacement Cavity
Simulations: Mohamed Hassan (TD)
Slabaugh | Booster Replacement Cavities

## Slide 17: Validation of higher order mode calculations (measured on Booster cavity and compared to simulated)
Q-undamped (84 MHz) ~2700
Q-damped (84 MHz)~115
Simulated Q0 (84 MHz)=75000
Simulated Q-damped (84 MHz) =116
84 MHz Large HOM
S21 Gap Probe (US) to 165 Port (DS)
Green: 84 MHz Port is open
Red: 84 MHz Port is matched

## Slide 19: Booster RF Cavity Tuner Modification

## Slide 20: Booster RF Cavity replacement girder
Plumbing and mounting reconfiguration complete

## Slide 21: Booster RF Cavity vacuum parts
Completed vacuum end shell assemblies
Ceramic leak check

## Slide 22: Booster RF Cavity Components

## Slide 23: Summary
Voltage – 60 kV
Frequency range – 37.7 to 52.9 MHz (39.2 to 53.2 with different bias)
Stem length: added 1”
Type and number of ferrite: Total of 4 ferrite replaced with aluminum, and all remaining ferrite are low-mu variety
  12 “Stackpole”
  The cavity is being assembled and is scheduled to be completed in June. There will be 2 to 3 weeks of testing prior to installation. The possibility of installation before the summer shutdown is good and will provide run time before shutting off for the summer.

## Slide 24: Ceramic Stresses

## Slide 25: Booster RF Cavity vacuum parts

## Slide 26: Replacement Cavity solid model