## Slide 1
Chandra Bhat, Fermilab
J-PARC, Japan
20190307
Longitudinal Beam Dynamics Issues
at the Fermilab Booster
C. Y. Tan
W. Pellico
S. Chaurize
F. Garcia
K. Seiya
T. Sullivan
K. Triplett
J. Reid
D. Johnson
T. Johnson
B. Hendrick,
S. Bhat
A. Waller
C. Drennan
N. Eddy
V. Grzelak
Acknowledgements

## Slide 2: Fermilab, US Premier Particle Physics Laboratory
Aerial
view of Fermilab
Site
MiniBooNE
MicroBooNE
NuMI:
MINOS+
MINERvA
NOvA
Muon:
g-2
Mu2e
MIPP
Test Beam
SeaQuest
M-Center
LBNF
Recycler
&
Main Injector
Booster
Tevatron
Recycler:
8 GeV Permanent
Magnet Storage Ring
Main Injector:
8 -120 GeV Accelerator
Booster:
0.4-8 GeV Accelerator
LINAC
Accumulator/
(Muon-ring)

## Slide 3
LINAC 400 MeV p Beam
8 GeV Beam
24 Sectors
Basically
These are Independent
of one another
FOFDOOD (DOODFOF)
Booster Layout
WCM
Collimators
Absorber
H&V Trans. Dampers
Inj. ORBUMP
Extra. Dogleg
H&V IPMs
Notcher
C= 475 Meter
# of RF Cavities= 22
Vrf (Volt)/Cavity= 50 KV
R/Q = 20 , Rs= 15 K
C=475 m, Trev=2.2-1.59s
h=84
RF
19-20
RF
15-16
RF
13-14
RF
11-12
RF
9-10
RF
21-22
RF
17-18
RF
7-8
RF
5,6
RF
1-2
RF
3-4
PIP Specification
fRF=37.8 MHz-52.8 MHz
Vrf(total) = 1 MV
Do we have a total of 22 RF cavities with 50kV/cavity

## Slide 4: Proton Improvement Plans at Fermilab (Past, Present and Future)
PIP: Goal was
  Extract 2.25E17 protons/hr (@15 Hz) from the Fermilab Booster
    12 batches of 4.26E12ppBp to RR/MI with for every 1.33 sec
      L<0.1 eVs/bunch &
      T<16 -mm-mr
      LINAC/Booster efficiency >85%
    To achieve beam power on NuMI target 700kW using RR&MI
    Provide 4.26E12ppBc to Booster Neutrino Program
PIP-I+: Goal prepare the Booster for PIP-II & also
  Extract 2.66E17 protons/hr (@15 Hz) from the Fermilab Booster
    12 batches of ~5E12ppBp to RR/MI with for every 1.2 sec
      Out put beam properties same as above
      LINAC/Booster efficiency >85%
    To achieve beam power on NuMI target 900kW using RR&MI
    Provide ~5E12ppBc to Booster Neutrino Program
PIP-II: Goal send 1.2MW proton beam power on the LBNF target, using newly built SC-LINAC and existing RR and MI
  But, ~4.63E17 protons/hr (@20 Hz) from the Fermilab Booster
Achieved ~1 year ahead of
Scheduled date 2018
working
To be completed
by 2023

## Slide 5: Injection Scheme in the Booster
Booster
Magnet Ramp
15 Hz
400 MeV LINAC Beam
Booster
Booster
Synchrotron
Bmin (400 MeV)
Bmax
(8 GeV)
Begin Inj.
Prior to 2016
~60s-200 s debunching
 40s
injection
Capture & Acceleration
using 37-52 MHz RF
system in 360s
1/30Hz  0.0333 s
~200s
Beam Acceleration
using 37-52 MHz
RF system
Bmin (400 MeV)
~260s
for Capture
>40s
Inj.
Improved Scheme for Adiabatic Beam Capture
“Early Injection Scheme”
Energy Acceptance ~5MeV
Beam E(95%) 1.5MeV
pseudo front-porch
CBhat, HB2016
This scheme gave us
an ability to inject ~30% more Beam
an additional 200 s for adiabatic beam capture …
(since Dec. 2015)
Since January 2019,
Flat bottom

## Slide 6: Longitudinal Beam Dynamics Simulations Beam Injection to extraction
Simulation Parameters: with SC
1. LINAC Beam E = 1.2 to 1.6 MeV,
2. Beam Int.= 2-12E12ppBc, beam capture with RF paraphase
E Dist.
30
-30
0
E (MeV)
Line-Charge Dist.
E-t Phase space (8.2E12ppc)
2
-2
0
Azimuthal Angle(deg)
E@Inj
= 1.5 MeV
3. Snap Bunch Rotation
Simulations suggest
one can achieve <20% emittance growth during capture.
L@Exit ~0.06 eVs (95%)
No particle losses
E @Exit< 2.75 MeV
Vrf=0 @ Injection
Vrf during
Capture

## Slide 7
(xE12ppBc)
Inj. to Ext. Efficiency
But!
Measured Beam Transmission from Injection to Extraction in the Booster
2
4
6
8
10
12
14
16
18
20 Booster Turn
Intensity (xE12 ppBc)
Injection at 400MeV & Extraction at 8 GeV
Booster Magnet Ramp
(schematic)
Transition Crossing
(T=5.47)
Beam power loss of
1W/m
~2W/m
All the losses are in the first 4 msec of the cycle
Not due to Transverse dynamics.
Many indications suggest this might be due to longitudinal beam dynamics induced by HLRF and LLRF.
Trans.Dynamics  Long. Beam dynamics issues.
Operational Beam Intensity
1 MW (1.2sec/MI cycle)
0.92MW (1.33sec/MI cycle)
0.94MW (1.2sec/MI cycle) or
0.85MW (1.33sec/MI cycle)
0.70 MW (1.33sec/MI cycle)
One can achieve with
12 out of 15 Booster Batches
5.56E12ppBc
5.2E12ppBc

## Slide 8: Identification of the Issues and Mitigation
I
II
RF responses to paraphase are not identical among 22 RF stations.
These phase errors were as large as 20deg
In 2018 these are fixed to better than 5 deg
DC Studies

## Slide 9: Identification of the issues and Fixes (cont.)
Phase jump
Vrf
Global balance OFF/ON
WCM
Sum RF Waveform
Phase jump
Va#Vb introduces phase slip
III
DC & 0.4-8 GeV Studies

## Slide 10
What is going on during the Beam Capture?
Capture with Operational Paraphase Curve
Capture with Adiabatic Paraphase Curve
What was Expected?: In an ideal situation beam capture in DC mode the RF phase should not slip relative to bunch centroid.
Observations: We see two types of RF phase slip relative to the bunch centroid
fast and
slow
FB-20190123-4BT-1E12-E17-DC-20RFst-4
FB-20181114-DC-6
Vrf
Vrf
 How are these possible?
No “NECK”
Time(ns)
Time(ns)

## Slide 11: Possible Explanations
Va=Vb
VaVb; Vb/Va=0.90
If Va=Vb and |(start)| >90 deg then RF phase slips by 180 deg.
If VaVb |(start)|=90 deg then the RF phase slips slowly by 90 deg and occurs till the end of the capture.
If VaVb |(start)|>90 deg then both of these slips happens.
Flipping Phase
Slipping Phase
&
Plipping Phase
This undesirable feature has a consequence during early part of the beam capture

## Slide 12: Simulations for Va=Vb and Va#Vb
Va/Vb=1
Va/Vb=0.96
Beam acceleration
Currently working on
Better phase control
Digital system to control amplitudes
Try to go for much earlier injection to finish beam capture by Bmin
Snap bunch rotation
Add 2-harmonic RF system at injection and extraction.