## Slide 1
PSA: There is evidence of a mouse in my office in Linac Gallery

## Slide 2
Initial neutralization studies with mass flow controller

## Slide 3
The case for the need for increased LEBT pressure:
The LEBT turbos run at their minimum speed
When doing LEBT pressure scans, we stop when turbos reach their minimum speed
We tested running with only 1 LEBT turbo in the past, it needed to run at max speed.
Previous BNL experience

## Slide 4
BNL started using Xenon around 2012 and used it for several years, then ran with N2 and finally air bleeding in. They are no longer bleeding in any gas. They used around 25L of Xenon over a several year span. Gas line is around 40cm from the source. (Tim Lehn, BNL)
BNL neutralization line and experience
Note:
Cost of 25L of Xenon and a regulator is around $2250.00

## Slide 5
~32cm
Location of our neutralization line

## Slide 6
Nitrogen flow control
Initially used manual leak valve, hard to control flow
Recently installed mass flow controller

## Slide 7
N2 injected into special made flange
Overall N2 injection

## Slide 8
Initial mass flow controller tests on Source B LEBT
Using the mass flow controller allows discrete and predictable changes in LEBT pressure

## Slide 9
First study with source A (5/29/2019)
Stopped at 5.6 x 10-6 Torr because beam current into tank 1 was decreasing.
Did not tune the LEBT solenoids for these scans
I believe that H and V numbers are swapped
No N2 flow

## Slide 10
Beam current a the tank 1 entrance decreased with increasing LEBT pressure.
Does not appear to be caused by H- stripping
First study with source A (5/29/2019)

## Slide 11
Next Study:
Increase turbo speed prior to injecting nitrogen
Tune the solenoids for each pressure
Check for repeatability
Try changing the S&H timing to sample different part of the beam
Next steps for test stand emittance studies:
Working with mechanical engineering to build new LEBT with increased pumping (currently 200 L/S compared to 400 L/s 940 L/S on operational LEBT’s)
Explore LEBT neutralization (detailed studies)
Effects of different source tuning on emittance
Cancel out magnetic field just DS of extractor